## Slide 1: Bidirectional Project CLLC Control Algorithm
FW: Joey De Guzman
EE: John Karlo Lee
Updated: 17-Sept, 2021

## Slide 2: Overview
Charger flowchart
Full-bridge/half-bridge configuration
Regulation scheme
Regulation state machine
Softstart
Regulation mode select
Synchronous rectifier control
Enable LLC2 for current balancing during forward mode
Voltage droop during reverse mode

## Slide 3: Charger flowchart
Vbat>400V
Start
configure
pri=FB, sec=FB
configure
pri=HB, sec=FB
G2V
G2V
configure
pri=MD,
sec=SR
configure
pri=SR,
sec=MD
configure
pri=MD,
sec=SR
configure
pri=SR,
sec=MD
PFM, PSPWM, burst
PFM, PSPWM, burst
PFM, burst
PFM, burst
N
Y
Y
N
Y
N
Legend
G2V – grid-to-vehicle
V2G – vehicle-to-grid
FB – full-bridge
HB – half-bridge
MD – main drive
SR – synchronous rectifier
PFM – pulse frequency modulation
PSPWM – phase shift PWM

## Slide 4: Full-bridge/half-bridge configuration
Full-bridge configuration
G2V: Vbat 400V-800V
V2G: Vbat 400V-800V
Half-bridge configuration
G2V: Vbat 150V-400V (half-bridge)
V2G: Vbat 150V-400V (voltage doubler)
4
4
4
FET is active
FET is open
FET is closed
G2V
V2G
G2V
V2G

## Slide 5: Regulation scheme
Control for full-bridge CLLC configuration
Control for half-bridge CLLC configuration
Control | fs(kHz) | PS(°) | Burst duty(%)
Burst | 300 | 36 | 0≤x≤100
PSWM | 300 | 0≤x≤36 | 100
PFM | fsmin≤x≤300 | 0 | 100
Lighter load
Control | fs(kHz) | Burst duty(%)
Burst | 300 | 0≤x≤100
PFM | fsmin≤x≤300 | 100
Lighter load

## Slide 6: Regulation state machine
Control for full-bridge CLLC configuration
Control for half-bridge CLLC configuration

## Slide 7: Softstart
Notes: http://www.plantuml.com/plantuml/uml/SoWkIImgAStDuIfEJin9LJ0sDL0epqmfoU2ArefLqDMrKm0A9xiM5UKNAN1n0HMNf2A9L7Cf87WWnPbvoKMfkQbv9K6fQLOAgI1Xk-AIr09qTIcf6EfiTB4fJCqlBkQgXTgCOZp8SXG1LDSYDAMaece22X3K1BPNeHh8TqZDIm463m00

## Slide 8: Regulation mode select
Notes: http://www.plantuml.com/plantuml/uml/SoWkIImgAStDuIfEJin9LJ0sDL0epqmfoU2ArefLqDMrKmZEJoi1A-BY0b8bgGW1XMek1GGFhDZPsKeXDR-u65CYp4eXkIm-Fvkh5ceEK2t80225Kq4OH44OtEZaPA02XSIy50L5c5g7rBmKeFC1

## Slide 9: Synchronous rectifier control
CLB
Stage 1: Digital filter for SR ON
Stage 2: Utilize 2 comparators for custom hysteresis
Stage 3: Limit one SR pulse per one cycle of main drive PWM
md RE
cmpl
cmph
pwmout
cmph – comparator that determines SR turn ON level
cmpl – comparator that determines SR turn OFF level
md RE – gives the rising edge timing of the main drive PWM
pwmout – SR pulse

## Slide 10: Synchronous rectifier control
Stage 1: Digital filter for SR turn ON
Notes: http://www.plantuml.com/plantuml/uml/SoWkIImgAStDuIfEJin9LJ0sDL0epqmfoU2ArefLqDMrK_3qympXuW8gAqa5inMgkHJ032k5vDo235i3A1UaDipHnzCbtjyltjatm0CedrSI3r8Jdv-MPXkXe8Oaa6Tho5KBDHPL6z1uL06eFOOAw18mrw5PP8XcKGJG8eVKl1IW9m40

## Slide 11: Synchronous rectifier control
Stage 2: Utilize 2 comparators for customized hysteresis
Notes: http://www.plantuml.com/plantuml/uml/SoWkIImgAStDuIfEJin9LJ0sDL0epqmfoU2ArefLqDMrKmXpzF5qYVTtSujtzWq8yG_XuW9gAKd545UevbB04BHIICujACaliJN08ebakX-o-WnRGmKr42F7DeAh5ceVkaeas_pGB0DgnvJ4y0h2jWYORGP0snnIyrA0mG40

## Slide 12: Synchronous rectifier control
Stage 3: Accept one SR pulse per one cycle of main drive PWM
Notes: http://www.plantuml.com/plantuml/uml/SoWkIImgAStDuIfEJin9LJ0sDL0epqmfoU2ArefLqDMrK_3qympXuW8gAqa5inMgkHJ032k5WlBS_D8IMmEe05YvgrzyS92LGd9kGKb-YQsXWff2IL9oIL5yLMfHlcq4LotKA8Wwa5aG5jGma0wO4DWu5yzWPFCCS9a7KWWr4Cf4E4y1BWRt4Dp025G33O46EgJcfG031000

## Slide 13: Enable LLC2 for current balancing during forward mode
Notes: http://www.plantuml.com/plantuml/uml/TL1DYuCm5BpdLxpZVk3YkdWH567r88YNtLif4lMr1c8AIQI5qlzU4X9Y3vxUCCDy9ANILEfruKIDb2Fyf35SsQHdSlWuGXGLq7JDFo5AKuqMtmdOQxIwwzlsDyb0ugbdbrKNjurQDNzEHgwGF5oATvaW1srFrTQUiHv11ux0-PW4EZJrHe0Sug_qpNCHbGFJAD_t3D-GlmPyEaSOvqURTHvlveKtJKo5WK7OBmmT9ilac-k_E8DnfkACmCJMKQAOreK_0G00

## Slide 14: Voltage droop during reverse mode
Notes: http://www.plantuml.com/plantuml/uml/SoWkIImgAStDuIfEJin9LJ0sDL0epqmfoU2ArefLqDMrK_3qympXuW8gAqa5iwkv5C0qMCx5nnNAjL8eIasBpyb9DemlIohDoLQm1Gb0sUXgZ33LSDL2BG4R2hG4J8Ci2NC9ylSFi598BelFHoY32WCLGbamzrWfA89LAYJcfIWa9mDPS2LOt9YUc9a75Kafoiylq0ApCmkACXMq5VBJqefJIv2bCOqomZ3A2Cae8tIZ4D90dpYavgK0Wnu0