## Slide 1: Architecture
Module 1
C2000™ Microcontroller Workshop
Copyright © 2019 Texas Instruments. All rights reserved.

## Slide 2: Module Objectives
Review the F28004x block diagram and device features
Describe the F28004x bus structure and memory map
Identify the various memory blocks on the F28004x
Identify the peripherals available on the F28004x

## Slide 3: TMS320F28004x Block Diagram

## Slide 4: C28x CPU Internal Bus Structure
Program-read Data Bus (32)
Data-write Address Bus (32)
Program Address Bus (22)
Execution
R-M-W
Atomic
ALU
Real-Time
JTAG
Emulation
Program
Decoder
PC
XAR0
to
XAR7
SP
DP
@X
ARAU
MPY32x32
XT
P
ACC
ALU
Registers
Debug
Register Bus / Result Bus
Data/Program-write Data Bus (32)
Data-read Address Bus (32)
Data-read Data Bus (32)
TMU
TR0-TR7
Program
Memory
Data
Memory
Peripherals
VCU
VR0-VR8
CLA
MR0-MR3
FPU
R0H-R7H

## Slide 5: C28x CPU + FPU + VCU + TMU and CLA
MCU/DSP balancing code density & execution time
  16-bit instructions for improved code density
  32-bit instructions for improved execution time
32-bit fixed-point CPU + FPU
32x32 fixed-point MAC, doubles as dual 16x16 MAC
IEEE Single-precision floating point hardware and MAC
Floating-point simplifies software development and boosts performance
Viterbi, Complex Math, CRC Unit (VCU) adds support for Viterbi decode, complex math and CRC operations
Parallel processing Control Law Accelerator (CLA) adds IEEE Single-precision 32-bit floating point math operations
CLA algorithm execution is independent of the main CPU
Trigonometric operations supported by TMU
Fast interrupt service time
Single cycle read-modify-write instructions
Data Bus
3
32-bit
Timers
CPU
Register Bus
Program Bus
32x32 bit
Multiplier
FPU
R-M-W
Atomic
ALU
CLA
CLA Bus
TMU
VCU
PIE
Watchdog

## Slide 6: C28x Atomic Read/Modify/Write
Registers
ALU / MPY
LOAD
STORE
WRITE
READ
CPU
Mem
Atomic Instructions Benefits
  Simpler programming
  Smaller, faster code
  Uninterruptible (Atomic)
  More efficient compiler
AND *XAR2,#1234h
2 words / 1 cycles
Atomic Read/Modify/Write
MOV AL,*XAR2
AND AL,#1234h
MOV *XAR2,AL
DINT
EINT
6 words / 6 cycles
Standard Load/Store
Note: Example shows non-atomic assembly instructions vs. atomic assembly instruction; Compiler intrinsics can be used for generating the atomic assembly instructions if the user needs guaranteed atomicity at the C level

## Slide 7: C28x CPU Pipeline
F1 F2 D1 D2 R1 R2 E
Protected Pipeline
  Order of results are as written in source code
  Programmer need not worry about the pipeline
8-stage pipeline
F1 F2 D1 D2 R1 R2 E
F1 F2 D1 D2 R1 R2 E
F1 F2 D1 D2 R1 R2 E
F1 F2 D1 D2 R1 R2 E
F1 F2 D1 D2 R1 R2 E
F1 F2 D1 D2 R1 R2 E
F1 F2 D1 D2 R1 R2 E
A
B
C
D
E
F
G
W
W
W
W
W
W
W
W
E & G Access
same address
R1 R2 E W
D2 R1 R2 E W
F1: Instruction Address
F2: Instruction Content
D1: Decode Instruction
D2: Resolve Operand Addr
R1: Operand Address
R2: Get Operand
E: CPU doing “real” work
W: store content to memory
H

## Slide 8: C28x CPU + FPU + VCU + TMU Pipeline
Floating Point Unit, VCU and TMU has an unprotected pipeline
  i.e. FPU/VCU/TMU can issue an instruction before previous instruction has written results
Compiler prevents pipeline conflicts
Assembler detects pipeline conflicts
Performance improvement by placing non-conflicting instructions in floating-point pipeline delay slots
F1 F2 D1 D2 R1 R2 E
W
F28x Pipeline
Fetch
Decode
Read
Exe
Write
Floating-point math operations, conversions between integer and floating-point formats, and complex MPY/MAC require 1 delay slot – everything else does not require a delay slot (load, store, max, min, absolute, negative, etc.)
Load
Store
0 delay slot instruction
1 delay slot instruction
D R E1 E2/W
VCU / TMU Instruction
D R E1 E2/W
FPU Instruction

## Slide 9: Simplified F28004x Memory Map
M0 RAM (1Kx16)
M1 RAM (1Kx16)
PIE Vectors
(512x16)
CLA to CPU MSG RAM (128x16)
CPU to CLA MSG RAM (128x16)
LS0 – LS7 RAM (2Kx16 each)
0x000000
0x000400
0x000D00
0x001480
0x008000
0x001500
GS0 – GS3 RAM (8Kx16 each)
CAN A MSG RAM (2Kx16)
CAN B MSG RAM (2Kx16)
FLASH
(128Kx16)
TI / User OTP (4Kx16)
Boot ROM (32Kx16)
BROM Vectors (64x16)
0x00C000
0x049000
0x04B000
0x078000
0x080000
0x3F8000
0x3FFFC0
LS0 – LS7 RAM
accessible by
CPU & CLA
GS0 – GS3 RAM
accessible by
DMA

## Slide 10: Dual Code Security Module
Prevents reverse engineering and protects valuable intellectual property
Various on-chip memory resources can be assigned to either zone 1 or zone 2
Each zone has its own password
128-bit user defined password is stored in OTP
128-bits = 2128 = 3.4 x 1038 possible passwords
To try 1 password every 8 cycles at 100 MHz, it would take at least 8.6 x 1023 years to try all possible combinations!
Z1_CSMPSWD0
Z1_CSMPSWD1
Z1_CSMPSWD2
Z1_CSMPSWD3
Z2_CSMPSWD0
Z2_CSMPSWD1
Z2_CSMPSWD2
Z2_CSMPSWD3

## Slide 11: C28x Fast Interrupt Response Manager
192 dedicated PIE vectors
No software decision making required
Direct access to RAM vectors
Auto flags update
Concurrent auto context save
28x CPU Interrupt logic
C28x
CPU
INTM
192
Peripheral Interrupts 12x16 = 192
12 interrupts
INT1 to INT12
PIE
Register
Map
PIE module For 192 interrupts
T ST0
AH AL
PH PL
AR1 (L) AR0 (L)
DP ST1
DBSTAT IER
PC(msw) PC(lsw)
Auto Context Save
IFR
IER

## Slide 12: Viterbi / Complex Math Unit (VCU)
Extends C28x instruction set to support:
Viterbi operations
  Decode for communications
Complex math
  16-bit fixed-point complex FFT
    used in spread spectrum communications, and many signal processing algorithms
  Complex filters
    used to improve data reliability, transmission distance, and power efficiency
  Power Line Communications (PLC) and radar applications
Cyclic Redundancy Check (CRC)
  Communications and memory robustness checks
  Other: OFDM interleaving & de-interleaving, Galois Field arithmetic, AES acceleration
VCU execution registers
VSTATUS
VR0
VR1
VR2
VR3
VR4
VR5
VR6
VR7
VR8
VT0
VT1
VCRC
VSM0 to VSM63
Data path logic for VCU-II Instruction
General instructions
CRC instructions
Arithmetic instructions
Galois Field instructions
Complex FFT instructions
VCU Control Logic

## Slide 13: Trigonometric Math Unit (TMU)
Supported by natural C and C-intrinsics
Significant performance impact on algorithms such as:
• Park / Inverse Park • dq0 Transform & Inverse dq0
• Space Vector GEN • FFT Magnitude & Phase Calculations
Adds instructions to FPU for calculating common Trigonometric operations
x
y
r
y = r * sin(rad)
x = r * cos(rad)
r = sqrt(x2 + y2)
rad = atan(y/x)
Operation | Instruction | Exe Cycles | Result Latency | FPU Cycles w/o TMU
Z = Y/X | DIVF32 Rz,Ry,Rx | 1 | 5 | ~24
Y = sqrt(X) | SQRTF32 Ry,Rx | 1 | 5 | ~26
Y = sin(X/2pi) | SINPUF32 Ry,Rx | 1 | 4 | ~33
Y = cos(X/2pi) | COSPUF32 Ry,Rx | 1 | 4 | ~33
Y = atan(X)/2pi | ATANPUF32 Ry,Rx | 1 | 4 | ~53
Instruction To Support ATAN2 Calculation | QUADF32 Rw,Rz,Ry,Rx ATANPUF32 Ra,Rz ADDF32 Rb,Ra,Rw | 3 | 11 | ~90
Y = X * 2pi | MPY2PIF32 Ry,Rx | 1 | 2 | ~4
Y = X * 1/2pi | DIV2PIF32 Ry,Rx | 1 | 2 | ~4

## Slide 14: Configurable Logic Block (CLB)
Collection of configurable logic tiles
Can be interconnected using software to implement custom digital logic functions
Enhances existing peripherals through a set of crossbar interconnections
Crossbars allow the CLB to be connected to external GPIO pins
Each tile contains the core reconfiguration logic
CPU interface can be used to exchange data with the rest of the device

## Slide 15: On-Chip Safety Features
Memory Protection
  ECC and parity enabled RAMs, shared RAMs protection
  ECC enabled flash memory
Clock Checks
  Missing clock detection logic
  PLLSLIP detection
  NMIWDs
  Windowed watchdog
Write Register Protection
  LOCK protection on system configuration registers
  EALLOW protection
  PIE vector address validity check
Annunciation
  Single error pin for external signalling of error

## Slide 16: Summary
High performance 32-bit CPU
32x32 bit or dual 16x16 bit MAC
IEEE single-precision floating point unit (FPU)
Hardware Control Law Accelerator (CLA)
Viterbi, complex math, CRC unit (VCU)
Trigonometric math unit (TMU)
Atomic read-modify-write instructions
Fast interrupt response manager
128Kw on-chip flash memory
Dual code security module (DCSM)
Control peripherals
Analog peripherals
Direct memory access (DMA)
Shared GPIO pins
Communications peripherals

## Slide 17
C2000 Technical Training
www.ti.com/c2000