## Slide 1: Programming Development Environment
Module 2
C2000™ Microcontroller Workshop
Copyright © 2019 Texas Instruments. All rights reserved.

## Slide 2: Module Objectives
Use Code Composer Studio to:
  Create a Project
  Set Build Options
Create a user linker command file which:
  Describes a system’s available memory
  Indicates where sections will be placed in memory

## Slide 3: Module Objectives
Use Code Composer Studio to:
  Create a Project
  Set Build Options
Create a user linker command file which:
  Describes a system’s available memory
  Indicates where sections will be placed in memory

## Slide 4: Code Composer Studio
Code Composer Studio includes:
  Integrated Edit/Debug GUI
  Code Generation Tools
  TI-RTOS
Asm
Link
Editor
Debug
Compile
Graphs,
Profiling
Code
Simulator
Development
Tool
External
Emulator
MCU
Board
Libraries
lnk.cmd
Build

## Slide 5: Code Composer Studio: IDE
Integrates: edit, code generation, and debug
Single-click access using buttons
Powerful graphing/profiling tools
Automated tasks using Scripts
Built-in access to RTOS functions
Based on the Eclipse open source software framework

## Slide 6: Edit and Debug Perspective (CCSv9)
Each perspective provides a set of functionality aimed at accomplishing a specific task
Edit Perspective
  Displays views used during code development
    C/C++ project, editor, etc.
Debug Perspective
  Displays views used for debugging
    Menus and toolbars associated with debugging, watch and memory windows, graphs, etc.

## Slide 7: Creating a Target Configuration
File  New  Target Configuration File
Select connection type
Select device
Save configuration

## Slide 8: CCSv9 Project
List of files:
  Source (C, assembly)
  Libraries
  Linker command files
  TI-RTOS configuration file
Project settings:
  Build options (compiler, assembler, linker, and TI-RTOS)
  Build configurations
Project files contain:

## Slide 9: Creating a New CCSv9 Project
File  New  CCS Project
1. Project Name, Location, and Device
2. Tool-chain
3. Project templates and examples

## Slide 10: CCSv9 Build Options – Compiler / Linker
Compiler
  22 categories for code generation tools
  Controls many aspects of the build process, such as:
    Optimization level
    Target device
    Compiler / assembly / link options
Linker
  9 categories for linking
    Specify various link options
  ${PROJECT_ROOT} specifies the current project directory

## Slide 11: Module Objectives
Use Code Composer Studio to:
  Create a Project
  Set Build Options
Create a user linker command file which:
  Describes a system’s available memory
  Indicates where sections will be placed in memory

## Slide 12: Sections
All code consists of different parts called sections
All default section names begin with “.”
The compiler has default section names for initialized and uninitialized sections
int x = 2;
int y = 7;
void main(void)
{
long z;
z = x + y;
}
Global vars (.ebss)
Init values (.cinit)
Local vars (.stack)
Code (.text)

## Slide 13: Compiler Section Names
Name Description Link Location
.text code FLASH
.cinit initialization values for FLASH
global and static variables
.econst constants (e.g. const int k = 3;) FLASH
.switch tables for switch statements FLASH
.pinit tables for global constructors (C++) FLASH
Initialized Sections
Name Description Link Location
.ebss global and static variables RAM
.stack stack space low 64Kw RAM
.esysmem memory for far malloc functions RAM
Uninitialized Sections
Note: During development initialized sections could be linked to RAM since the emulator can be used to load the RAM

## Slide 14: Placing Sections in Memory
.ebss
.cinit
.text
Memory
RAMM0
(0x400)
0x00 0000
0x08 0000
0x00 0400
RAMM1
(0x400)
FLASH
(0x40000)
Sections
.stack

## Slide 15: Linking
Linker
Link.cmd
.map
.obj
.out
Memory description
How to place s/w into h/w

## Slide 16: Linker Command File
SECTIONS
{
.text:> FLASH PAGE = 0
.ebss:> RAMM0 PAGE = 1
.cinit:> FLASH PAGE = 0
.stack:> RAMM1 PAGE = 1
}
MEMORY
{
PAGE 0: /* Program Memory */
FLASH: origin = 0x080000, length = 0x40000
PAGE 1: /* Data Memory */
RAMM0: origin = 0x000000, length = 0x400
RAMM1: origin = 0x000400, length = 0x400
}

## Slide 17: Linker Command File Summary
Memory Map Description
  Name
  Location
  Size
Sections Description
  Directs software sections into named memory regions
  Allows per-file discrimination
  Allows separate load/run locations

## Slide 18: Lab 2: Linker Command File
System Description:
TMS320F28004x
All internal RAM
blocks allocated
Placement of Sections:
.text into RAM Block RAMGS01 on PAGE 0 (program memory)
.cinit into RAM Block RAMGS01 on PAGE 0 (program memory)
.ebss into RAM Block RAMM0 on PAGE 1 (data memory)
.stack into RAM Block RAMM1 on PAGE 1 (data memory)
F28004x
Memory
on-chip memory

## Slide 19
C2000 Technical Training
www.ti.com/c2000