## Slide 1: Peripheral Register Programming
Module 3
C2000™ Microcontroller Workshop
Copyright © 2019 Texas Instruments. All rights reserved.

## Slide 2: Module Objectives
Review register programming model
Understand the usage of the F28004x Driverlib and associated files
Program an application using Driverlib
Discuss Driverlib optimization

## Slide 3: Register Programming Model
Driverlib
  C functions automatically set register bit fields
  Common tasks and peripheral modes supported
  Reduces learning curve and simplifies programming
Bit Field Header Files
  C structures – Peripheral Register Header Files
  Register access whole or by bits and bit fields are manipulated without masking
  Ease-of-use with CCS IDE
Direct
  User code (C or assembly) defines and access register addresses
Hardware
Software
Registers and Addresses
Driverlib
Hardware Abstraction
Bit Fields
Direct

## Slide 4: Programming Model Comparison
The device support package includes documentation and examples showing how to use the Bit Field Header Files or Driverlib
Device support packages located at: C:\ti\c2000\C2000Ware\device_support\
C:\ti\c2000\C2000Ware\driverlib\
C2000Ware can be downloaded at www.ti.com/tool/c2000ware
EPwm1Regs.CMPA.bit.CMPA = EPwm1Regs.TBPRD * duty;
EPWM_setCounterCompareValue(EPWM1_BASE, EPWM_COUNTER_COMPARE_A, duty);
*CMPR1 = 0x1234;
Direct
Register addresses # defined individually
User must compute bit-field masks
Not easy-to-read
Bit Field Header Files
Header files define all registers as structures
Bit-fields directly accessible
Easy-to-read
Driverlib
Driverlib performs low-level register manipulation
Easy-to-read
Highest abstraction level

## Slide 5: Driver Library (Driverlib)
Driverlib “APIs” provide many advantages and benefits:
  Require less detailed knowledge of the hardware
  Produce code that is easy-to-write and easy-to-read
  Generally require less development time
  Provide portability across other C2000 devices
  Optimize well; remove overhead and speed up code execution
If needed, “direct register access” can be used to create custom Driverlib functions
  Requires detailed knowledge of:
    Operation of each register and bit field
    Interactions and sequencing required for proper peripheral operation
  Can result in smaller and more efficient code
Both APIs and direct register access can be used independently or combined

## Slide 6: Driverlib File Structure
Software driver (Driverlib API)
Contains source code for drivers
  .c files and .h files
Direct register access
Contains peripheral, interrupt, and register access header files
hw_*.h
  One per peripheral / memmap device function
  Defines all registers and bit fields within the registers for each peripheral
  Used by driver API to access a peripheral
  Can be used to bypass driverlib API
hw_memmap.h
  Defines base address for each peripheral
hw_ints.h
  Defines interrupt numbers (used with interrupt.c)
hw_types.h
  Defines type definitions

## Slide 7: Construction of a Driverlib Function
Driverlib API functions are built on top of the direct register access model
  Useful to understand for debugging or when needing to directly access a register or bit field
  Uses a similar traditional #define approach
Naming convention used in header files macros:
  Values that end in _BASE are module instance base addresses
  Values that contain an _O_ are register address offsets
  Values that end in _M are mask for multi-bit field register
  Values that end in _S are the number of bits to shift
  hw_types.h contains the follow macros:
  HWREG(x) are 32-bit accesses
  HWREGH(x) are 16-bit accesses (or upper/lower 32-bit word)
  HWREGB(x) are 8-bit accesses
  HWREGBP(x) are used with byte peripherals
  where x is the address to be accessed

## Slide 8: Driverlib Function Example
static inline void EPWM_setClockPrescaler(uint32_t base,
EPWM_ClockDivider prescaler,
EPWM_HSClockDivider highSpeedPrescaler)
{
ASSERT(EPWM_isBaseValid(base));
// write to CLKDIV and HSPCLKDIV bit
HWREGH(base + EPWM_O_TBCTL) =
((HWREGH(base + EPWM_O_TBCTL) &
~(EPWM_TBCTL_CLKDIV_M | EPWM_TBCTL_HSPCLKDIV_M))|
(((uint16_t)prescaler << EPWM_TBCTL_CLKDIV_S) |
((uint16_t)highSpeedPrescaler << EPWM_TBCTL_HSPCLKDIV_S)));
}
epwm.h – EPWM Driver
// Configure EPWM clock prescaler to TBCLK = EPWMCLK
EPWM_setClockPrescaler(EPWM2_BASE, EPWM_CLOCK_DIVIDER_1, EPWM_HSCLOCK_DIVIDER_1);
user.c – user source file
#define EPWM2_BASE 0x00004100U // EPWM2
hw_memmap.h
Contains #define for all:
EPWM_xxx values in epwm.h
hw_epwm.h
Contains typedef enum values for:
EPWM_CLOCK_DIVIDER (_1 = 0)
EPWM_HSCLOCK_DIVIDER (_1 = 0)
epwm.h
Note: CCS ‘F3’ will open declaration

## Slide 9: Driverlib Optimization
In general, software abstraction can come at the cost of performance
However, Driverlib’s low-level abstraction and optimization-conscious design makes it efficient
Most functions have been declared as inline functions
  Allows the compiler to treat functions like macros when optimizer is turned on
    Removes the overhead of function calls and speeds up code execution
Use compiler option --opt_level set to 0 or higher

## Slide 10: Optimization Example
Read ADC conversion results
  Optimization level of -O2
  Single MOV instruction is generated for each function call
When compiled with:
  Optimization level of -O2
  Turn off inlining (--disable_inlining)
Results:
  22 words of code
    4 words for ADC_readResult() and 18 words for the calling functions
  53 cycles to execute

## Slide 11: Driverlib API Functions
ADC | DMA | Interrupt
ASysCtl | ECAP | LIN
CAN | EPWM | MemCfg
CLA | EQEP | PGA
CLAPROMCRC | Flash | PMBus
CMPSS | FSI | SCI
CPU Timer | GPIO | SDFM
DAC | HRCAP | SPI
DCC | HRPWM | SysCtrl
DCSM | I2C | X-BAR
See the F28004x Peripheral Driver Library User’s Guide for details

## Slide 12: Driverlib Examples
Example projects are helpful for getting started
C:\ti\c2000\C2000Ware_<version>\driverlib\f28004x\examples

## Slide 13: Content Assist
Activate by: Ctrl + Space

## Slide 14: Driverlib Documentation
Available in .pdf or .html formats
C:\ti\c2000\C2000Ware_<version>\device_support\f28004x\docs

## Slide 15: Driverlib Summary
Easier code development
Easy to use
Has been written to be optimized well
CCS – hover over function to view description
Compatible with Bit Field Header Files
TI has already done all the work!
  Use the correct Driverlib package for your device:
Go to http://www.ti.com and enter “C2000Ware” in the keyword search box
F28004x | F2807x | F2837xS | F2837xD

## Slide 16: Lab File Directory Structure
All modified files are in the Project Folder
Project Source Files
Other Source Files that are “Added” to the Project Folder
Supporting Files
Note: CCSv9 will automatically add ALL files contained in the folder where the project is created
Easier to make projects portable
${PROJECT_ROOT} provides an anchor point for paths to files that travel with the project
Easier to maintain and update supporting files
Source files for multiple part lab exercises

## Slide 17
C2000 Technical Training
www.ti.com/c2000