## Slide 1: System Initialization
Module 5
C2000™ Microcontroller Workshop
Copyright © 2019 Texas Instruments. All rights reserved.

## Slide 2: Module Objectives
OSC/PLL Clock Module
Watchdog Timer
General Purpose I/O
External Interrupts
Low Power Modes
Register Protection

## Slide 3: Module Objectives
OSC/PLL Clock Module
Watchdog Timer
General Purpose I/O
External Interrupts
Low Power Modes
Register Protection

## Slide 4: Oscillator / PLL Clock Module
* default
X2
XTAL OSC
X1
XTAL
XCLKIN
(X2 n.c.)
Internal
OSC 1
(10 MHz)
Internal
OSC 2
(10 MHz)
CLKSRCCTL1
PLL
PLLCLK
OSCCLK
PLLSYSCLK
(PLL bypass)
SYSPLLMULT
MUX
1/n
SYSCLKDIVSEL
OSC1CLK
OSC2CLK
XTAL
WDCLK
1x
00*
01
0*
1
SYSPLLCTL1
CPU
PCLKCRx
PCLKCRx
One per SYSCLK peripheral
One per LSPCLK peripheral
CLKSRCCTL2
One per CAN module
0*
1
SYSCLK
LOSPCP
LSPCLK
CPUCLK
PERxSYSCLK
PERxLSPCLK
CAN bit Clock

## Slide 5: PLL and LOSPCP
PLLCLK
OSCCLK
CPU
PLLSYSCLK
SYSCLK
LOSPCP
(PLL bypass)
LSPCLK
1/n
0*
1
1x
00*
01
INTOSC1
INTOSC2
XTAL
SYSCTL_OSCSRC_OSC1
SYSCTL_OSCSRC_OSC2
SYSCTL_OSCSRC_XTAL
SYSCTL_PLL_ENABLE
SYSCTL_PLL_DISABLE
SYSCTL_SYSDIV(x)
where x is either 1 or an even value up to 126
SYSCTL_IMULT(x)
where x is a value from 1 to 127
SYSCTL_FMULT_0
SYSCTL_FMULT_1_4
SYSCTL_FMULT_1_2
SYSCTL_FMULT_3_4
SysCtl_setClock(config);
The config parameter is the OR of several different values, many of which are grouped into sets where only one can be chosen
SYSCTL_LSPCLK_PRESCALE_x
where x is 1, 2, 4, 6, 8, 10, 12, 14
SysCtl_setLowSpeedClock( );
LSPCLK = SYSCLK / 4 (default)
PLL

## Slide 6: Initializing Clock Modules
// CPU Initialization
Device_init();
•
•
•
Main.c
device.h
#define DEVICE_SETCLOCK_CFG (SYSCTL_OSCSRC_XTAL |
SYSCTL_IMULT(10) |
SYSCTL_FMULT_NONE |
SYSCTL_SYSDIV(2) |
SYSCTL_PLL_ENABLE)
device.c
void Device_init(void)
{
// Set up PLL control and clock dividers
SysCtl_setClock(DEVICE_SETCLOCK_CFG)
SysCtl_setLowSpeedClock(SYSCTL_LSPCLK_PRESCALE_4);
// Turn on all peripherals
Device_enableAllPeripherals()
}
void Device_enableAllPeripherals(void
{
SysCtl_enablePeripheral(SYSCTL_PERIPH_CLK_<name>);
}
•
•
•
•
•
•
sysctl.h
Contains values that can be passed to:
SysCtl_setClock()
SysCtl_setLowSpeedClock()
SysCtl_enablePeripheral()
;
100 MHz SYSCLK frequency based on DEVICE_SETCLOCK_CFG
PLLSYSCLK = 20MHz (XTAL_OSC) * 10 (IMULT) * 1 (FMULT) / 2 (PLLCLK_BY_2)
;
)

## Slide 7: Peripheral Clock Enable / Disable
SYSCTL_PERIPH_CLK_CLA1 | SYSCTL_PERIPH_CLK_ADCx (x = A to C)
SYSCTL_PERIPH_CLK_EPWMx (x = 1 to 8) | SYSCTL_PERIPH_CLK_CMPSSx (x = 1 to 7)
SYSCTL_PERIPH_CLK_ECAPx (x = 1 to 7) | SYSCTL_PERIPH_CLK_PGAx (x = 1 to 7)
SYSCTL_PERIPH_CLK_EQEPx (x = 1 or 2) | SYSCTL_PERIPH_CLK_DACx (x = A or B)
SYSCTL_PERIPH_CLK_SD1 | SYSCTL_PERIPH_CLK_FSITXA
SYSCTL_PERIPH_CLK_SCIx (x = A or B) | SYSCTL_PERIPH_CLK_FSIRXA
SYSCTL_PERIPH_CLK_SPIx (x = A or B) | SYSCTL_PERIPH_CLK_LINA
SYSCTL_PERIPH_CLK_I2CA | SYSCTL_PERIPH_CLK_PMBUSA
SYSCTL_PERIPH_CLK_CANx (x = A or B) | SYSCTL_PERIPH_CLK_DCC0
SYSCLK
Peripheral
PCLKCRx
Register
Driverlib function used to enable / disable peripheral:
SysCtl_[enable|disable]Peripheral(peripheral);
  peripheral parameter values:

## Slide 8: Module Objectives
OSC/PLL Clock Module
Watchdog Timer
General Purpose I/O
External Interrupts
Low Power Modes
Register Protection

## Slide 9: Watchdog Timer
Resets the device if the CPU crashes
  Watchdog counter runs independently of CPU
  If counter overflows, a reset or interrupt is triggered (user selectable)
  CPU must write correct data key sequence to reset the counter before overflow
Watchdog must be serviced or disabled within 131,072 WDCLK cycles after reset
This translates to 13.11 ms with a 10 MHz WDCLK

## Slide 10: Watchdog Timer Module
WDCLK
System
Reset
8-bit Watchdog
Counter
CLR
Watchdog
Reset Key
Register
55 + AA
Detector
1 0 1
/
/
3
3
WDDIS
WDCHK
Bad WDCHK Key
Output
Pulse
WDRST
WDINT
WDOVERRIDE
Good Key
Watchdog
Pre-scaler
WDPS
WDCNTR
window minimum
WDWCR
WDCNTR less than WDWCR
CNT
WDKEY
Watchdog
Pre-divider
WDPRECLKDIV

## Slide 11: Watchdog Pre-divider and Pre-scaler
Remember: Watchdog starts counting immediately after reset is released!
Reset default with WDCLK = 10 MHz computed as
(1/10 MHz) * 512 * 1 * 256 = 13.11 ms
WDCLK
Watchdog
Pre-scaler
WDPS
Watchdog
Pre-divider
WDPRECLKDIV
SysCtl_setWatchdogPrescaler(SYSCTL_WD_PRESCALE_x);
where x is 1, 2, 4, 8, 16, 32, or 64
default = 1
SysCtl_setWatchdogPredivider(SYSCTL_WD_PREDIV_x);
where x is 2, 4, 8, 16, 32, 64, 128, 256, 512, 1024, 2048, or 4096
default = 512 (providing backwards compatibility)

## Slide 12: Watchdog Driverlib Functions
WDDIS – disable / enable
  Functions only if WDOVERRIDE is not cleared
SysCtl_disableWatchdog();
SysCtl_enableWatchdog();
WDOVERRIDE (clear only to protect – reset device to disable)
SysCtl_clearWatchdogOverride();
Watchdog Mode – reset / interrupt
SysCtl_setWatchdogMode(mode);
    mode parameter values:
    SYSCTL_WD_MODE_RESET
    SYSCTL_WD_MODE_INTERRUPT
Watchdog Minimum Window
SysCtl_setWatchdogWindowValue(value);
    value parameter sets a minimum delay between counter resets (0 = disabled)

## Slide 13: Resetting the Watchdog
Driverlib functions:
  SysCtl_serviceWatchdog(); // resets the watchdog
  SysCtl_enableWatchdogReset(); // writes 0x55 WDKEY
  SysCtl_resetWatchdog(); // writes 0xAA WDKEY
WDKEY write values:
  0x55 - counter enabled for reset on next 0xAA write
  0xAA - counter set to zero if reset enabled
Writing any other value has no effect
Watchdog should not be serviced solely in an ISR
  If main code crashes, but interrupt continues to execute, the watchdog will not catch the crash
  Could put the 0x55 WDKEY in the main code, and the 0xAA WDKEY in an ISR; this catches main code crashes and also ISR crashes

## Slide 14: WDKEY Write Results
Sequential
Step
1
2
3
4
5
6
7
8
9
10
11
12
13
14
Value Written
to WDKEY
0xAA
0xAA
0x55
0x55
0x55
0xAA
0xAA
0x55
0xAA
0x55
0x23
0xAA
0x55
0xAA
Result
No action
No action
WD counter enabled for reset on next AAh write
WD counter enabled for reset on next AAh write
WD counter enabled for reset on next AAh write
WD counter is reset
No action
WD counter enabled for reset on next AAh write
WD counter is reset
WD counter enabled for reset on next AAh write
No effect; WD counter not reset on next AAh write
No action due to previous invalid value
WD counter enabled for reset on next AAh write
WD counter is reset

## Slide 15: Module Objectives
OSC/PLL Clock Module
Watchdog Timer
General Purpose I/O
External Interrupts
Low Power Modes
Register Protection

## Slide 16: GPIO Grouping Overview
Internal Bus
GPIO Port A Group
Mux1 Register
(GPAGMUX1)
[GPIO 0 to 15]
GPIO Port A
Direction Register
(GPADIR)
[GPIO 0 to 31]
GPIO Port A Mux1
Register
(GPAMUX1)
[GPIO 0 to 15]
GPIO Port A Group
Mux2 Register
(GPAGMUX2)
[GPIO 16 to 31]
GPIO Port A Mux2
Register
(GPAMUX2)
[GPIO 16 to 31]
GPIO Port A
Input
Qual
GPIO Port B Group
Mux1 Register
(GPBGMUX1)
[GPIO 32 to 47]
GPIO Port B
Direction Register
(GPBDIR)
[GPIO 32 to 63]
GPIO Port B Mux1
Register
(GPBMUX1)
[GPIO 32 to 47]
GPIO Port B Group
Mux2 Register
(GPBGMUX2)
[GPIO 48 to 63]
GPIO Port B Mux2
Register
(GPBMUX2)
[GPIO 48 to 63]
GPIO Port B
Input
Qual
Analog
Port H
Input
Qual
[GPIO 224 to 255]
Input
Inverter

## Slide 17: GPIO Pin Block Diagram
GPyDAT(W)
GPySET
GPyCLEAR
GPyTOGGLE
GPyDAT(W)
GPySET
GPyCLEAR
GPyTOGGLE
00:00
00:01
00:10
00:11
01:00
01:01
01:10
01:11
10:xx
11:xx
Peripheral 1
Peripheral 2
Peripheral 3
GPIO
GPIO & Peripherals 9-11
Peripheral 5
Peripheral 6
Peripheral 7
GPIO
GPIO & Peripherals 13-15
00:00
00:01
00:10
00:11
01:00
01:01
01:10
01:11
10:xx
11:xx
Peripheral 1
Peripheral 2
Peripheral 3
unused
Peripherals 9-11
Peripheral 5
Peripheral 6
Peripheral 7
Peripherals 13-15
unused
GPyGMUX1/2
GPyMUX1/2
GPyG:GPy
00
01
10
11
CPU
CLA
reserved
reserved
Input
X-BAR
GPyCSEL1-4
Pin
Internal Pull-Up
0 = enable
1 = disable
(default GPIO 0-xx)
GPyPUD
0 = Input
1 = Output
GPyDIR
Input
Qualification
GPyINV
GPyQSEL1/2
GPyCTRL
0 1
GPyDAT(R)
CPU
GPyDAT(R)
CLA
y = A or B
CPU
CPU
CPU
CPU
CPU
CPU
GPyODR
CPU
0 = Normal
1 = Open Drain

## Slide 18: Configuring GPIO Pins using Driverlib
Configure peripheral multiplexing
GPIO_setPinConfig(pinConfig);
  pinConfig is defined in pin_map.h (GPIO_#_value)
Configure pin properties
GPIO_setPadConfig(pin, pinType);
  pin is the GPIO pin number
  pinType can be the following values:
    GPIO_PIN_TYPE_STD
    GPIO_PIN_TYPE_PULLUP
    GPIO_PIN_TYPE_OD
    GPIO_PIN_TYPE_INVERT
  INVERT may be OR-ed with STD or PULLUP
Set direction for pins configured as GPIO
GPIO_setDirectionMode(pin, pinIO);
  pin is the GPIO pin number
  pinIO can be following values:
    GPIO_DIR_MODE_IN
    GPIO_DIR_MODE_OUT

## Slide 19: GPIO Input Qualification
Input qualification available on ports A, B, and H
Individually selectable per pin
  no qualification (peripherals only)
  sync to SYSCLK only
  qualify 3 samples
  qualify 6 samples
QUALPRD = SYSCLKOUT/n
  where n can be 1 or an even value between 2 and 510 inclusive
Input
Qualification
pin
to GPIO and peripheral modules
SYSCLK
T
T
T
samples taken
T = qual period

## Slide 20: Input Qualification Driverlib Functions
Qualification Mode
GPIO_setQualificationMode(pin, qualification);
  pin is the GPIO pin number
  qualification values are:
    GPIO_QUAL_SYNC
    GPIO_QUAL_3SAMPLE
    GPIO_QUAL_6SAMPLE
    GPIO_QUAL_ASYNC
Qualification Period
GPIO_setQualificationPeriod(pin, divider);
  pin is the GPIO pin number
  divider is the value by which the frequency of SYSCLKOUT is divided and it can be 1 or an even value between 2 and 510 inclusive

## Slide 21: GPIO Core Select
Selects which core’s GPIODAT/SET/CLEAR/TOGGLE registers are used to control a pin
Each pin individually controlled
A: GPIO31-24 GPIO23-16 GPIO15-8 GPIO7-0
B: GPIO63-56 GPIO55-48 GPIO47-40 GPIO39-32
GPxCSEL1
0
31
GPxCSEL3
0
31
GPxCSEL4
0
31
GPxCSEL2
0
31
Driverlib function used to select core:
GPIO_setMasterCore(pin, core);
  pin is the GPIO pin number
  core parameter values:
    GPIO_CORE_CPU1
    GPIO_CORE_CPU1_CLA1

## Slide 22: Driverlib GPIO Data Control Functions
Pin Functions
  GPIO_readPin(pin);
  GPIO_writePin(pin, outVal);
  GPIO_togglePin(pin);
  pin is the GPIO pin number
  outVal parameter is the value written to the pin
Port Functions
  GPIO_readPortData(port);
  GPIO_writePortData(port, outVal);
  GPIO_setPortPins(port, pinMask);
  GPIO_clearPortPins(port, pinMask);
  GPIO_togglePortPins(port, pinMask);
  port is the GPIO port: GPIO_PORT_x where x is the port letter
  outVal parameter is bit-packed value (32 pins) written to the port
  pinMask parameter is a bit-packed value (32 pins) masking the port

## Slide 23: GPIO Input X-BAR

## Slide 24: GPIO Input X-BAR Architecture
INPUTx
GPIO 0
GPIO n
This block diagram is replicated 16 times
input | Destinations (pin is the GPIO pin number)
XBAR_INPUT1 | eCAPx, ePWM X-BAR, ePWM[TZ1, TRIP1], Output X-BAR
XBAR_INPUT2 | eCAPx, ePWM X-BAR, ePWM[TZ2, TRIP2], Output X-BAR
XBAR_INPUT3 | eCAPx, ePWM X-BAR, ePWM[TZ3, TRIP3], Output X-BAR
XBAR_INPUT4 | eCAPx, ePWM X-BAR, XINT1, Output X-BAR
XBAR_INPUT5 | eCAPx, ePWM X-BAR, XINT2, ADCEXTSOC, EXTSYNCIN1, Output X-BAR
XBAR_INPUT6 | eCAPx, ePWM X-BAR, XINT3, ePWM[TRIP6], EXTSYNCIN2, Output X-BAR
XBAR_INPUT7 | eCAPx, ePWM X-BAR
XBAR_INPUT8 | eCAPx, ePWM X-BAR
XBAR_INPUT9 | eCAPx, ePWM X-BAR
XBAR_INPUT10 | eCAPx, ePWM X-BAR
XBAR_INPUT11 | eCAPx, ePWM X-BAR
XBAR_INPUT12 | eCAPx, ePWM X-BAR
XBAR_INPUT13 | eCAPx, ePWM X-BAR, XINT4
XBAR_INPUT14 | eCAPx, ePWM X-BAR, XINT5
XBAR_INPUT15 | eCAPx
XBAR_INPUT16 | eCAPx
XBAR_setInputPin(input, pin);

## Slide 25: GPIO Output X-BAR

## Slide 26: GPIO Output X-BAR Architecture
MUX | 0 | 1 | 2 | 3
16 | SD1FLT1.COMPH | SD1FLT1.COMPH_OR_COMPL |  | 
17 | SD1FLT1.COMPL |  |  | CLAHALT
18 | SD1FLT2.COMPH | SD1FLT2.COMPH_OR_COMPL |  | 
19 | SD1FLT2.COMPL |  |  | 
20 | SD1FLT3.COMPH | SD1FLT3.COMPH_OR_COMPL |  | 
21 | SD1FLT3.COMPL |  |  | 
22 | SD1FLT4.COMPH | SD1FLT4.COMPH_OR_COMPL |  | 
23 | SD1FLT4.COMPL |  |  | 
24 |  |  |  | 
25 |  |  |  | 
26 |  |  |  | 
27 |  |  |  | 
28 |  |  |  | 
29 |  |  |  | 
30 |  |  |  | 
31 |  |  |  | 
MUX | 0 | 1 | 2 | 3
0 | CMPSS1.CTRIPOUTH | CMPSS1.CTRIPOUTH_OR_CTRIPOUTL | ADCAEVT1 | ECAP1OUT
1 | CMPSS1.CTRIPOUTL | INPUTXBAR1 |  | ADCCEVT1
2 | CMPSS2.CTRIPOUTH | CMPSS2.CTRIPOUTH_OR_CTRIPOUTL | ADCAEVT2 | ECAP2OUT
3 | CMPSS2.CTRIPOUTL | INPUTXBAR2 |  | ADCCEVT2
4 | CMPSS3.CTRIPOUTH | CMPSS3.CTRIPOUTH_OR_CTRIPOUTL | ADCAEVT3 | ECAP3OUT
5 | CMPSS3.CTRIPOUTL | INPUTXBAR3 |  | ADCCEVT3
6 | CMPSS4.CTRIPOUTH | CMPSS4.CTRIPOUTH_OR_CTRIPOUTL | ADCAEVT4 | ECAP4OUT
7 | CMPSS4.CTRIPOUTL | INPUTXBAR4 |  | ADCCEVT4
8 | CMPSS5.CTRIPOUTH | CMPSS5.CTRIPOUTH_OR_CTRIPOUTL | ADCBEVT1 | ECAP5OUT
9 | CMPSS5.CTRIPOUTL | INPUTXBAR5 |  | 
10 | CMPSS6.CTRIPOUTH | CMPSS6.CTRIPOUTH_OR_CTRIPOUTL | ADCBEVT2 | ECAP6OUT
11 | CMPSS6.CTRIPOUTL | INPUTXBAR6 |  | 
12 | CMPSS7.CTRIPOUTH | CMPSS7.CTRIPOUTH_OR_CTRIPOUTL | ADCBEVT3 | ECAP7OUT
13 | CMPSS7.CTRIPOUTL | ADCSOCAO |  | 
14 |  |  | ADCBEVT4 | EXTSYNCOUT
15 |  | ADCSOCBO |  | 
0
0.0
0.1
0.2
0.3
1
1.0
1.1
1.2
1.3
31
31.0
31.1
31.2
31.3
Latch
OUTPUTx
XBAR_invertOutputSignal(output, invert);
XBAR_setOutputLatchMode(output, enable);
XBAR_enableOutputMux(output, muxes);
XBAR_setOutputMuxConfig(output, muxConfig);
This block diagram is replicated 8 times
Muxed with Peripheral GPIO Pins

## Slide 27: Module Objectives
OSC/PLL Clock Module
Watchdog Timer
General Purpose I/O
External Interrupts
Low Power Modes
Register Protection

## Slide 28: External Interrupts
5 external interrupt signals
  XINT1, XINT2, XINT3, XINT4 and XINT5
Each external interrupt can be mapped to any of the GPIO pins via the X-BAR Input architecture
  XINT1-5 are sources for Input X-BAR signals 4, 5, 6, 13, and 14 respectively
XINT1, XINT2, and XINT3 also have a free-running 16-bit counter which measures the elapsed time between interrupts
  Counter resets to zero each time the interrupt occurs
Driverlib function used to read counter value:
    GPIO_getInterruptCounter(extIntNum);
    extIntNum parameter is: GPIO_INT_XINTx (x = 1, 2, or 3)

## Slide 29: Configuring External Interrupts
Configuring external interrupts is a multi-step process:
  Select GPIO pin, set polarity, and enable interrupt
  GPIO_setInterruptPin(pin, extIntNum);
  GPIO_setInterruptType(extIntNum, intType);
  GPIO_[enable|disable]Interrupt(extIntNum);
  pin is the GPIO pin number
  extIntNum parameter specifies the external interrupt
    GPIO_INT_XINT1
    GPIO_INT_XINT2
    GPIO_INT_XINT3
    GPIO_INT_XINT4
    GPIO_INT_XINT5
  intType parameter specifies the type of interrupt trigger
    GPIO_INT_TYPE_FALLING_EDGE
    GPIO_INT_TYPE_RISING_EDGE
    GPIO_INT_TYPE_BOTH_EDGES

## Slide 30: Module Objectives
OSC/PLL Clock Module
Watchdog Timer
General Purpose I/O
External Interrupts
Low Power Modes
Register Protection

## Slide 31: Low Power Modes
Low Power Mode | CPU Logic Clock | Peripheral Logic Clock | Watchdog Clock | PLL | INTOSC 1/2 | XTAL
Normal Run | on | on | on | on | on | on
IDLE | off | on | on | on | on | on
HALT | off | off | off | off | on | on
HALT
  INTOSC – not automatically powered down; software configurable
  XTAL – can be powered down by software at any time
STANDBY is not supported but can be emulated – see device Technical Reference Manual
See device data sheet for each low power mode power consumption

## Slide 32: Low Power Mode Exit
IDLE
HALT
Reset
yes
yes
Any Enabled Interrupt
yes
no
yes
no / yes
Exit
Interrupt
Low Power
Mode
Watchdog
Interrupt
GPIO
0 - 63 Signal
no
yes

## Slide 33: Low Power Mode Driverlib Functions
Configuring low power mode
  SysCtl_enterIdleMode(); //enter IDLE mode
  SysCtl_enterHaltMode(); //enter HALT mode
Set pin to wake up device from HALT mode
  SysCtl_enableLPMWakeupPin(pin);
  SysCtl_disableLPMWakeupPin(pin);
  pin is the GPIO pin number (numerical value 0-63)
Run watchdog while in HALT mode
  SysCtl_enableWatchdogInHalt();
  SysCtl_disableWatchdogInHalt();

## Slide 34: Module Objectives
OSC/PLL Clock Module
Watchdog Timer
General Purpose I/O
External Interrupts
Low Power Modes
Register Protection

## Slide 35: LOCK Protection Registers
“LOCK” registers protects several system configuration registers from spurious CPU writes
Once the LOCK Driverlib functions are set the respective locked registers can no longer be modified by software:
ASysCtl_lockTemperatureSensor | ASysCtl_lockCMPHNMux | PGA_lockRegisters
ASysCtl_lockANAREF | ASysCtl_lockCMPLNMux | SysCtl_lockAccessControlRegs
ASysCtl_lockVMON | ASysCtl_lockVREG | SysCtl_lockSyncSelect
ASysCtl_lockDCDC | DAC_lockRegister | XBAR_lockInput
ASysCtl_lockPGAADCINMux | EPWM_lockRegisters | XBAR_lockOutput
ASysCtl_lockCMPHPMux | HRPWM_lockRegisters | XBAR_lockEPWM
ASysCtl_lockCMPLPMux | MemCfg_commitConfig | 
FSI_lockTxCtrl | GPIO_lockPortConfig | MemCfg_lockConfig
FSI_lockRxCtrl | GPIO_unlockPortConfig | MemCfg_unlockConfig
SysCtl_lockExtADCSOCSelect |  | 
The following Driverlib functions can be locked/unlocked:

## Slide 36: EALLOW Protection (1 of 2)
EALLOW stands for Emulation Allow
Code access to protected registers allowed only when EALLOW = 1 in the ST1 register
The emulator can always access protected registers
EALLOW bit controlled by assembly level instructions
  ‘EALLOW’ sets the bit (register access enabled)
  ‘EDIS’ clears the bit (register access disabled)
EALLOW bit cleared upon ISR entry, restored upon exit

## Slide 37: EALLOW Protection (2 of 2)
Device Configuration & Emulation
Flash
Code Security Module
PIE Vector Table
DMA, CLA, SD, EMIF, X-Bar (some registers)
CANA/B (control registers only; mailbox RAM not protected)
ePWM, CMPSS, ADC, DAC (some registers)
GPIO (control registers only)
System Control
See device data sheet and Technical Reference Manual for detailed listings
Driverlib functions automatically take care of EALLOW and EDIS protection
The following registers are protected:

## Slide 38: Lab 5: Procedure - System Initialization
LAB5 files have been provided as a starting point
Use watchdog to generate a reset and interrupt:
  Part 1
  Perform processor system initialization
    Test operation with watchdog disabled
  Configure the watchdog to generate a reset
    Learn about reset process
  Part 2
  Initialize the peripheral interrupt expansion (PIE) vectors
  Configure the watchdog to generate an interrupt
    Learn about the interrupt process

## Slide 39
C2000 Technical Training
www.ti.com/c2000