## Slide 1: Analog Subsystem
Module 6
C2000™ Microcontroller Workshop
Copyright © 2019 Texas Instruments. All rights reserved.

## Slide 2: Module Objectives
Understand the operation of the:
  Analog-to-Digital Converter (ADC)
  Comparator Subsystem (CMPSS)
  Programmable Gain Amplifier (PGA)
  Digital-to-Analog Converter (DAC)
  Analog Subsystem Interconnect
Use the ADC to perform data acquisition

## Slide 3: Analog System Peripherals
Three 12-bit Analog-to-Digital Converters (ADCs)
  3.45 MSPS each (up to 10.35 MSPS per system)
  Selectable internal reference of 2.5 V or 3.3 V
  Ratiometric external reference set by VREFHI/VREFLO
Seven Comparator Subsystems (CMPSS)
  Each contains:
    Two analog comparators
    Two programmable 12-bit reference DACs
    One ramp generator and two digital glitch filters
Seven Programmable Gain Amplifiers (PGAs)
  Each features:
    Four programmable gain modes: 3x, 6x, 12x, 24x
    Programmable output filtering
Two 12-bit Buffered Digital-to-Analog Converter Outputs (DACs)
  Selectable reference voltage source

## Slide 4: ADC Module Block Diagram
12-bit
A/D
Converter
SOCx
EOCx
S/H
MUX
ADCRESULT0
ADCRESULT1
ADCRESULT2
ADCRESULT15
Result
MUX
ADC
Generation
Logic
ADC full-scale input range is VREFLO to VREFHI
CHSEL
ADC
Interrupt
Logic
ADCINT1-4
Software
External Pin(GPIO/ADCEXTSOC)
EPWMxSOCA/C (x = 1 to 8)
EPWMxSOCB/D (x = 1 to 8)
CPU1 Timer (0,1,2)
SOCx Signal
ADCINT1
ADCINT2
SOC0 TRIGSEL CHSEL ACQPS
SOC1 TRIGSEL CHSEL ACQPS
SOC2 TRIGSEL CHSEL ACQPS
SOC3 TRIGSEL CHSEL ACQPS
SOC15 TRIGSEL CHSEL ACQPS
SOCx Triggers
SOCx Configuration Registers
ADCIN1
ADCIN0
ADCIN2
ADCIN3
ADCIN14
ADCIN15
Post Processing Blocks
*** Multiple ADC modules allow for simultaneous sampling or independent operation ***

## Slide 5: ADC SOCx Functional Diagram
This block diagram is replicated 16 times
ADCINT1
ADCINT2
Re-Trigger
ADCINT1
ADCINT2
ADCINT3
ADCINT4
Channel
Select
Sample
Window
Result
Register
S
O
C
x
E
O
C
x
ADC_setupSOC(base, socNumber, trigger, channel, sampleWindow);
ADC_setInterruptSOCTrigger(base, socNumber, trigger);
ADC_setInterruptSource(base, adcIntNum, socNumber);
ADC_[enable|disable]Interrupt(base, adcIntNum);
ADC_readResult(resultBase, socNumber);
Software Trigger
TINT0 (CPU1 Timer 0)
TINT1 (CPU1 Timer 1)
TINT2 (CPU1 Timer 2)
ADCEXTSOC (GPIO)
SOCA/C (ePWM1)
SOCB/D (ePWM1)
SOCA/C (ePWM8)
SOCB/D (ePWM8)
T
r
i
g
g
e
r
ADC_forceSOC(base, socNumber);
EOC Int Pulse: ADC_setInterruptPulseMode(base, pulseMode);
(generation at beginning of conversion or one cycle prior to results)

## Slide 6: ADC SOC Driverlib Function
Configure a start-of-conversion (SOC)
ADC_setupSOC(base, socNumber, trigger, channel, sampleWindow);
  base is the ADC base address: ADCx_BASE (x = A to C)
  socNumber values are:
    ADC_SOC_NUMBERx (x = 0 to 15)
  trigger values are:
    ADC_TRIGGER_SW_ONLY
    ADC_TRIGGER_CPU1_TINTx (x = 0 to 2)
    ADC_TRIGGER_GPIO
    ADC_TRIGGER_EPWMx_SOCA (x = 1 to 8)
    ADC_TRIGGER_EPWMx_SOCB (x = 1 to 8)
  channel values are:
    ADC_CH_ADCINx (x = 0 to 15)
  sampleWindow parameter is the acquisition window duration in SYSCLK cycles: value between 1 and 512 cycles inclusive

## Slide 7: ADC Driverlib Functions
Configure an interrupt start-of-conversion trigger
ADC_setInterruptSOCTrigger(base, socNumber, trigger);
Set EOC source for an ADC interrupt
ADC_setInterruptSource(base, adcIntNum, socNumber);
ADC_[enable|disable]Interrupt(base, adcIntNum);
Force an SOC conversion (software trigger)
ADC_forceSOC(base, socNumber);
Configure ADC EOC interrupt pulse generation
ADC_setInterruptPulseMode(base, pulseMode);
Read ADC result register
ADC_readResult(resultBase, socNumber);
  base is the ADC base address: ADCx_BASE (x = A to C)
    socNumber is: ADC_SOC_NUMBERx (x = 0 to 15)
    Trigger value is:
      ADC_INT_SOC_TRIGGER_NONE
      ADC_INT_SOC_TRIGGER_ADCINTx (x = 1 or 2)
    adcIntNum value is: ADC_INT_NUMBERx (x = 1 to 4)
    pulseMode value is: ADC_PULSE_END_OF_x (x = ACQ_WIN or CONV)
    resultBase value is: ADCxRESULT_BASE (x = A to C)

## Slide 8: Example – ADC Triggering
Sample A1  A3  A5 when ePWM1 SOCB/D is generated and then generate ADCINT1:
Channel
A1
Sample
20 cycles
Result0
Channel
A3
Sample
26 cycles
Result1
Channel
A5
Sample
22 cycles
Result2
SOC0
SOC1
SOC2
no interrupt
no interrupt
ADCINT1
SOCB/D (ETPWM1)
Sample A2  A4  A6 continuously and generate ADCINT2:
Channel
A2
Sample
22 cycles
Result3
Channel
A4
Sample
28 cycles
Result4
Channel
A6
Sample
24 cycles
Result5
SOC3
SOC4
SOC5
no interrupt
no interrupt
ADCINT2
ADCINT2
Software Trigger
Note: setting ADCINT2 flag does not need to generate an interrupt

## Slide 9: Example – ADC Ping-Pong Triggering
Sample all channels continuously and provide Ping-Pong interrupts to CPU/system:
Channel
B0
Sample
20 cycles
SOC0
no interrupt
ADCINT2
Software Trigger
Result0
Channel
B1
Sample
20 cycles
SOC1
no interrupt
Result1
Channel
B2
Sample
20 cycles
SOC2
no interrupt
Result2
Channel
B3
Sample
20 cycles
SOC3
Result3
Channel
B4
Sample
20 cycles
SOC4
no interrupt
Result4
Channel
B5
Sample
20 cycles
SOC5
Result5
ADCINT1
ADCINT2
ADCINT1

## Slide 10: ADC Conversion Priority
When multiple SOC flags are set at the same time – priority determines the order in which they are converted
High Priority
  High priority SOC will interrupt the round robin wheel after current conversion completes and insert itself as the next conversion
  After its conversion completes, the round robin wheel will continue where it was interrupted
Round Robin Burst Mode
  Allows a single trigger to convert one or more SOCs in the round robin wheel
  Uses BURSTTRIG instead of TRIGSEL for all round robin SOCs (not high priority)
Round Robin Priority (default)
  No SOC has an inherent higher priority than another
  Priority depends on the round robin pointer

## Slide 11: Conversion Priority Functional Diagram
Round Robin Pointer
Points to the last converted
round robin SOCx and
determines order
of conversions
SOC Priority
Determines cutoff point
for high priority and
round robin mode
SOC0
SOC1
SOC2
SOC3
SOC4
SOC5
SOC6
SOC7
SOC8
SOC9
SOC10
SOC11
SOC12
SOC13
SOC14
SOC15
Round Robin
High Priority
SOCPRIORITY
RRPOINTER
ADC_setSOCPriority(base, priMode);
  base is the ADC base address: ADCx_BASE (x = A to C)
  priMode values are:
    ADC_PRI_ALL_ROUND_ROBIN
    ADC_PRI_ALL_HIPRI
    ADC_PRI_SOCx_HIPRI (x = 0 to 14)

## Slide 12: Round Robin Priority Example
SOC
0
SOC
1
SOC
2
SOC
3
SOC
4
SOC
5
SOC
6
SOC
7
SOC
8
SOC
9
SOC
10
SOC
11
SOC
12
SOC
13
SOC
14
SOC
15
RRPOINTER
SOC7 trigger received
SOC7 is converted; RRPOINTER now points to SOC7; SOC8 is now highest RR priority
SOC2 & SOC12 triggers received simultaneously
SOC12 is converted; RRPOINTER points to SOC12; SOC13 is now highest RR priority
SOC2 is converted; RRPOINTER points to SOC2; SOC3 is now highest RR priority
SOCPRIORITY configured as 0; RRPOINTER configured as 15; SOC0 is highest RR priority

## Slide 13: High Priority Example
SOC
4
SOC
5
SOC
0
SOC
6
SOC
7
SOC
8
SOC
9
SOC
10
SOC
11
SOC
12
SOC
13
SOC
14
SOC
15
RRPOINTER
SOC
1
SOC
2
SOC
3
High Priority
SOC7 trigger received
SOC7 is converted; RRPOINTER points to SOC7; SOC8 is now highest RR priority
SOC2 is converted; RRPOINTER stays pointing to SOC7
SOC12 is converted; RRPOINTER points to SOC12; SOC13 is now highest RR priority
SOCPRIORITY configured as 4; RRPOINTER configured as 15; SOC4 is highest RR priority
SOC2 & SOC12 triggers received simultaneously

## Slide 14: Round Robin Burst Mode Diagram
Burst Enable
Disables/enables burst mode
BURSTEN
BURSTSIZE
BURSTTRIGSEL
SOC Burst Size
Determines how many SOCs are converted per burst trigger
SOC Burst Trigger Source Select
Determines which trigger starts a burst conversion sequence
Software, CPU1 Timer0-2
ePWM1 ADCSOCA/C – B/D  ePWM8 ADCSOCA/C – B/D
ADC_[enable|disable]BurstMode(base);
ADC_setBurstModeConfig(base, trigger, burstSize);
  base is the ADC base address: ADCx_BASE (x = A to C)
  trigger parameter uses the same values as the ADC_setupSOC() API
  burstSize parameter is a value between 1 and 16 inclusive

## Slide 15: Round Robin Burst Mode with High Priority Example
SOC
4
SOC
5
SOC
0
SOC
6
SOC
7
SOC
8
SOC
9
SOC
10
SOC
11
SOC
12
SOC
13
SOC
14
SOC
15
RRPOINTER
SOC
1
SOC
2
SOC
3
High Priority
BURSTTRIG trigger received
SOC4 & SOC5 is converted; RRPOINTER points to SOC5; SOC6 is now highest RR priority
SOC1 is converted; RRPOINTER stays pointing to SOC5
SOC6 & SOC7 is converted; RRPOINTER points to SOC7; SOC8 is now highest RR priority
SOCPRIORITY configured as 4; RRPOINTER configured as 15; SOC4 is highest RR priority
BURSTTRIG & SOC1 triggers received simultaneously
Note: BURSTEN = 1, BURSTSIZE = 1

## Slide 16: Purpose of the Post Processing Block
Offset Correction
  Remove an offset associated with an ADCIN channel possibly caused by external sensors and signal sources
    Zero-overhead; saving cycles
Error from Set-point Calculation
  Subtract out a reference value which can be used to automatically calculate an error from a set-point or expected value
    Reduces the sample to output latency and software overhead
Limit and Zero-Crossing Detection
  Automatically perform a check against a high/low limit or zero-crossing and can generate a trip to the ePWM and/or an interrupt
    Decreases the sample to ePWM latency and reduces software overhead; trip the ePWM based on an out of range ADC conversion without CPU intervention
Trigger-to-Sample Delay Capture
  Capable of recording the delay between when the SOC is triggered and when it begins to be sampled
    Allows software techniques to reduce the delay error

## Slide 17: Post Processing Block - Diagram

## Slide 18: Post Processing Block Interrupt Event
Each ADC module contains four Post Processing Blocks
Each Post Processing Block can be associated with any of the 16 ADCRESULTx registers

## Slide 19: ADC Clocking Flow
XTAL
(20 MHz)
ADCCLK (50 MHz)
To ADC core
sampling window
ACQPS
(7+1)
SYSCLKDIV
(/2)
To CPU
sampling window = (ACQPS + 1)*(1/SYSCLK)
IMULT/FMULT
(x10.00)
PRESCALE
(/2)
ADC_setPrescaler(ADCA_BASE, ADC_CLK_DIV_2_0);
ADC_setupSOC(…, …, …, …, 8);
SysCtl_enablePeripheral(SYSCTL_PERIPH_CLK_ADCA);
SysCtl_setClock(SYSCTL_OSCSRC_XTAL | SYSCTL_IMULT(10) | SYSCTL_FMULT_NONE | SYSCTL_SYSDIV(2) | SYSCTL_PLL_ENABLE );
PLLCLK
(200 MHz)
SYSCLK
(100 MHz)

## Slide 20: ADC Timing
SYSCLK = 100 MHz (10 ns period)
ADCCLK = 50 MHz (20 ns period)
Maximum Sample Rate: 3.45 MSPS – see data sheet for details
Sample + Hold (sampling window) time = 80 ns
Conversion time = 210 ns
Sampling rate = 80 ns + 210 ns = 290 ns  3.45 MSPS
  Above timing using ADCINTCYCLE = 0 (default)
SYSCLK
ADCCLK
8 cycles
Sample
10.5 ADCCLK cycles = 21 SYSCLK cycles
Convert
2 cycles
Write
2 cycles
Latch
Generate Early
Interrupt
Generate Late
Interrupt
ADCINTCYCLE

## Slide 21: ADC Conversion Result Registers
Selectable internal reference of 2.5 V or 3.3 V
Ratiometric external reference set by VREFHI/VREFLO
LSB
MSB
15 14 13 12 11 10 9 8 7 6 5 4 3 2 1 0
ADC_readResult(resultBase, socNumber);
ADCINx Voltage | Digital Results | AdcnResultRegs. ADCRESULTx
3.3 V | 0xFFF | 0000¦1111¦1111¦1111
1.65 V | 0x7FF | 0000¦0111¦1111¦1111
0.00081 V | 0x1 | 0000¦0000¦0000¦0001
0 V | 0x0 | 0000¦0000¦0000¦0000
    resultBase value is: ADCxRESULT_BASE (x = A to C)
    socNumber is: ADC_SOC_NUMBERx (x = 0 to 15)
Note: above table based on internal reference of 3.3 V; for external reference VREFHI is VDDA maximum, however VREFHI is typically selected as 2.5 V or 3.0 V

## Slide 22: How Can We Handle Signed Input Voltages?
Example: -1.65 V  Vin  +1.65 V
1) Add 1.65 volts to the analog input
Vin
1.65V
ADCIN0
GND
VREFLO
-
+
R
R
R
-
+
R
R
ADCA
#include “Lab.h”
#define offset 0x07FF
void main(void)
{
int16 value; // signed
value = ADC_readResult(resultBase, socNumber) – offset;
}
2) Subtract “1.65” from the digital result

## Slide 23: Built-In ADC Calibration
TI reserved OTP contains device specific calibration data for the ADC, internal oscillators and buffered DAC
The Boot ROM contains a Device_cal() routine that copies the calibration data to their respective registers
Device_cal() must be run to meet the specifications in the datasheet
  The Bootloader automatically calls Device_cal() such that no action is normally required by the user
  If the Bootloader is bypassed (e.g. during development) Device_cal() should be called by the application:
#define Device_cal (void (*)(void))0x70280
void main(void)
{
(*Device_cal)(); // call Device_cal()
}

## Slide 24: Analog Subsystem External Reference
Voltage
Reference
REF3230
REF3225
REF3030
REF3025
(or similar)
ADC
VREFHIA
VREFLOA
VREFHIB
VREFLOB
VREFHIC
VREFLOC
CA
CB
CC
Reference Generation
Non-Inverting Buffers

## Slide 25: Comparator Subsystem
Each CMPSS consists of:
  Two analog comparators
  Two programmable reference 12-bit DACs
  Two digital filters and one ramp generator
Each comparator generates a digital output
  Indicates if voltage on positive input is greater than the voltage on the negative input
  Positive input can be driven from an external pin or PGA
  Negative input can be driven by an external pin or 12-bit DAC
Each comparator output can be digitally filtered to remove spurious trip signals (majority vote)
Ramp generator used for peak current mode control
Ability to synchronize with EPWMSYNCO event, SYSCLK, and a clear signal with EPWMBLANK
DAC reference voltage can be either VDDA or VDAC

## Slide 26: Comparator Subsystem Block Diagram
DACxVALA * DACREF
4096
VDACx =
DAC Reference
Comparator Truth Table
Voltages Output
Voltage A < Voltage B 0
Voltage A > Voltage B 1
+
-
A
B
Output

## Slide 27: Programmable Gain Amplifier (PGA)
Amplifies small input signals to increase the dynamic range of the downstream ADC and CMPSS modules
Reduces cost and design effort over external standalone amplifiers
  On-chip integration ensures compatible with ADC and CMPSS
  Internally powered by VDDA and VSSA
Adaptable to various performance needs
  Software selectable gain and filter settings
    Four programmable gain modes: 3x, 6x, 12x, 24x
    Embedded series resistors for RC filtering
Hardware-based offset and gain trimming reduces offset and gain errors
  Instead of software post-processing

## Slide 28: PGA Block Diagram
Support for low-pass filtering by connecting an external capacitor to PGA_OF pin:
  cut-off frequency based on standard RC equation
PGA_OUT is an internal signal available for sampling and monitoring by the internal ADC and CMPSS modules
Filtered and non-filtered paths to ADC and CMPSS
PGA Output Filter pin can be used as a regular ADC/CMPSS pin
PGA Input can be used as a regular ADC/CMPSS pin
To ADC and CMPSS
Four Programmable Gain Modes:
3x, 6x, 12x, 24x

## Slide 29: Digital-to-Analog Converter
12-bit DAC provides a programmable reference output voltage
Analog output buffer is capable of driving an external load
Selectable reference voltage
Can be used as a general-purpose DAC for generating a DC voltage and AC waveforms (e.g. sine, square, triangle, etc.)
Ability to be synchronized with EPWMSYNCPER events

## Slide 30: Buffered DAC Block Diagram
DACVALA * DACREF
4096
DACOUT =
Ideal Output
DAC internal reference: 2.5 V and 3.3 V option
  3.3 V option outputs 1.65 V and then use 2x mode on DAC
  2.5 V option outputs 2.5 V and then use 1x mode on DAC
DAC_setReferenceVoltage(base, source);
0
1
AMP
(x1 or x2)
12-bit
DAC
DAC
VALS
VSSA
VDDA
DACOUT
DAC
VALA
VSSA
Internal
Reference
Circuit
0
1
1.65 V
2.5 V
VDAC
1
0
0
1
6
7
EPWM1SYNCPER
EPWM2SYNCPER
EPWM7SYNCPER
EPWM8SYNCPER
0
1
D Q
D Q
SYSCLK
VREFHI
DACREF
DAC_[enable|disable]Output(base);
DAC_setGainMode(base, mode);
DAC_setLoadMode(base, mode);
DAC_setShadowValue(base, value);
DAC_setPWMSyncSignal(base, signal);

## Slide 31: DAC Driverlib Functions
Set the DAC reference voltage
DAC_setReferenceVoltage(base, source);
Set the DAC gain mode
DAC_setGainMode(base, mode);
Set the DAC load mode
DAC_setLoadMode(base, mode);
Set DAC shadow value
DAC_setShadowValue(base, value);
Enable / disable DAC output
DAC_[enable|disable]Output(base);
Set DAC PWMSYNC signal
DAC_setPWMSyncSignal(base, signal);
  base is the ADC base address: DACx_BASE (x = A or B)
    source value is: DAC_REF_VDAC or DAC_REF_ADC_VREFHI
    mode (gain) value is: DAC_GAIN_ONE or DAC_GAIN_TWO
    mode (load) value is: DAC_LOAD_SYSCLK or DAC_LOAD_PWMSYNC
    value is the 12-bit code to be loaded into the active value register
    signal is the selected PWM signal (e.g. 2 selects PWM sync signal 2)

## Slide 32: Analog Subsystem Interconnect
Analog functions for:
  PGA inputs and outputs
  ADC inputs
  CMPSS inputs
are grouped into functional units by PGAs
Pins shared for:
  PGA functions
  ADC inputs
  DAC outputs
  CMPSS inputs
  AIO’s
Note: AIO input functionality only (name used to match legacy devices)

## Slide 33: Generic Analog Group Structure
Determines routing of the analog pins interconnect
Analog Group x

## Slide 34: Analog Group Connections Gx_ADCAB & GxADCC
General-purpose ADC input that connects to:
  Gx_ADCA or Gx_ADCB
  Gx_ADCC
Connects to positive comparator input multiplexers
  Gx_ADCAB at position ‘3’
  Gx_ADCC at position ‘1’
Connects to negative comparator input multiplexers
  Gx_ADCAB at position ‘0’
  Gx_ADCC at position ‘1’
Connects to AIO
Used for lower pin-count packages
Gx_ADCC is combined with the PGA input to allow ADC, CMPSS, or AIO to be use if PGA is not used

## Slide 35: Analog Group Connections PGAx_IN & PGAx_OUT & PGA_OF
PGAx_IN
  Input to PGAx
  Connects to positive comparator input multiplexer at position ‘2’
PGAx_OUT
  Output to PGAx (to ADCs)
  Connects to positive comparator input multiplexer at position ‘4’
PGAx Filtered Output
  Connects to ADCs and positive comparator input multiplexer at position ‘0’ by passing PGA output through switch + resistor with an external capacitor on the PGAx_OF pin
  Connects to AIO
If switch is open, PGAx_OF pin can be used as general-purpose ADC input or AIO

## Slide 36: Analog Group Connections - Example
Determine the connections in Analog Group 1 for the 100 PZ package

## Slide 37: Analog Pins and Internal Connections

## Slide 38: Analog Group Connections - Example
AIO233
AIO224
AIO237
‘A3’ (10)
A3
A2, B6
C0
A11, B7
‘A2/B6/PGA1_OF’ (9)
‘C0’ (19)
‘PGA1_IN’ (18)
‘PGA1_GND’ (14)
Pin Name
Group Name
Pin #

## Slide 39: Lab 6: ADC Sampling
ADC-A
ADCINA0
RESULT0
...
data
memory
pointer rewind
CPU copies result
to buffer during
ADC ISR
ePWM2
ePWM2 triggering
ADC on period match using SOCA trigger every 20 µs (50 kHz)
GND
+3.3 V
(GPIO59)
Toggle
(GPIO25)
jumper
wire
View ADC buffer PWM samples
Code Composer
Studio
DAC-B
Sine
Table

## Slide 40: Lab 6: Code Flow Diagram
Start
General Initialization
PLL and clocks
Watchdog configure
GPIO setup
PIE initialization
ADC Initialization
convert channel A0 on
ePWM2 period match
send interrupt on EOC
to trigger ADC ISR
setup a results buffer
in memory
ePWM2 Initialization
clear counter
set period register
set to trigger ADC on
period match
set the clock prescaler
enable the timer
Main Loop
while(1)
{
}
ADC ISR
read the ADC result
write to result buffer
adjust the buffer pointer
toggle the GPIO pin
return from interrupt
ADC interrupt
return

## Slide 41
C2000 Technical Training
www.ti.com/c2000

## Slide 42: Analog Group Connection on F28003x Similar to F28004x’s except for no PGA See Sec 7.13 of F28003x datasheet

## Slide 43: See Sec 7.13 of F28003x datasheet

## Slide 44: See Sec 7.13 of F28003x datasheet

## Slide 45: Accuracy (refer to each datasheet)
F28003x INL/DNL are much better than dsPIC33CK/CH

## Slide 46: Open/Short Detection

## Slide 47: Input Model
Input impedance is as small as possible to have fastest S/H (ACQPS) .
If Comparators are enabled, Cp is little affected.
ADCINB3 is of larger Cp and not recommended for fast sampling.

## Slide 48: 16.13.1 (TRM) Ensuring Synchronous Operation (1/3)

## Slide 49: 16.13.1 (TRM) Ensuring Synchronous Operation (2/3)

## Slide 50: 16.13.1 (TRM) Ensuring Synchronous Operation (2/3)
BAD example because of asynchronous between ADC modules.

## Slide 51: DAC Ramp for High Comparator can Realize Peak Current Mode with Slope Compensation
See
TIDM-02000 for PSFB DC/DC
TIDM-DC-DC-BUCK for Buck DC/DC