## Slide 1: Control Peripherals
Module 7
C2000™ Microcontroller Workshop
Copyright © 2019 Texas Instruments. All rights reserved.

## Slide 2: Module Objectives
Pulse Width Modulation (PWM) review
Generate a PWM waveform with the Pulse Width Modulator Module (ePWM)
Use the Capture Module (eCAP) to measure the width of a waveform
Explain the function of Quadrature Encoder Pulse Module (eQEP)
Describe the purpose of the Sigma Delta Filter Module (SDFM)

## Slide 3: What is Pulse Width Modulation?
PWM is a scheme to represent a signal as a sequence of pulses
  fixed carrier frequency
  fixed pulse amplitude
  pulse width proportional to instantaneous signal amplitude
  PWM energy  original signal energy
t
Original Signal
T
t
PWM representation

## Slide 4: Why use PWM with Power Switching Devices?
Desired output currents or voltages are known
Power switching devices are transistors
  Difficult to control in proportional region
  Easy to control in saturated region
PWM is a digital signal  easy for MCU to output
PWM approx.
of desired signal
DC Supply
Desired
signal to
system
?
DC Supply
Unknown Gate Signal
Gate Signal Known with PWM
PWM

## Slide 5: ePWM Module Signals and Connections
ePWMx
ePWMx+1
EPWMxSYNCI
EPWMxSYNCO
PIE
CLA
EPWMxINT
EPWMxTZINT
ePWMx-1
EPWMxSOCB
EPWMxSOCA
ADC
ePWM
X-Bar
EMUSTOP – TZ6
CLOCKFAIL – TZ5
EQEPERR – TZ4
CPU
SYSCTRL
eQEP
EPWMxA
EPWMxB
GPIO
MUX
INPUT
X-Bar
Note: the order in which the ePWM modules are connected is determined by the device synchronization scheme

## Slide 6: ePWM Synchronization Scheme
ePWM1
ePWM2
ePWM3
ePWM4
ePWM5
ePWM6
ePWM7
ePWM8
eCAP4
eCAP5
EXTSYNCIN1
EXTSYNCIN2
EPWM1
SYNCOUT
EPWM4
SYNCOUT
EPWM7
SYNCOUT
ECAP1
SYNCOUT
ECAP4
SYNCOUT
EXT
SYNCOUT
EPWM4SYNCIN
EPWM7SYNCIN
ECAP1SYNCIN
ECAP4SYNCIN
ECAP6SYNCIN
SYNCOUT
eCAP1
eCAP2
eCAP3
eCAP6
eCAP7

## Slide 7: ePWM Block Diagram

## Slide 8: ePWM Time-Base Sub-Module

## Slide 9: Time-Base Count Modes
TBCTR
TBCTR
TBCTR
TBPRD
TBPRD
TBPRD
Count Up Mode
Count Down Mode
Count Up and Down Mode
Asymmetrical
Waveform
Asymmetrical
Waveform
Symmetrical
Waveform

## Slide 10: ePWM Phase Synchronization Example
SyncIn
SyncOut
CTR=zero
CTR=CMPB *
X
En
o
o
o
o
o
o
o
=120°
Phase

EPWM2A
EPWM2B
SyncIn
SyncOut
CTR=zero
CTR=CMPB *
X
En
o
o
o
o
o
o
o
=240°
Phase

EPWM3A
EPWM3B
SyncIn
SyncOut
CTR=zero
CTR=CMPB *
X
En
o
o
o
o
o
o
o
=0°
Phase

EPWM1A
EPWM1B
=120°
=120°
=240°
Ext. SyncIn
To eCAP1
SyncIn
* Extended selection for CMPC and CMPD available
EPWM_[enable|disable]PhaseShiftLoad(base);
EPWM_setPhaseShift(base, phaseCount);
EPWM_setSyncOutPulseMode(base, mode);

## Slide 11: Time-Base Functional Diagram
Shadow
Clock
Prescaler
16-Bit
Counter
Period
Register
TBCLK
TB Signals
EPWMCLK
EPWMSYNCI
EPWMSYNCO
TBCLK = EPWMCLK / (HSPCLKDIV * CLKDIV)
Clock Prescaler = HSPCLKDIV * CLKDIV
EPWM_setClockPrescaler(base, prescaler, highSpeedPrescaler);
EPWM_setTimeBaseCountMode(base, counterMode);
EPWM_setPeriodLoadMode(base, loadMode);
EPWM_setTimeBasePeriod(base, periodCount);

## Slide 12: Time-Base Driverlib Functions
Set Time-Base clock (HSPCLKDIV and CLKDIV)
EPWM_setClockPrescaler(base, prescaler, highSpeedPrescaler);
Set Time-Base count mode
EPWM_setTimeBaseCountMode(base, counterMode);
Set Time-Base period value and period load mode
EPWM_setTimeBasePeriod(base, periodCount);
EPWM_setPeriodLoadMode(base, loadMode);
Set EPWMSYNC out pulse event
EPWM_setSyncOutPulseMode(base, mode);
  base is the ePWM base address: EPWMx_BASE (x = 1 to 8)
    prescaler value is: EPWM_CLOCK_DIVIDER_x (x = 2^n where n is 0 to 7)
    highSpeedPrescaler value is: EPWM_HSCLOCK_DIVIDER_x (x = 1 or an even value between 2 and 14 inclusive)
    counterMode value is: EPWM_COUNTER_MODE_x (x = UP, DOWN, UP_DOWN, or STOP_FREEZE )
    periodCount can have a maximum value of 0xFFFF
    loadMode value is: EPWM_PERIOD_x (x = SHADOW_LOAD or DIRECT_LOAD)
    mode value is: EPWM_SYNC_OUT_PULSE_ON_x (x = SOFTWARE, COUNTER_ZERO, COUNTER_COMPARE_y (y = B, C, or D), or EPWM_SYNC_OUT_PULSE_DISABLED)

## Slide 13: ePWM Counter Compare Sub-Module

## Slide 14: Counter Compare Event Waveforms
TBCTR
TBCTR
TBCTR
TBPRD
TBPRD
TBPRD
Count Up Mode
Count Down Mode
Count Up and Down Mode
Asymmetrical
Waveform
Asymmetrical
Waveform
Symmetrical
Waveform
CMPA
CMPA
CMPA
CMPB
CMPB
CMPB





















= compare events are fed to the Action Qualifier Sub-Module



















CMPC and CMPD available for use as event triggers

## Slide 15: Counter Compare Functional Diagram
Shadow
Compare A
Counter Compare
Shadow
Compare B
Shadow
Compare C
Shadow
Compare D
TB Signals
Signals to
AQ & ET
EPWM_setCounterCompareValue(base, compModule, compCount);
EPWM_disableCounterCompareShadowLoadMode(base, compModule);
EPWM_setCounterCompareShadowLoadMode(base, compModule, loadMode);
Function applies to Compare A, B, C, and D
If shadow mode disabled
Functions apply to Shadow A, B, C, and D
Immediate mode – the shadow register is not used
Shadow mode – the compare register is double buffered

## Slide 16: Counter Compare Driverlib Functions
Set Counter Compare value
EPWM_setCounterCompareValue(base, compModule, compCount);
Enable and set Counter Compare shadow load mode
EPWM_setCounterCompareShadowLoadMode(base, compModule, loadMode);
Disable Counter Compare shadow load mode
EPWM_disableCounterCompareShadowLoadMode(base, compModule);
  base is the ePWM base address: EPWMx_BASE (x = 1 to 8)
    compModule value is: EPWM_COUNTER_COMPARE_x (x = A, B, C, or D)
    compCount can have a maximum value of 0xFFFF)
    loadMode value is:
        EPWM_COMP_LOAD_ON_CNTR_x (x = ZERO, PERIOD, or ZERO_PERIOD)
        EPWM_COMP_LOAD_FREEZE
        EPWM_COMP_LOAD_ON_SYNC_CNTR_x (x = ZERO, PERIOD, or ZERO_PERIOD)
        EPWM_COMP_LOAD_ON_SYNC_ONLY

## Slide 17: ePWM Action Qualifier Sub-Module

## Slide 18: ePWM Action Qualifier Actions for EPWMA and EPWMB
SW

SW

SW
X
SW
T
S/W
Force
Do Nothing
Clear Low
Set High
Toggle
EPWM
Output
Actions
Time-Base Counter equals:
Z

Z

Z
X
Z
T
Zero
CA

CA

CA
X
CA
T
CMPA
CB

CB

CB
X
CB
T
CMPB
P

P

P
X
P
T
TBPRD
T1

T1

T1
X
T1
T
T1
T2

T2

T2
X
T2
T
T2
Trigger Events:
Tx Event Sources = DCAEVT1, DCAEVT2, DCBEVT1, DCBEVT2, TZ1, TZ2, TZ3, EPWMxSYNCIN

## Slide 19: Count Up Asymmetric Waveform with Independent Modulation on EPWMA / B
Z

P
X
CB
X
CA

Z

P
X
CB
X
CA

Z

P
X
Z

P
X
CB

CA
X
Z

P
X
CB

CA
X
Z

P
X
TBCTR
TBPRD




EPWMA
EPWMB





CMPA
CMPB
Notes: The next few figures show how the action qualifier uses the compare matches to modulate the output pins. Notice that the output pins for EPWMA and EPWMB are completely independent. Here, on the EPWMA output, the waveform will be set high on zero match and clear low on compare A match. On the EPWMB output, the waveform will be set high on zero match and clear low on compare B match.

## Slide 20: Count Up Asymmetric Waveform with Independent Modulation on EPWMA
CA

CB

CA

CB

Z
T
Z
T
Z
T
EPWMA
EPWMB
TBCTR
TBPRD






CMPB
CMPA



Notes: This figure has the EPWMA output set high on compare A match and clear low on compare B match, while the EPWMB output is configured to toggle on zero match.

## Slide 21: Count Up-Down Symmetric Waveform with Independent Modulation on EPWMA / B
CA

CA

CA

CA

CB

CB

CB

CB

EPWMA
EPWMB
TBCTR
TBPRD










CMPB
CMPA



Notes: Here you can see that we can have different output actions on the up-count and down-count using a single compare register. So, for the EPWMA and EPWMB outputs, we are setting high on the compare A and B up-count matches and clearing low on the compare A and B down-down matches.

## Slide 22: Count Up-Down Symmetric Waveform with Independent Modulation on EPWMA
CA

CB

CA

CB

Z

P

Z

P

EPWMA
EPWMB
TBCTR
TBPRD






CMPB
CMPA



Notes: And finally, again using different output actions on the up-count and down-count, we have the EPWMA output set high on the compare A up-count match and clear low on the compare B down-count match. The EPWMB output will clear low on zero match and set high on period match.

## Slide 23: Action Qualifier Driverlib Functions
Configure Action Qualifier output on ePWMA or ePWMB
EPWM_setActionQualifierAction(base, epwmOutput, output, event);
Set Action Qualifier trigger source for event T1 or T2
EPWM_setActionQualifierT1TriggerSource(base, trigger);
EPWM_setActionQualifierT2TriggerSource(base, trigger);
  base is the ePWM base address: EPWMx_BASE (x = 1 to 8)
    epwmOutput value is: EPWM_AQ_OUTPUT_x (x = A or B)
    output value is: EPWM_AQ_OUTPUT_x (x = NO_CHANGE, LOW, HIGH, or TOGGLE)
    event value is:
        EPWM_AQ_OUTPUT_ON_TIMEBASE_x (x = ZERO, PERIOD, UP_CMPA, DOWN_CMPA, UP_CMPB, or DOWN_CMPB)
        EPWM_AQ_OUTPUT_ON_T1_x (x = COUNT_UP or COUNT_DOWN)
        EPWM_AQ_OUTPUT_ON_T2_x (x = COUNT_UP or COUNT_DOWN)
    trigger value is: EPWM_AQ_TRIGGER_EVENT_TRIG_x (x = DCA_1, DCA_2, DCB_1, DCB_2, TZ_1, TZ_2, TZ_3, or EPWM_SYNCIN)

## Slide 24: Action Qualifier Driverlib Functions
Enable and set Action Qualifier shadow load mode
EPWM_setActionQualifierShadowLoadMode(base, aqModule, loadMode);
Disable Action Qualifier shadow load mode
EPWM_disableActionQualifierShadowLoadMode(base, aqModule);
  base is the ePWM base address: EPWMx_BASE (x = 1 to 8)
    aqModule value is: EPWM_ACTION_QUALIFIER_x (x = A or B)
    loadMode value is:
        EPWM_AQ_LOAD_ON_CNTR_x (x = ZERO, PERIOD, or ZERO_PERIOD)
        EPWM_AQ_LOAD_FREEZE
        EPWM_AQ_LOAD_ON_SYNC_CNTR_x (x = ZERO, PERIOD, or ZERO_PERIOD)
        EPWM_AQ_LOAD_ON_SYNC_ONLY

## Slide 25: Action Qualifier Driverlib Functions
Trigger continuous software forced output on ePWM (A or B) EPWM_setActionQualifierContSWForceAction(base, epwmOutput, output);
Set continuous software force shadow reload mode EPWM_setActionQualifierContSWForceShadowMode(base, mode);
Set one time software forced action output and force action
EPWM_setActionQualifierSWAction(base, epwmOutput, output*);
EPWM_forceActionQualifierSWAction(base, epwmOutput);
  base is the ePWM base address: EPWMx_BASE (x = 1 to 8)
    epwmOutput value is: EPWM_AQ_OUTPUT_x (x = A or B)
    output value is: EPWM_AQ_x (x = SW_DISABLED, OUTPUT_LOW, or OUTPUT_HIGH)
    mode value is:
        EPWM_AQ_SW_SH_LOAD_ON_x (x = CNTR_ZERO, CNTR_PERIOD, or CNTR_ZERO_PERIOD)
        EPWM_AQ_SW_IMMEDIATE_LOAD
    output* value is: EPWM_AQ_OUTPUT_x (x = NO_CHANGE, LOW, HIGH, or TOGGLE)

## Slide 26: Symmetric PWM Computation Example
Determine TBPRD and CMPA for 100 kHz, 25% duty symmetric PWM from a 100 MHz time base clock
CMPA = (100% - duty cycle)*TBPRD = 0.75*500 = 375
TBPRD =
fTBCLK
fPWM
2
2
1
1
100 kHz
100 MHz
.
.
= 500
=
Counter
Compare
Period
PWM Pin
fTBCLK = 100 MHz
CA

CA



fPWM = 100 kHz
(TPWM = 10 s)
(TTBCLK = 10 ns)

## Slide 27: Asymmetric PWM Computation Example
Determine TBPRD and CMPA for 100 kHz, 25% duty asymmetric PWM from a 100 MHz time base clock
CMPA = (100% - duty cycle)*(TBPRD+1) - 1 = 0.75*(999+1) - 1 = 749
TBPRD =
fTBCLK
fPWM
100 kHz
100 MHz
- 1 = 999
- 1 =
Counter
Compare
Period
PWM Pin
P

CA

fTBCLK = 100 MHz


fPWM = 100 kHz
(TPWM = 10 s)
(TTBCLK = 10 ns)

## Slide 28: ePWM Dead-Band Sub-Module

## Slide 29: Motivation for Dead-Band
Transistor gates turn on faster than they shut off
Short circuit if both gates are on at the same time!
to power switching device
supply rail
gate signals are
complementary PWM
Original EPWM
Rising Edge Delay
Falling Edge Delay
RED
FED
Dead
Band
Shadow
EPWMxA
EPWMxB
EPWMxA
EPWMxB

## Slide 30: Dead-Band Block Diagram
Rising Edge Delay
In Out
(14-bit counter)
Falling Edge Delay
In Out
(14-bit counter)



0
1



0
1



0
1



1
0






PWMxA
PWMxB
PWMxB
PWMxA
S1
S0
S2
S3
FED
RED
OUT_MODE
POLSEL



0
1



0
1
S4
S5
IN_MODE
HALFCYCLE



0
1



0
1
S6
S7
OUTSWAP




1
0
S8



0
1
S8
DEDB_
MODE


See the F28004x Driver Library User’s Guide for available functions

## Slide 31: ePWM Chopper Sub-Module

## Slide 32: Purpose of the PWM Chopper
Allows a high frequency carrier signal to modulate the PWM waveform generated by the Action Qualifier and Dead-Band modules
Used with pulse transformer-based gate drivers to control power switching elements

## Slide 33: Chopper Waveform
EPWMxA
EPWMxB
CHPFREQ
EPWMxA
EPWMxB
OSHT
EPWMxA
Programmable
Pulse Width
(OSHTWTH)
Sustaining
Pulses
See the F28004x Driver Library User’s Guide for available functions
With One-Shot Pulse on EPWMxA and/or EPWMxB

## Slide 34: ePWM Trip-Zone and Digital Compare Sub-Modules

## Slide 35: Trip-Zone Features
Trip-Zone has a fast, clock independent logic path to high-impedance the EPWMxA/B output pins
Interrupt latency may not protect hardware when responding to over current conditions or short-circuits through ISR software
Supports: #1) one-shot trip for major short circuits or over current conditions
#2) cycle-by-cycle trip for current limiting operation
CPU
core
P
W
M
O
U
T
P
U
T
S
EPWMxTZINT
TZ6
TZ5
TZ4
INPUT X-Bar
ePWM X-Bar
Cycle-by-Cycle
Mode
One-Shot
Mode
EPWMxA
EPWMxB
Digital
Compare
CPU
SYSCTRL
eQEP1
EMUSTOP
CLOCKFAIL
EQEP1ERR
Over
Current
Sensors
TZ1 – TZ3
See ‘Trip-Zone Submodule Mode Control Logic’ figure in F28004x TRM for details

## Slide 36: Trip-Zone Sub-Module Control Logic

## Slide 37: Trip-Zone Driverlib Functions
Enable / disable Trip-Zone signals
EPWM_[enable|disable]TripZoneSignals(base, tzSignal);
Set Trip-Zone Action
EPWM_setTripZoneAction(base, tzEvent, tzAction);
Enable / disable Trip-Zone interrupts
EPWM_[enable|disable]TripZoneInterrupt(base, tzInterrupt);
  base is the ePWM base address: EPWMx_BASE (x = 1 to 8)
    tzSignal is logical OR values of:
        EPWM_TZ_SIGNAL_CBCx (x = 1 to 6)
        EPWM_TZ_SIGNAL_x (x = DCAEVT2 or DCBEVT2) <CBC>
        EPWM_TZ_SIGNAL_OSHTx (x = 1 to 6)
        EPWM_TZ_SIGNAL_x (x = DCAEVT1 or DCBEVT1) <OSHT>
    tzEvent value is: EPWM_TZ_ACTION_EVENT_x (x = TZA, TZB, DCAEVT1, DCAEVT2, DCBEVT1, or DCBEVT2)
    tzAction value is: EPWM_TZ_ACTION_x (x = HIGH_Z, HIGH, LOW, or DISABLE)
    tzInterrupt is logical OR values of: EPWM_TZ_INTERRUPT_x (x = CBC, OST, DCAEVT1, DCAEVT2, DCBEVT1, or DCBEVT2)

## Slide 38: Digital Compare Trip Inputs
GPIO
MUX
INPUT
X-BAR
ePWM
X-BAR
Digital
Compare
Sub-
Module
TRIPIN1 & TZ1
TRIPIN2 & TZ2
TRIPIN3 & TZ3
TRIPIN6
TRIPIN4
TRIPIN5
TRIPIN7
TRIPIN8
TRIPIN9
TRIPIN10
TRIPIN11
TRIPIN12
TRIPIN1 & TZ1
TRIPIN2 & TZ2
TRIPIN3 & TZ3
TRIPIN6
TRIPIN4
TRIPIN5
TRIPIN7
TRIPIN8
TRIPIN9
TRIPIN10
TRIPIN11
TRIPIN12
TRIP COMBO
TRIPIN14 (ECCDBLERR)
TRIPIN15 (PIEERR)
TRIPIN15
TRIPIN14

## Slide 39: ePWM X-BAR

## Slide 40: ePWM X-Bar Architecture
MUX | 0 | 1 | 2 | 3
16 | SD1FLT1.COMPH | SD1FLT1.COMPH_OR_COMPL |  | 
17 | SD1FLT1.COMPL | INPUT7 |  | CLAHALT
18 | SD1FLT2.COMPH | SD1FLT2.COMPH_OR_COMPL |  | 
19 | SD1FLT2.COMPL | INPUT8 |  | 
20 | SD1FLT3.COMPH | SD1FLT3.COMPH_OR_COMPL |  | 
21 | SD1FLT3.COMPL | INPUT9 |  | 
22 | SD1FLT4.COMPH | SD1FLT4.COMPH_OR_COMPL |  | 
23 | SD1FLT4.COMPL | INPUT10 |  | 
24 |  |  |  | 
25 |  | INPUT11 |  | 
26 |  |  |  | 
27 |  | INPUT12 |  | 
28 |  |  |  | 
29 |  | INPUT13 |  | 
30 |  |  |  | 
31 |  | INPUT14 |  | 
MUX | 0 | 1 | 2 | 3
0 | CMPSS1.CTRIPH | CMPSS1.CTRIPH_OR_CTRIPL | ADCAEVT1 | ECAP1OUT
1 | CMPSS1.CTRIPL | INPUTXBAR1 |  | ADCCEVT1
2 | CMPSS2.CTRIPH | CMPSS2.CTRIPH_OR_CTRIPL | ADCAEVT2 | ECAP2OUT
3 | CMPSS2.CTRIPL | INPUTXBAR2 |  | ADCCEVT2
4 | CMPSS3.CTRIPH | CMPSS3.CTRIPH_OR_CTRIPL | ADCAEVT3 | ECAP3OUT
5 | CMPSS3.CTRIPL | INPUTXBAR3 |  | ADCCEVT3
6 | CMPSS4.CTRIPH | CMPSS4.CTRIPH_OR_CTRIPL | ADCAEVT4 | ECAP4OUT
7 | CMPSS4.CTRIPL | INPUTXBAR4 |  | ADCCEVT4
8 | CMPSS5.CTRIPH | CMPSS5.CTRIPH_OR_CTRIPL | ADCBEVT1 | ECAP5OUT
9 | CMPSS5.CTRIPL | INPUTXBAR5 |  | 
10 | CMPSS6.CTRIPH | CMPSS6.CTRIPH_OR_CTRIPL | ADCBEVT2 | ECAP6OUT
11 | CMPSS6.CTRIPL | INPUTXBAR6 |  | 
12 | CMPSS7.CTRIPH | CMPSS7.CTRIPH_OR_CTRIPL | ADCBEVT3 | ECAP7OUT
13 | CMPSS7.CTRIPL | ADCSOCA |  | 
14 |  |  | ADCBEVT4 | EXTSYNCOUT
15 |  | ADCSOCB |  | 
0
0.0
0.1
0.2
0.3
1
1.0
1.1
1.2
1.3
31
31.0
31.1
31.2
31.3
TRIPINx
XBAR_setEPWMMuxConfig(trip, muxConfig);
XBAR_invertEPWMSignal(trip, invert);
This block diagram is replicated 8 times
XBAR_enableEPWMMux(trip, muxes);
XBAR_disableEPWMMux(trip, muxes);

## Slide 41: Purpose of the Digital Compare Sub-Module
Generates ‘compare’ events that can:
  Trip the ePWM
  Generate a Trip interrupt
  Sync the ePWM
  Generate an ADC start of conversion
Digital compare module inputs are:
  Input X-Bar
  ePWM X-Bar
  Trip-zone input pins
A compare event is generated when one or more of its selected inputs are either high or low
Optional ‘Blanking’ can be used to temporarily disable the compare action in alignment with PWM switching to eliminate noise effects

## Slide 42: Digital Compare Sub-Module Signals
Digital Trip
Event A1
Compare
Digital Trip
Event A2
Compare
Digital Trip
Event B1
Compare
Digital Trip
Event B2
Compare
Generate PWM Sync
Time-Base Sub-Module
Generate SOCA
Event-Trigger Sub-Module
Trip PWMA Output
Generate Trip Interrupt
Trip-Zone Sub-Module
Generate PWM Sync
Time-Base Sub-Module
Generate SOCB
Event-Trigger Sub-Module
Trip PWMB Output
Generate Trip Interrupt
Trip-Zone Sub-Module
DCAH
DCAL
DCBH
DCBL
DCAEVT1
DCAEVT2
DCBEVT1
DCBEVT2
blanking
blanking
TRIPIN1 & TZ1
TRIPIN2 & TZ2
TRIPIN3 & TZ3
TRIPIN4
TRIPIN12
TRIPIN15
TRIPIN14
TRIP COMBO
●
●
●
EPWM_selectDigitalCompareTripInput(base, tripSource, dcType);
EPWM_[enable|disable]DigitalCompareTripCombinationInput(base, tripInput, dcType);
EPWM_setTripZoneDigitalCompareEventCondition(base, dcType*, dcEvent);

## Slide 43: Digital Compare Events
The user selects the input for each of DCAH, DCAL, DCBH, DCBL
Each A and B compare uses its corresponding DCyH/L inputs (y = A or B)
The user selects the signal state that triggers each compare from the following choices:
DCyH  low DCyL  don’t care
DCyH  high DCyL  don’t care
iii. DCyL  low DCyH  don’t care
iv. DCyL  high DCyH  don’t care
v. DCyL  high DCyH  low
EPWM_setTripZoneDigitalCompareEventCondition(base, dcType, dcEvent);

## Slide 44: Digital Compare Driverlib Functions
Select Digital Compare trip inputs
EPWM_selectDigitalCompareTripInput(base, tripSource, dcType);
Enable / disable Digital Compare trip combination inputs
EPWM_[enable|disable]DigitalCompareTripCombinationInput( base, tripInput, dcType);
Set Digital Compare conditions which cause Trip-Zone events
EPWM_setTripZoneDigitalCompareEventCondition(base, dcType*, dcEvent);
  base is the ePWM base address: EPWMx_BASE (x = 1 to 8)
    tripSource value is:
        EPWM_DC_TRIP_TRIPINx (x = 1 to 12, 14, 15)
        EPWM_DC_TRIP_COMBINATION - selects trip signals enabled by the
        EPWM_enableDigitalCompareTripCombinationInput() function
    dcType value is: EPWM_DC_TYPE_x (x = DCAH, DCAL, DCBH , or DCBL)
    tripInput value is: EPWM_DC_COMBINATIONAL_TRIPINx (x = 1 to 12, 14, 15)
    dcType* value is: EPWM_TZ_DC_OUTPUT_x (x = A1, A2, B1, or B2)
    dcEvent value is: EPWM_TZ_EVENT_x (x = DC_DISABLED, DCyH_LOW, DCyH_HIGH, DCyL_LOW, DCyL_HIGH, or DCyL_HIGH_DCyH_LOW)  where y in DCyH/DCyL represents DCAH/DCAL or DCBH/DCBL

## Slide 45: Digital Compare Driverlib Functions
Enable / disable Digital Compare Sync Event
EPWM_[enable|disable]DigitalCompareSyncEvent(base, dcModule);
Enable / disable Digital Compare ADC trigger
EPWM_[enable|disable]DigitalCompareADCTrigger(base, dcModule);
Enable / disable Trip-Zone signals and Trip-Zone interrupts
  See Trip-Zone Driverlib Functions:
EPWM_[enable|disable]TripZoneSignals(base, tzSignal);
EPWM_[enable|disable]TripZoneInterrupt(base, tzInterrupt);
  base is the ePWM base address: EPWMx_BASE (x = 1 to 8)
    dcModule value is: EPWM_DC_MODULE_x (x = A or B)
Generate PWM Sync
Time-Base Sub-Module
Generate SOCx
Event-Trigger Sub-Module
Trip PWMx Output
Generate Trip Interrupt
Trip-Zone Sub-Module
DCxEVT1
DCxEVT2
(x = A or B)

## Slide 46: ePWM Event-Trigger Sub-Module

## Slide 47: Event-Trigger Interrupts and SOC
TBCTR
TBPRD
CMPD
CMPA
CTR = 0
CTR = PRD
CTRU = CMPA
CTRD = CMPA
CTRU = CMPB
CTRD = CMPB
CTR = 0 or PRD
CMPC
CMPB
CTRU = CMPC
CTRD = CMPC
CTRU = CMPD
CTRD = CMPD





















DCAEVT1.soc / DCBEVT1.soc generates EPWMxSOCA/B pulse (x = 1 to 8)

## Slide 48: Event-Trigger Driverlib Functions
Enable / disable Event-Trigger ADC SOC
EPWM_[enable|disable]ADCTrigger(base, adcSOCType);
Set Event-Trigger ADC SOC source
EPWM_setADCTriggerSource(base, adcSOCType, socSource);
Set Event-Trigger ADC SOC prescale
EPWM_setADCTriggerEventPrescale(base, adcSOCType, preScaleCount);
  base is the ePWM base address: EPWMx_BASE (x = 1 to 8)
    adcSOCType value is: EPWM_SOC_x (x = A or B)
    socSource value is:
        EPWM_SOC_DCxEVT1 (x = A or B)
        EPWM_SOC_TBCTR_x (x = ZERO, PERIOD, ZERO_OR_PERIOD)
        EPWM_SOC_TBCTR_U_CMPx (x = A, B, C, or D)
        EPWM_SOC_TBCTR_D_CMPx (x = A, B, C, or D)
    preScaleCount value is: 1 to 15 (0 disables the prescale)

## Slide 49: Event-Trigger Driverlib Functions
Enable / disable Event-Trigger interrupt
EPWM_[enable|disable]Interrupt(base);
Set Event-Trigger interrupt source
EPWM_setInterruptSource(base, interruptSource);
Set Event-Trigger interrupt event counts
EPWM_setInterruptEventCount(base, eventCount);
  base is the ePWM base address: EPWMx_BASE (x = 1 to 8)
    interruptSource value is:
        EPWM_INT_TBCTR_x (x = ZERO, PERIOD, ZERO_OR_PERIOD)
        EPWM_INT_TBCTR_U_CMPx (x = A, B, C, or D)
        EPWM_INT_TBCTR_D_CMPx (x = A, B, C, or D)
    eventCount maximum value is: 15 (Determines the number of events that have to occur before an interrupt is issued)

## Slide 50: High-Resolution PWM (HRPWM)
Significantly increases the resolution of conventionally derived digital PWM
Uses 8-bit extensions to Compare registers (CMPxHR), Period register (TBPRDHR) and Phase register (TBPHSHR) for edge positioning control
Typically used when PWM resolution falls below ~9-10 bits which occurs at frequencies greater than ~200 kHz (with system clock of 100 MHz)
Not all ePWM outputs support HRPWM feature (see device datasheet)
PWM Period
Device Clock
(i.e. 100 MHz)
Regular PWM Step
(i.e. 10 ns)
HRPWM
Micro Step (~150 ps)
HRPWM divides a clock cycle into smaller steps
called Micro Steps
(Step Size ~= 150 ps)
ms
ms
ms
ms
ms
ms
Calibration Logic
Calibration Logic tracks the number of Micro Steps per clock to account for variations caused by Temp/Volt/Process

## Slide 51: HRPWM block diagram

## Slide 52: HRPWM Registers

## Slide 53: Limitations – Minimum duty (1/2)
Minimum 3 PWM cycles for HR duty if HRPCTL[HRPE]=0
Minimum 6 PWM cycles for HR duty if HRPCTL[HRPE]= 1
Minimum 7 PWM cycles for HR Deadband (DBREDHR or DBFEDHR)

## Slide 54: Limitations – Minimum duty (2/2)

## Slide 55: Limitations – HR Period and Sync
When high-resolution period mode is enabled, an EPWMxSYNC pulse will introduce +/- 1 - 2 cycle jitter to the PWM
When EPWMxSYNCI is EPWMxSYNCO source, a software synchronization pulse should be issued only once during high-resolution period initialization.
Refer to TIDM-02002 CLLLC, which uses HR period at PWM resonant 500 KHz.

## Slide 56: Advanced Features on Type-4 PWM
PWM (Type-4) Features | C2000 devices Gen 3 | System benefit
High-Resolution on PWM output capability (on period, enables frequency modulated PWM strategies, dead-band capabilities) | Y | Enables better performance high-frequency power conversion. Achieve cleaner waveforms and avoid oscillations/limit cycle at output.
CMPC & CMPD (enables generation ADC SOC and INT anywhere in PWM period) | Y | Trigger ADC conversion at any point. Enables highly accurate oversampling.
Load on SYNC (support for shadow-to-active load on a SYNC event) | Y | Enables variable frequency applications (allows LLC control in power conversion).
Simultaneous register writes across multiple PWM modules | Y | Enables complex, high frequency power control (interleaved, LLC topologies). Especially applicable in time-critical applications
Action qualifier registers (shadowing of AQCTLA and AQCTLB registers) | Y | Cleanly disable and re-enable 1 PWM phase. Needed to implement Peak Current Mode Control (PCMC)
Delayed trip functionality (dead-band insertion capability on a trip event) | Y | Enables Zero Voltage Switching (ZVS) which leads to higher efficiencies. Achieve PSFB, PCMC, transition mode PFC topologies/implementations
Global load (from shadow to active registers) | Y | Enables control of interleaved LLC topologies at high frequencies
Valley switching (ability to switch PWM output at valley point) | Y | Enables improvement in Power Factor (PF) and Total Harmonic Distortion (THD), especially relevant in PFC applications. Enables light load efficiency.

## Slide 57: Delayed trip
Useful for peak current mode for buck, boost, phase-shift full bridge

## Slide 58: Peak Current Mode Control – Sync Buck
Peak current mode control of a synchronous DC-DC buck converter.

## Slide 59
Peak Current Mode Control – PSFB
Peak current mode control of a Phase Shifted Full-Bridge (PSFB) DC-DC converter.

## Slide 60: ePWM Action Qualifier Actions for EPWMA and EPWMB
SW

SW

SW
X
SW
T
S/W
Force
Do Nothing
Clear Low
Set High
Toggle
EPWM
Output
Actions
Time-Base Counter equals:
Z

Z

Z
X
Z
T
Zero
CA

CA

CA
X
CA
T
CMPA
CB

CB

CB
X
CB
T
CMPB
P

P

P
X
P
T
TBPRD
T1

T1

T1
X
T1
T
T1
T2

T2

T2
X
T2
T
T2
Trigger Events:
Tx Event Sources = DCAEVT1, DCAEVT2, DCBEVT1, DCBEVT2, TZ1, TZ2, TZ3, EPWMxSYNCIN
Can be used from trip events

## Slide 61: Simultaneous Writes One Shot & Global Reload Capability
Useful for variable frequency topologies like LLC resonant

## Slide 62: Shadow to Active Load on SYNC (Variable Frequency Application)

## Slide 63: Simultaneous Writes to Shadow Registers Between Modules by EPWMXLINK (Variable Frequency Application)

## Slide 64
One Shot & Global Reload
For all registers that have this mode enabled, shadow to active loads occur at the same event defined by GLDCTL[GLDMODE]
Global reload pulse pre-scalar provides capability to choose transfers to happen once in ‘N’ occurrences of selected event
One shot reload usage
Initialization
  Enable global reload
  Link GLDCTL2 registers
Run Time
  Update all registers
  Write ‘1’ to GLDCTL2[OSHTLD]
  Write ‘1’ to GLDCTL2[GFRCLD], if desired

## Slide 65: Valley Switching
Useful for DCM like PFC light loads

## Slide 66: Need for Valley Switching - Flyback in DCM and CCM mode
CCM Mode of operation
DCM Mode of operation
DCM Mode is typically encountered at light load, where efficiency standards are hard to meet and any savings reflect a larger percentage and under high input line condition

## Slide 67: What is Valley Switching ?
Soft-switching technique that improves system efficiency
Switch should be turned ON at the valley point of the voltage across it
Results is slight variance of the frequency
Where is it used ?
AC/DC, DC/DC for Server, Telecom rectifiers, data storage and general digital power
Challenges ?
Resonant oscillations are dependent on circuit parasitics and typically in the MHz
Need for programmable number of valleys
Dependence on dedicated external circuit

## Slide 68: Valley Switching Enhancements
A hardware mechanism to precisely control PWM ON/OFF time instants to implement valley switching
Captures time period of oscillations to accurately delay PWM switching instant
Ability to add software programmable offset to captured delay
Programmable number of edges before the delay takes effect
Multiple choices of triggers and events
Allows easy adaptability for optimum performance under changing system/operating conditions

## Slide 69: Valley Switching Result on TIDM-1022 (Load < 10%, 750W)

## Slide 70: Backup

## Slide 71: Capture Module (eCAP)
The eCAP module timestamps transitions on a capture input pin
  Can be used to measure the time width of a pulse
Auxiliary PWM generation
Timer
Timestamp
Values
Trigger
pin
t1
t2

## Slide 72: eCAP Module Block Diagram – Capture Mode
Capture 1
Register
Capture 2
Register
Capture 3
Register
Capture 4
Register
Polarity
Select 1
Polarity
Select 2
Polarity
Select 3
Polarity
Select 4
Event Qualifier
Event
Prescale
[127:16]
[15:0]
Other
Sources
Input
X-BAR
32-Bit
Time-Stamp
Counter
Hi-Res
Capture
Delta Mode
Reset
Continuous / One-shot
Capture Control
PIE
(ECAPx)
DMA
Trigger
ECAP_enableCaptureMode(base);

## Slide 73: eCAP Module Block Diagram – APWM Mode
32-Bit
Time-Stamp
Counter
Period
Register
(CAP3)
Compare
Register
(CAP4)
Compare
Register
(CAP2)
PWM
Compare
Logic
Shadowed
Shadowed
immediate
mode
shadow
mode
shadow
mode
immediate
mode
Period
Register
(CAP1)
Output
X-BAR
ECAP_enableAPWMMode(base);

## Slide 74: eCAP Driverlib Function
Enable capture or APWM mode
ECAP_enableCaptureMode(base);
ECAP_enableAPWMMode(base);
Select eCAP input signal
ECAP_selectECAPInput(base, input);
Stop / start time stamp counter
ECAP_[stop|start]Counter(base);
  base is the eCAP base address: ECAPx_BASE (x = 1 to 7)
    input value is:
        ECAP_INPUT_INPUTXBARx (x = 1 to 16)
        ECAP_INPUT_CANx_INT0 (x = A or B)
        ECAP_INPUT_ECAP_DELAY_CLOCK
        ECAP_INPUT_OUTPUTXBARx (x = 1 to 8)
        ECAP_INPUT_ADC_y_EVENTx (x = 1 to 4) (y = A, B, or C)
        ECAP_INPUT_SDFM1_FLTx_COMPARE_y (x = 1 to 4) (y = LOW, HIGH, or HIGH_OR_LOW)
        ECAP_INPUT_CMPSSx_CTRIP_y (x = 1 to 7) (y = LOW, HIGH, or HIGH_OR_LOW)

## Slide 75: eCAP Driverlib Function
Enable / disable load of time stamp on capture event (CAP1 –CAP4)
ECAP_[enable|disable]TimeStampCapture(base);
Set capture mode (continuous/wrap or one-shot/stop mode)
ECAP_setCaptureMode(base, mode, event);
Sets the capture event polarity (rising or falling edge)
ECAP_setEventPolarity(base, event, polarity);
Enable / disable counter reset on event (delta / absolute time stamp)
ECAP_[enable|disable]CounterResetOnEvent(base, event);
Set and enable / disable capture event interrupt source
ECAP_[enable|disable]Interrupt(base, intFlags);
Set eCAP input event filter prescale counter
ECAP_setEventPrescaler(base, preScalerValue);
  base is the eCAP base address: ECAPx_BASE (x = 1 to 7)
    mode value is: ECAP_CONTINUOUS_CAPTURE_MODE or ECAP_ONE_SHOT_CAPTURE_MODE
    event value is: ECAP_EVENT_x (x = 1 to 4)
    polarity value is: ECAP_EVNT_RISING_EDGE or ECAP_EVNT_FALLING_EDGE
    intFlags value is: ECAP_ISR_SOURCE_CAPTURE_x (x = EVENT_1, EVENT_2, EVENT_3, EVENT_4, OVERFLOW, PERIOD, COMPARE)
    preScalerValue value is: 1, 2, …31 (divide is 2x - i.e. 5 is /10; 1 = no prescale)

## Slide 76: What is an Incremental Quadrature Encoder?
A digital (angular) position sensor
slots spaced  deg. apart
photo sensors spaced /4 deg. apart
light source (LED)
shaft rotation
Ch. A
Ch. B
Quadrature Output from Photo Sensors

/4
Incremental Optical Encoder

## Slide 77: How is Position Determined from Quadrature Signals?
Ch. A
Ch. B
(00)
(11)
(10)
(01)
(A,B) =
00
01
11
10
Quadrature Decoder
State Machine
increment
counter
decrement
counter
Position resolution is /4 degrees
Illegal Transitions; generate phase error interrupt

## Slide 78: eQEP Module Block Diagram
Quadrature
Decoder
EQEPxA/XCLK
EQEPxB/XDIR
EQEPxI
EQEPxS
Position/Counter
Compare
Quadrature
Capture
32-Bit Unit
Time-Base
QEP
Watchdog
Generate the direction and clock for the position counter in quadrature count mode
Generate a sync output and/or interrupt on a position compare match
Measure the elapsed time between the unit position events; used for low speed measurement
Generate periodic interrupts for velocity calculations
Monitors the quadrature clock to indicate proper operation of the motion control system
Quadrature -clock mode
Direction -count mode
CPUx.SYSCLK
See the F28004x Driver Library User’s Guide for available functions

## Slide 79: eQEP Module Connections
Ch. A
Ch. B
Index
Quadrature
Decoder
EQEPxA/XCLK
EQEPxB/XDIR
EQEPxI
EQEPxS
Position/Counter
Compare
Quadrature
Capture
32-Bit Unit
Time-Base
QEP
Watchdog
Strobe
from homing sensor
CPUx.SYSCLK

## Slide 80: Sigma Delta Filter Module (SDFM)
SDFM is a four-channel digital filter designed specifically for current measurement and resolver position decoding in motor control applications
Each channel can receive an independent modulator bit stream
Bit streams are processed by four individually programmable digital decimation filters
Filters include a fast comparator for immediate digital threshold comparisons for over-current monitoring
Filter-bypass mode available to enable data logging, analysis, and customized filtering
0100111010…
Digital
Isolator
Isolation Boundary
Digital
Isolator

## Slide 81: SDFM Block Diagram

## Slide 82: Isolated Phase Current-Sense Example
SDFM enables galvanic isolation when utilized in conjunction with isolated sigma delta modulators
TMS320F28004x

## Slide 83: Lab 7: Control Peripherals
ADC
RESULT0
...
data
memory
pointer rewind
CPU copies
result to
buffer during
ADC ISR
ePWM2
jumper
wire
ADC-
INA0
TB Counter
Compare
Action Qualifier
ePWM1
eCAP1
Capture 1 Register
Capture 2 Register
Capture 3 Register
Capture 4 Register
View ADC buffer PWM samples
Code Composer
Studio
ePWM2 triggering
ADC on period match using SOCA trigger every 20 µs (50 kHz)
Input X-BAR
Notes: This foil describes the lab flow.
Connector wire: used to select the desired input to the ADC.
GP Timer 2: used to auto-trigger the ADC at a 50kHz rate.
The ADC will send an interrupt to the CPU when each conversion is done. Note that we are taking an ADC interrupt on every conversion (IM=0 in ADCTRL2), rather than on every other conversion. We could have written the code to do the later if we had wanted to, and saved some CPU interrupt overhead.
In the ADC ISR, the CPU will read the ADC result FIFO, and write the result into the data memory allocated for use as the results buffer. The CPU will then increment the pointer into the buffer, and check to see if the end of the buffer has been reached. If so, the pointer is rewound to the beginning of the buffer.
The contents of the buffer will be plotted in Code Explorer.

## Slide 84
C2000 Technical Training
www.ti.com/c2000