## Slide 1: Direct Memory Access Controller
Module 8
C2000™ Microcontroller Workshop
Copyright © 2019 Texas Instruments. All rights reserved.

## Slide 2: Module Objectives
Understand the operation of the Direct Memory Access (DMA) controller
Show how to use the DMA to transfer data between peripherals and/or memory without intervention from the CPU

## Slide 3: DMA Triggers, Sources, and Destinations
DMA
6-channels
ADC
Result
Registers
Triggers
PIE
DINTCH1-6
eCAP
GS0 RAM
GS3 RAM
eQEP
CMPSS
PGA
DAC
ADCA/B/C(INT1-4, EVT)
XINT(1-5) TINT(0-2)
EPWM1-8(SOCA-B)
ECAP1-7 SD1FLT(1-4)
SPITX/RX(A/B)
CANAIF/CANBIF(1-3)
LINATX/RX
FSITXA/FSIRXA
software
SDFM
ePWM
LIN
SPI
PMBus
FSI
CAN

## Slide 4: DMA Definitions
Word
  16 or 32 bits
  Word size is configurable per DMA channel
Burst
  Consists of multiple words
  Smallest amount of data transferred at one time
Burst Size
  Number of words per burst
  Specified by BURST_SIZE register
    5-bit ‘N-1’ value (maximum of 32 words/burst)
Transfer
  Consists of multiple bursts
Transfer Size
  Number of bursts per transfer
  Specified by TRANSFER_SIZE register
    16-bit ‘N-1’ value - exceeds any practical requirements

## Slide 5: Simplified State Machine Operation
Burst Size times
Transfer Size times
The DMA state machine at its most basic level is two nested loops
End Transfer
Move Word
Start Transfer
DMA can be configured to re-initialize at the end of the transfer (continuous mode)

## Slide 6: Basic Address Control Registers
SRC_ADDR
SRC_ADDR_SHADOW
DST_ADDR
DST_ADDR_SHADOW
SRC_BURST_STEP
SRC_TRANSFER_STEP
DST_BURST_STEP
DST_TRANSFER_STEP
Active pointers
Pointer shadow registers copied to active pointers at start of transfer
Signed value added to active pointer after each word
Signed value added to active pointer after each burst
32

## Slide 7: Simplified State Machine Example
3 words/burst
2 bursts/transfer
Read/Write Data
Add Burst Step
to Address
Pointer
Add Transfer
Step to Address
Pointer
Moved
“Burst Size”
Words?
Moved
“Transfer Size”
Bursts?
Y
Y
N
N
Wait for event
to start/continue
transfer
Start Transfer
End Transfer

## Slide 8: DMA Interrupts
Each DMA channel has its own PIE interrupt
The mode for each interrupt can be configured individually
The CHINTMODE bit in the MODE register selects the interrupt mode
Read/Write Data
Add Burst Step
to Address
Pointer
End Transfer
Add Transfer
Step to Address
Pointer
Moved
“Burst Size”
Words?
Moved
“Transfer Size”
Bursts?
Y
Y
N
N
Wait for event
to start/continue
transfer
Start Transfer
Mode #1: Interrupt at start of transfer
Mode #2: Interrupt at end of transfer

## Slide 9: Simple Example
0x4444
0x0000
0x00004003
0x00004002
0x00004001
0x00004000
0x00000000
0x0000F003
0x0000F002
0x0000F001
0x0000F000
0x00000000
0x3333
0x0000
0x2222
0x0000
0x0000F000
0x1111
0x0000
Read/Write Data
Add Burst Step
to Address
Pointer
End Transfer
Add Transfer
Step to Address
Pointer
Moved
“Burst Size”
Words?
Moved
“Transfer Size”
Bursts?
Y
Y
N
N
Wait for event
to start/continue
transfer
SRC_ADDR_SHADOW
SRC_ADDR
SRC_BURST_STEP
SRC_TRANSFER_STEP
BURST_SIZE*
TRANSFER_SIZE*
Addr
Value
0x1111
0xF000
0x2222
0xF001
0x3333
0xF002
0x4444
0xF003
Source Registers
0x0001
0x0001
0x0001
0x0001
DST_ADDR_SHADOW
DST_ADDR
DST_BURST_STEP
DST_TRANSFER_STEP
Addr
Value
0x4000
0x4001
0x4002
0x4003
Destination Registers
0x00004000
0x0001
0x0001
2 words/burst
2 bursts/transfer
* Size registers are N-1
Objective: Move 4 words from memory location 0xF000 to memory location 0x4000 and interrupt CPU at end of transfer
Start Transfer
Note: This example could also have been done using 1 word/burst and 4 bursts/transfer, or 4 words/burst and 1 burst/transfer. This would affect Round-Robin progression, but not interrupts.
Interrupt to PIE

## Slide 10: Data Binning Example
ADCA Results
GS1 RAM
CH0
CH1
CH2
CH3
CH4
0x0B00
CH0
CH1
CH2
CH3
CH4
CH0
CH1
CH2
CH3
CH4
1st Conversion Sequence
0xF000
0xF003
0xF006
0xF009
0xF00C
0x0B01
0x0B02
0x0B03
0x0B04
0xF001
0xF004
0xF007
0xF00A
0xF00D
0xF002
0xF005
0xF008
0xF00B
0xF00E
2nd Conversion Sequence
3rd Conversion Sequence
CH0
CH1
CH2
CH3
CH4
Objective: Bin 3 samples of 5 ADC channels, then interrupt the CPU

## Slide 11: Data Binning Example Register Setup
* Size registers are N-1
BURST_SIZE*
TRANSFER_SIZE*
0x0004
5 words/burst
0x0002
3 bursts/transfer
SRC_ADDR_SHADOW
SRC_BURST_STEP
SRC_TRANSFER_STEP
0x00000B00
0x0001
DST_ADDR_SHADOW
DST_BURST_STEP
DST_TRANSFER_STEP
0x0003
0xFFF5
(-11)
0xFFFC
(-4)
CH4
CH3
CH2
CH1
CH0
0x0B00
0x0B01
0x0B02
ADCA Results
GS1 RAM
0xF000
0xF003
0xF006
0xF009
0xF00C
CH0
CH0
CH0
CH1
CH1
CH1
CH2
CH2
CH2
CH3
CH3
CH3
CH4
CH4
CH4
0xF001
0xF004
0xF007
0xF00A
0xF00D
0xF002
0xF005
0xF008
0xF00B
0xF00E
0x0B03
0x0B04
Objective: Bin 3 samples of 5 ADC channels, then interrupt the CPU
SOC0 – SOC4 configured to CH0 – CH4, respectively, ADCA configured to re-trigger (continuous conversion)
ADC Registers:
DMA Registers:
0x0000F000
starting address**
** Typically use a relocatable symbol in your code, not a hard value

## Slide 12: Ping-Pong Buffer Example
ADCA Result Register
50 word ‘Ping’ buffer
50 word ‘Pong’ buffer
GS0 RAM
0x0B00
DMA Interrupt
DMA Interrupt
0xC140
Objective: Buffer ADC ch. 0 ping-pong style, 50 samples per buffer
ADCRESULT0
SOC0 configured to ADCINA0 with 1 conversion per trigger

## Slide 13: Ping-Pong Example Register Setup
DMA configured to re-init after transfer (CONTINUOUS = 1)
SRC_BURST_STEP
SRC_TRANSFER_STEP
0x0000
DST_BURST_STEP
DST_TRANSFER_STEP
0x0001
SRC_ADDR_SHADOW
DST_ADDR_SHADOW
BURST_SIZE*
TRANSFER_SIZE*
0x0000
1 word/burst
0x0031
50 bursts/transfer
* Size registers are N-1
Objective: Buffer ADC ch. 0 ping-pong style, 50 samples per buffer
don’t care
since BURST_SIZE = 0
don’t care
since BURST_SIZE = 0
0x00000B00
starting address
0x0000C140
starting address**
Read/Write Data
Add Burst Step
to Address
Pointer
End Transfer
Add Transfer Step
to Address Pointer
Moved
“Burst Size”
Words?
Moved
“Transfer Size”
Bursts?
Y
Y
N
N
Wait for event to
start/continue transfer
Start Transfer
Convert ADCA Channel ADCINA0 – 1 conversion per trigger (i.e. ePWM2SOCA)
DMA Registers:
ADC Registers:
Other:
** DST_ADDR_SHADOW must be changed between ping and pong buffer address in the DMA ISR. Typically use a relocatable symbol in your code, not a hard value.

## Slide 14: Channel Priority Modes
Round Robin Mode:
  All channels have equal priority
  After each enabled channel has transferred a burst of words, the next enabled channel is serviced in round robin fashion
Channel 1 High Priority Mode:
  Same as Round Robin except CH1 can interrupt DMA state machine
  If CH1 trigger occurs, the current word (not the complete burst) on any other channel is completed and execution is halted
  CH1 is serviced for complete burst
  When completed, execution returns to previous active channel
  This mode is intended primarily for the ADC, but can be used by any DMA event configured to trigger CH1
DMA
event?
CH6
CH1
CH2
CH5
CH4
CH3
Y
N

## Slide 15: Priority Modes and the State Machine
Read/Write Data
Add Burst Step
to Address
Pointer
Add Transfer
Step to Address
Pointer
Moved
“Burst Size”
Words?
Moved
“Transfer Size”
Bursts?
Y
Y
N
N
Point where other
pending channels
are serviced
Wait for event
to start/continue
transfer
Point where
CH1 can
interrupt other
channels in
CH1 Priority Mode
Start Transfer
End Transfer

## Slide 16: DMA Throughput
4 cycles/word
1 cycle delay to start each burst
1 cycle delay returning from CH1 high priority interrupt
32-bit transfer doubles throughput
  Example: 128 16-bit words from ADC to RAM
    8 bursts * [(4 cycles/word * 16 words/burst) + 1] = 520 cycles
  Example: 64 32-bit words from ADC to RAM
    8 bursts * [(4 cycles/word * 8 words/burst) + 1] = 264 cycles

## Slide 17: DMA vs. CPU Access Arbitration
DMA has priority over CPU
  If a multi-cycle CPU access is already in progress, DMA stalls until current CPU access finishes
  The DMA will interrupt back-to-back CPU accesses
Can the CPU be locked out?
  Generally No!
  DMA is multi-cycle transfer; CPU will sneak in an access when the DMA is accessing the other end of the transfer (e.g. while DMA accesses destination location, the CPU can access the source location)

## Slide 18: DMA Driverlib Functions
Initialize the DMA controller (hard reset)
DMA_initController();
Set DMA channel priority mode (round-robin or CH1 high priority)
DMA_setPriorityMode(ch1IsHighPri);
Configures the DMA channel trigger and mode
DMA_configMode(base, trigger, config);
Enable /disable peripheral trigger for DMA transfer
DMA_[enable|disable]Trigger(base);
Start / stop DMA channel (‘start’ – wait for first trigger event)
DMA_[start|stop]Channel(base);
  ch1IsHighPri value is ‘false’ for round-robin or ‘true’ for CH1 high priority
  base is the DMA channel base address: DMA_CHx_BASE (x = 1 to 6)
    trigger value is located in dma.h – see table on next slide for values
    config value is the logical OR of:
        DMA_CFG_ONESHOT_x (x = DISABLE or ENABLE)
        DMA_CFG_CONTINUOUS_x (x = DISABLE or ENABLE)
        DMA_CFG_SIZE_xBIT (x = 16 or 32)

## Slide 19: Peripheral Interrupt Trigger Sources
DMA_TRIGGER_SOFTWARE | DMA_TRIGGER_XINT2 | DMA_TRIGGER_EPWM7SOCB | DMA_TRIGGER_SPIATX
DMA_TRIGGER_ADCA1 | DMA_TRIGGER_XINT3 | DMA_TRIGGER_EPWM8SOCA | DMA_TRIGGER_SPIARX
DMA_TRIGGER_ADCA2 | DMA_TRIGGER_XINT4 | DMA_TRIGGER_EPWM8SOCB | DMA_TRIGGER_SPIBTX
DMA_TRIGGER_ADCA3 | DMA_TRIGGER_XINT5 | DMA_TRIGGER_TINT0 | DMA_TRIGGER_SPIBRX
DMA_TRIGGER_ADCA4 | DMA_TRIGGER_EPWM1SOCA | DMA_TRIGGER_TINT1 | DMA_TRIGGER_LINATX
DMA_TRIGGER_ADCAEVT | DMA_TRIGGER_EPWM1SOCB | DMA_TRIGGER_TINT2 | DMA_TRIGGER_LINARX
DMA_TRIGGER_ADCB1 | DMA_TRIGGER_EPWM2SOCA | DMA_TRIGGER_ECAP1 | DMA_TRIGGER_FSITXA
DMA_TRIGGER_ADCB2 | DMA_TRIGGER_EPWM2SOCB | DMA_TRIGGER_ECAP2 | DMA_TRIGGER_FSIRXA
DMA_TRIGGER_ADCB3 | DMA_TRIGGER_EPWM3SOCA | DMA_TRIGGER_ECAP3 | DMA_TRIGGER_CANAIF1
DMA_TRIGGER_ADCB4 | DMA_TRIGGER_EPWM3SOCB | DMA_TRIGGER_ECAP4 | DMA_TRIGGER_CANAIF2
DMA_TRIGGER_ADCBEVT | DMA_TRIGGER_EPWM4SOCA | DMA_TRIGGER_ECAP5 | DMA_TRIGGER_CANAIF3
DMA_TRIGGER_ADCC1 | DMA_TRIGGER_EPWM4SOCB | DMA_TRIGGER_ECAP6 | DMA_TRIGGER_CANBIF1
DMA_TRIGGER_ADCC2 | DMA_TRIGGER_EPWM5SOCA | DMA_TRIGGER_ECAP7 | DMA_TRIGGER_CANBIF2
DMA_TRIGGER_ADCC3 | DMA_TRIGGER_EPWM5SOCB | DMA_TRIGGER_SDFM1FLT1 | DMA_TRIGGER_CANBIF3
DMA_TRIGGER_ADCC4 | DMA_TRIGGER_EPWM6SOCA | DMA_TRIGGER_SDFM1FLT2 | 
DMA_TRIGGER_ADCCEVT | DMA_TRIGGER_EPWM6SOCB | DMA_TRIGGER_SDFM1FLT3 | 
DMA_TRIGGER_XINT1 | DMA_TRIGGER_EPWM7SOCA | DMA_TRIGGER_SDFM1FLT4 | 
DMA_configMode(base, trigger, config);

## Slide 20: DMA Driverlib Functions
Configure the source and destination addresses of the DMA channel
DMA_configAddresses(base, const void * destAddr, const void * srcAddr);
Configures the burst size and the address step size
DMA_configBurst (base, size, srcStep, destStep);
Configures the transfer size and the address step size
DMA_configTransfer (base, transferSize, srcStep, destStep);
Set the channel interrupt mode
DMA_setInterruptMode(base, mode);
Enable / disable DMA channel CPU interrupt
DMA_[enable|disable]Interrupt (base);
  base is the DMA channel base address: DMA_CHx_BASE (x = 1 to 6)
    destAddr is a pointer to the destination address
    srcAddr is a pointer to the source address
    size values is the number of words per burst (range from 1 to 32 words)
    srcStep and destStep value is the step size (signed values from -4096 to 4095)
    transferSize value is the number of bursts per transfer (max value of 65536)
    mode value is: DMA_INT_AT_BEGINNING or DMA_INT_AT_END

## Slide 21: Lab 8: Servicing the ADC with DMA
ADC
RESULT0
ePWM2
jumper
wire
ADCINA0
data
memory
Pointer
rewind
Display using CCS
TB Counter
Compare
Action Qualifier
ePWM1
ePWM2 triggering ADC on period match using SOCA trigger every 20 µs (50 kHz)
Objective:
Configure the DMA to buffer ADCA Channel A0 ping-pong style with 50 samples per buffer
ping
CPU writes data to AdcBuf during DMA ISR
pong
data
memory
DMA

## Slide 22
C2000 Technical Training
www.ti.com/c2000