## Slide 1: System Design
Module 10
C2000™ Microcontroller Workshop
Copyright © 2019 Texas Instruments. All rights reserved.

## Slide 2: Module Objectives
JTAG Emulation
Analysis and Diagnostic Capabilities
Flash Configuration and Memory Performance
Flash Programming
Dual Code Security Module (DCSM)

## Slide 3: Module Objectives
JTAG Emulation
Analysis and Diagnostic Capabilities
Flash Configuration and Memory Performance
Flash Programming
Dual Code Security Module (DCSM)

## Slide 4: JTAG Emulation System
Some Available Debug Probes
XDS100 CLASS -
BlackHawk: USB100
Spectrum Digital: XDS100
XDS110 CLASS -
Texas Instruments: XDS110
XDS200 CLASS -
BlackHawk: USB200
Spectrum Digital: XDS200
These debug probes offer a balance of low cost with good performance compared to the XDS100/XDS110 class debug probes
These debug probes are ultra-low cost and open-design which can used to create your own debug probe
H
E
A
D
E
R
System Under Test
SCAN IN
SCAN OUT
Debug Probe
TMS320C2000
Note: XDS510 CLASS debug probes are not recommended (obsolete); and for C2000, XDS560 CLASS debug probes are expensive and typically do not offer much advantage over the XDS200 CLASS debug probes
This debug probe replaces the XDS100 class while supporting a wider variety of standards

## Slide 5: Emulation Connections to the Device

## Slide 6: Emulation Mode Driverlib Functions
Driverlib Function | Options
CLAPROMCRC_setEmulationMode() | CLAPROMCRC_MODE_SOFT CLAPROMCRC_MODE_FREE
CPUTimer_setEmulationMode() | CPUTIMER_EMULATIONMODE_STOPAFTERNEXTDECREMENT CPUTIMER_EMULATIONMODE_STOPATZERO CPUTIMER_EMULATIONMODE_RUNFREE
DMA_setEmulationMode() | DMA_EMULATION_STOP DMA_EMULATION_FREE_RUN
ECAP_setEmulationMode() | ECAP_EMULATION_STOP ECAP_EMULATION_RUN_TO_ZERO ECAP_EMULATION_FREE_RUN
EPWM_setEmulationMode() | EPWM_EMULATION_STOP_AFTER_NEXT_TB EPWM_EMULATION_STOP_AFTER_FULL_CYCLE EPWM_EMULATION_FREE_RUN
EQEP_setEmulationMode() | EQEP_EMULATIONMODE_STOPIMMEDIATELY EQEP_EMULATIONMODE_STOPATROLLOVER EQEP_EMULATIONMODE_RUNFREE
I2C_setEmulationMode() | I2C_EMULATION_STOP_SCL_LOW I2C_EMULATION_FREE_RUN
SPI_setEmulationMode() | SPI_EMULATION_STOP_MIDWAY SPI_EMULATION_STOP_AFTER_TRANSMIT SPI_EMULATION_FREE_RUN
Selects the behavior of the peripheral during emulation control
Note: see the F28004x Driverlib User’s Guide for detailed usage

## Slide 7: Module Objectives
JTAG Emulation
Analysis and Diagnostic Capabilities
Flash Configuration and Memory Performance
Flash Programming
Dual Code Security Module (DCSM)

## Slide 8: Analysis and Diagnostic Capabilities
C28x CPU has two hardware analysis units:
  Address and Data Comparison Units (ACU/DCU)
    ACU – counts events or monitors address buses
    DCU – monitors address and data buses
  ACU and DCU can be configured as analysis breakpoints or watchpoints; in addition, ACU can be configured as a benchmark counter or event counter
Embedded real-time analysis and diagnostic (ERAD) module:
  Enhances the debug and system analysis capabilities
  ERAD module is implemented external to the C28x CPU core
  ERAD module consists of Enhanced Bus Comparator Units (EBC) and Benchmark System Event Counter Units (BSEC)
    EBC – used to generate hardware breakpoints, hardware watchpoints and other output events
    BSEC – used to analyze and profile the system

## Slide 9: C28x CPU Hardware Analysis Units
The C28x CPU two hardware analysis units can be configured to provide any one of the following advanced debug features:
Halt program execution after a specific value is written to a variable
1 Address Watchpoint with Data
Halt on a specified instruction only after some other specific routine has executed
1 Pair Chained Breakpoints
Halt on a specified instruction
(for debugging in flash)
2 Hardware Breakpoints
A memory location is getting corrupted; halt the processor when any value is written to this location
2 Address Watchpoints
Debug Activity
Analysis Configuration





## Slide 10: ERAD Module
8 Enhanced Bus Comparator Units
  Similar to ACU/DCU
  Inputs: address bus, program counter, data bus
  Comparison mode
    (>, >=, <, <=)
  Output: debug triggers, event output
4 Benchmark System Event Counter Units
  Similar to count feature in ACU
  Inputs: events from EBC, system events
  Outputs: debug events
ERAD can be used by the application or debugger
Enhanced Bus Comparator Units (EBC)
Benchmark System Event Counter Unit (BSEC)
Address Bus
Data Bus
Program Counter
ACU
DCU
C28x CPU
System Events
ERAD
Debug
Triggers
Event
Output
Counter
Events
x8
x4
ERAD expands device debug and system analysis capabilities to 10 hardware breakpoints and 10 hardware watchpoints

## Slide 11: Module Objectives
JTAG Emulation
Analysis and Diagnostic Capabilities
Flash Configuration and Memory Performance
Flash Programming
Dual Code Security Module (DCSM)

## Slide 12: Basic Flash Operation
RWAIT bit-field in the FRDCNTL register specifies the number of random accesses wait states
OTP reads are hardwired for 10 wait states (RWAIT has no effect)
Must specify the number of SYSCLK cycle wait-states; Reset defaults are maximum value (15)
Flash/OTP reads returned after (RWAIT + 1 SYSCLK cycles)
Flash configuration code should not be run from the flash memory
*** Refer to the F28004x data sheet for value details ***
For 100 MHz, RWAIT = 4
    ctrlBase is base address of the flash control registers: FLASH0CTRL_BASE
    waitstates value is a number between 0 and 15
Set the number of wait states for a flash read access
Flash_setWaitstates(ctrlBase, waitstates);

## Slide 13: Speeding Up Execution in Flash / OTP
16 or 32 dispatched
16
128
Aligned 128-bit fetch
2-level deep fetch buffer
128
C28x core decoder unit
128-bit data cache
MUX
Instruction fetch
Data read either from program or data memory
Flash or OTP
    ctrlBase is base address of the flash control registers: FLASH0CTRL_BASE
Enable prefetch mechanism:
Flash_enablePrefetch(ctrlBase);
Enable data cache:
Flash_enableCache(ctrlBase);

## Slide 14: Code Execution Performance
Assume 100 MHz SYSCLKOUT and single-cycle execution for each instruction
Internal RAM: 100 MIPS
Fetch up to 32 bits every cycle  1 instruction/cycle
Flash: 100 MIPS
Assume RWAIT=4, prefetch buffer enabled
Fetch 128 bits every 4 cycles:
(128 bits) / (32-bits per instruction worst-case)  4 instructions/4 cycles
PC discontinuity will degrade this, while 16-bit instructions can help
Benchmarking in control applications has shown actual performance of about 90% efficiency, yielding approximately 90 MIPS

## Slide 15: Data Access Performance
Assume 100 MHz SYSCLKOUT
Internal RAM has best data performance – put time critical data here
Flash performance often sufficient for constants and tables
Note that the flash instruction fetch pipeline will also stall during a flash data access
For best flash performance, arrange data so that all 128 bits in a cache line are utilized (e.g. sequential access)
Memory 16-bit access 32-bit access Notes
(words/cycle) (words/cycle)
Internal RAM 1 1
Flash 0.73 0.57
‘sequential’ access (8 words/11 cycles) (4 words/7 cycles)
Flash 0.25 0.25
random access (1 word/4 cycles) (1 word/4 cycles)
Assumes RWAIT = 4,
flash data cache enabled,
all 128 bits in cache are used
Assumes RWAIT = 4

## Slide 16: Flash / OTP Power Modes
Power configuration settings save power by putting Flash/OTP to ‘Sleep’ or ‘Standby’ mode; flash will automatically enter ‘Active’ mode if a Flash/OTP access is made
At reset Flash/OTP is in sleep mode
Operates in three power modes:
  Sleep (lowest power)
  Standby (shorter transition time to active)
  Active (highest power)
After an access is made, Flash/OTP can automatically power down to ‘Standby’ or ‘Sleep’ (active grace period set in user programmable counters)
    ctrlBase is base address of the flash control registers: FLASH0CTRL_BASE
    bank parameter is: FLASH_BANK0 or FLASH_BANK1
    powerMode value for:
      Bank – FLASH_BANK_PWR_x (x = SLEEP, STANDBY, or ACTIVE)
      Pump – FLASH_PUMP_PWR_x (x = SLEEP or ACTIVE)
Set fallback power mode for flash bank:
Flash_setBankPowerMode(ctrlBase, bank, powerMode);
Set fallback power mode for charge pump:
Flash_setPumpPowerMode(ctrlBase, powerMode);

## Slide 17: Error Correction Code (ECC) Protection
Provides capability to screen out Flash/OTP memory faults (enabled at reset)
Single error correction and double error detection (SECDED)
For every 64-bits of Flash/OTP, 8 ECC check bits are calculated and programmed into ECC memory
ECC check bits are programmed along with Flash/OTP data
During an instruction fetch or data read operation the 64-bit data/8-bit ECC are processed by the SECDED to determine one of three conditions:
  No error occurred
  A correctable error (single bit data error) occurred
  A non-correctable error (double bit data error or address error) occurred
SECDED
Single-bit data error
Address/double-bit data error
Single-bit error position
Corrected data out
SECDED
Single-bit data error
Address/double-bit data error
Single-bit error position
Corrected data out
128-bit aligned
Flash
and
OTP
ECC (15:8)
Data (127:64)
ECC (7:0)
Data (63:0)
    ctrlBase is base address of the ECC registers: FLASH0ECC_BASE
Enable ECC protection: Flash_enableECC(eccBase);

## Slide 18: Initializing Flash Module
// CPU Initialization
Device_init();
•
•
•
Main.c
flash.c
void Flash_initModule(uint32_t ctrlBase, uint32_t eccBase, uint16_t waitstates)
{
Flash_setBankPowerMode(ctrlBase, FLASH_BANK0, FLASH_BANK_PWR_ACTIVE);
Flash_setBankPowerMode(ctrlBase, FLASH_BANK1, FLASH_BANK_PWR_ACTIVE);
Flash_setPumpPowerMode(ctrlBase, FLASH_PUMP_PWR_ACTIVE);
Flash_disableCache(ctrlBase); //disable before changing wait states
Flash_disablePrefetch(ctrlBase); //disable before changing wait states
Flash_setWaitstates(ctrlBase, waitstates);
Flash_enableCache(ctrlBase); //enable to improve performance
Flash_enablePrefetch(ctrlBase); //enable to improve performance
Flash_enableECC(eccBase);
}
device.c
void Device_init(void)
{
#ifdef _FLASH
// Copy time critical and flash setup code to RAM
memcpy(...&Ramfuncs...);
#endif
// Call flash initialization setup
Flash_initModule(FLASH0CTRL_BASE, FLASH0ECC_BASE, DEVICE_FLASH_WAITSTATES)
}
device.h
#define DEVICE_FLASH_WAITSTATES 4
;

## Slide 19: Module Objectives
JTAG Emulation
Analysis and Diagnostic Capabilities
Flash Configuration and Memory Performance
Flash Programming
Dual Code Security Module (DCSM)

## Slide 20: Flash Programming Basics
The device CPU performs the flash programming
The CPU executes flash utility code from RAM that reads the flash data and writes it into the flash memory
We need to get the flash utility code and the flash data into RAM
FLASH
CPU
RAM
F28004x
JTAG
Emulator
SPI
Flash Utility Code
Flash Data
I2C
ROM
Bootloader
CAN
SCI
RS232
GPIO

## Slide 21: Flash Programming Basics
Sequence of steps for flash programming:
Minimum Erase size is a sector
Minimum Program size is a bit!
1. Erase - Set all bits to one
Program - Program selected bits with zero
Verify - Verify flash contents
Algorithm Function
Flash Bank 0
Flash Bank 1
0x0008 0000
0x0008 FFFF
0x0009 0000
0x0009 FFFF
64K x 16
64K x 16

## Slide 22: Flash Programming Utilities
JTAG Emulator Based
  CCS on-chip Flash programmer (Tools  On-Chip Flash)
  CCS UniFlash (TI universal Flash utility)
  BlackHawk Flash utilities (requires Blackhawk emulator)
  Elprotronic FlashPro2000
  Spectrum Digital SDFlash JTAG (requires SD emulator)
SCI Serial Port Bootloader Based
  CodeSkin C2Prog
  Elprotronic FlashPro2000
Production Test/Programming Equipment Based
  BP Microsystems programmer
  Data I/O programmer
Build your own custom utility
  Can use any of the ROM bootloader methods
  Can embed flash programming into your application
  Flash API algorithms provided by TI
* TI web has links to all utilities (http://www.ti.com/c2000)

## Slide 23: Module Objectives
JTAG Emulation
Analysis and Diagnostic Capabilities
Flash Configuration and Memory Performance
Flash Programming
Dual Code Security Module (DCSM)

## Slide 24: Dual Code Security Module (DCSM)
DCSM offers protection for two zones – zone 1 & zone 2
Each zone has its own dedicated secure OTP
  Contains security configurations for each zone
The following on-chip memory can be secured:
  Flash – each sector individually
  LS0-7 RAM – each block individually
Data reads and writes from secured memory are only allowed for code running from secured memory
All other data read/write accesses are blocked:
  JTAG emulator/debugger, ROM bootloader, code running in external memory or unsecured internal memory

## Slide 25: Zone Selection
Each securable on-chip memory resource can be allocated to either zone 1 (Z1), zone 2 (Z2), or as non-secure
  DcsmZ1Regs.Z1_GRABSECTR register:
    Allocates individual flash sectors to zone 1 or non-secure
  DcsmZ2Regs.Z2_GRABSECTR register:
    Allocates individual flash sectors to zone 2 or non-secure
  DcsmZ1Regs.Z1_GRABRAMR register:
    Allocates LS0-7 to zone 1 or non-secure
  DcsmZ2Regs.Z2_GRABRAMR register:
    Allocates LS0-7 to zone 2 or non-secure
Technical Reference Manual contains a table to resolve mapping conflicts

## Slide 26: CSM Passwords
Each zone is secured by its own 128-bit (four 32-bit words) user defined CSM password
Passwords for each zone is stored in its dedicated OTP location
  Location based on a zone-specific link pointer
128-bit CSMKEY registers are used to secure and unsecure the device
Password locations for each zone can be locked and secured by programming PSWDLOCK fields in the OTP with any value other than “1111” (0xF)
Zx_CSMPSWD0
Zx_CSMPSWD1
Zx_CSMPSWD2
Zx_CSMPSWD3

## Slide 27: Zone Select Bits in OTP
xxx11111111111111111111111111111 0x020
xxx11111111111111111111111111110 0x030
xxx1111111111111111111111111110x 0x040
xxx111111111111111111111111110xx 0x050
xxx11111111111111111111111110xxx 0x060
xxx1111111111111111111111110xxxx 0x070
xxx111111111111111111111110xxxxx 0x080
xxx11111111111111111111110xxxxxx 0x090
xxx1111111111111111111110xxxxxxx 0x0A0
xxx111111111111111111110xxxxxxxx 0x0B0
xxx11111111111111111110xxxxxxxxx 0x0C0
xxx1111111111111111110xxxxxxxxxx 0x0D0
xxx111111111111111110xxxxxxxxxxx 0x0E0
xxx11111111111111110xxxxxxxxxxxx 0x0F0
xxx1111111111111110xxxxxxxxxxxxx 0x100
xxx111111111111110xxxxxxxxxxxxxx 0x110
xxx11111111111110xxxxxxxxxxxxxxx 0x120
xxx1111111111110xxxxxxxxxxxxxxxx 0x130
xxx111111111110xxxxxxxxxxxxxxxxx 0x140
xxx11111111110xxxxxxxxxxxxxxxxxx 0x150
xxx1111111110xxxxxxxxxxxxxxxxxxx 0x160
xxx111111110xxxxxxxxxxxxxxxxxxxx 0x170
xxx11111110xxxxxxxxxxxxxxxxxxxxx 0x180
xxx1111110xxxxxxxxxxxxxxxxxxxxxx 0x190
xxx111110xxxxxxxxxxxxxxxxxxxxxxx 0x1A0
xxx11110xxxxxxxxxxxxxxxxxxxxxxxx 0x1B0
xxx1110xxxxxxxxxxxxxxxxxxxxxxxxx 0x1C0
xxx110xxxxxxxxxxxxxxxxxxxxxxxxxx 0x1D0
xxx10xxxxxxxxxxxxxxxxxxxxxxxxxxx 0x1E0
xxx0xxxxxxxxxxxxxxxxxxxxxxxxxxxx 0x1F0
Zx-LINKPOINTER
Address offset of Zone-Select block
Zone Select Block | 
Addr. Offset | 32-bit Content
0x0 | Zx-EXEONLYRAM
0x2 | Zx-EXEONLYSECT
0x4 | Zx-GRABRAM
0x6 | Zx-GRABSECT
0x8 | Zx-CSMPSWD0
0xA | Zx-CSMPSWD1
0xC | Zx-CSMPSWD2
0xE | Zx-CSMPSWD3
Final link pointer value is resolved by comparing all three individual link pointer values (bit-wise voting logic)
OTP value “1” programmed as “0” (no erase operation)

## Slide 28: Zone Select Block - Linker Pointer
Zone Select Block | 
Addr. Offset | 32-bit Content
0x0 | Zx-EXEONLYRAM
0x2 | Zx-EXEONLYSECT
0x4 | Zx-GRABRAM
0x6 | Zx-GRABSECT
0x8 | Zx-CSMPSWD0
0xA | Zx-CSMPSWD1
0xC | Zx-CSMPSWD2
0xE | Zx-CSMPSWD3
Zone 1 OTP FLASH | 
0x78000 | Z1-LINKPOINTER1
0x78002 | Reserved
0x78004 | Z1-LINKPOINTER2
0x78006 | Reserved
0x78008 | Z1-LINKPOINTER3
0x7800A | Reserved
0x78010 | Z1-PSWDLOCK
0x78012 | Reserved
0x78014 | Z1-CRCLOCK
0x78016 | Reserved
0x78018 | Reserved
0x7801A | Reserved
0x7801E | Z1-BOOTCTRL
0x78020 | ZoneSelectBlock1 (16 x 16-bits)
0x78030 | ZoneSelectBlock2 (16 x 16-bits)
● ● | ● ●
0x781F0 | ZoneSelectBlockn (16 x 16-bits)
Zone 2 OTP FLASH | 
0x78200 | Z2-LINKPOINTER1
0x78202 | Reserved
0x78204 | Z2-LINKPOINTER2
0x78206 | Reserved
0x78208 | Z2-LINKPOINTER3
0x7820A | Reserved
0x78210 | Z2-PSWDLOCK
0x78212 | Reserved
0x78214 | Z2-CRCLOCK
0x78216 | Reserved
0x78218 | Reserved
0x7821A | Reserved
0x7821E | Z2-BOOTCTRL
0x78220 | ZoneSelectBlock1 (16 x 16-bits)
0x78230 | ZoneSelectBlock2 (16 x 16-bits)
● ● | ● ●
0x783F0 | ZoneSelectBlockn (16 x 16-bits)
Three link pointers need to be programmed with the same value (not ECC protected)

## Slide 29: Secure and Unsecure the CSM
The CSM is always secured after reset
To unsecure the CSM:
  Perform a dummy read of each CSMPSWD(0,1,2,3) register (passwords in the OTP)
  Write the correct password to each CSMKEY(0,1,2,3) register
The boot ROM code will automatically unlock the device as part of the initialization sequence for devices that do not have passwords programmed
  See Technical Reference Manual for details

## Slide 30: CSM Password Match Flow
Zone secure after reset or runtime
Start
Zone
Unsecure
Write the CSM Password of that Zone into CSMKEY(0/1/2/3) registers
Correct password?
Yes
No
Read Linkpointer and calculate the address of ZoneSelectBlock
Dummy Read of CSM PWL of the Secure Zone which needed to be unsecure

## Slide 31: Lab 10: Programming the Flash
Objective:
Program system into flash memory
Learn use of CCS flash programmer
DO NOT PROGRAM PASSWORDS
ADC
RESULT0
ePWM2
jumper
wire
TB Counter
Compare
Action Qualifier
ePWM1
ADCINA0
ePWM2 triggering
ADC on period match using SOCA trigger every 20 µs (50 kHz)
CPU copies
result to
buffer during
CLA ISR
...
data
memory
pointer rewind
Display using CCS
CLA
_Cla1Task1
_Cla1Task2
_Cla1Task8

## Slide 32: Flash Memory Section Blocks
SECTIONS
{
codestart :> BEGIN_FLASH, PAGE = 0
}
Lab_10.cmd
BEGIN_FLASH
length = 0x2
page = 0
FLASH_BANK0_SEC0
length = 0x000FFE
page = 0
0x080000
0x080002
0x081000
origin =
FLASH_BANK0_SEC1_15
length = 0x00F000
page = 0
FLASH_BANK1_SEC0_15
length = 0x010000
page = 0
0x090000

## Slide 33: Startup Sequence from Flash Memory
0x080000
0x3F8000
0x3FFFC0
Boot ROM (32Kw)
BROM vector (64w)
* reset vector
Boot Code
RESET
InitBoot
{SCAN GPIO}
FLASH (128Kw)
_c_int00
LB
“rts2800_fpu32.lib”
“user” code sections
_c_int00
main ( )
{
}
2
3
4
5
1
……
……
……
* reset vector = 0x3FC7A5

## Slide 34
C2000 Technical Training
www.ti.com/c2000