## Slide 1: Communications
Module 11
C2000™ Microcontroller Workshop
Copyright © 2019 Texas Instruments. All rights reserved.

## Slide 2: Module Objectives
Serial Peripheral Interface (SPI)
Serial Communication Interface (SCI)
Local Interconnect Network (LIN)
Inter-Integrated Circuit (I2C)
Controller Area Network (CAN)
Power Management Bus (PMBus)
Fast Serial Interface (FSI)

## Slide 3: Module Objectives
Serial Peripheral Interface (SPI)
Serial Communication Interface (SCI)
Local Interconnect Network (LIN)
Inter-Integrated Circuit (I2C)
Controller Area Network (CAN)
Power Management Bus (PMBus)
Fast Serial Interface (FSI)

## Slide 4: SPI Data Flow
Simultaneous transmits and receive
SPI Master provides the clock signal
SPI Shift Register
SPI Device #1 - Master
SPI Device #2 - Slave
shift
shift
clock
SPI Shift Register

## Slide 5: SPI Block Diagram
C28x - SPI Master Mode Shown
SPIRXBUF.15-0
SPIDAT.15-0
SPICLK
SPISOMI
SPISIMO
LSPCLK
baud
rate
clock
polarity
clock
phase
SPITXBUF.15-0
LSB
MSB
TX FIFO_0
TX FIFO_15
RX FIFO_15
RX FIFO_0

## Slide 6: SPI Data Character Justification
Programmable data length of 1 to 16 bits
Transmitted data of less than 16 bits must be left justified
  MSB transmitted first
Received data of less than 16 bits are right justified
User software must mask-off unused MSB’s
11001001XXXXXXXX
XXXXXXXX11001001
SPIDAT - Processor #1
SPIDAT - Processor #2

## Slide 7: SPI Summary
Synchronous serial communications
  Two wire transmit or receive (half duplex)
  Three wire transmit and receive (full duplex)
Software configurable as master or slave
  C28x provides clock signal in master mode
Data length programmable from 1-16 bits
125 different programmable baud rates

## Slide 8: Module Objectives
Serial Peripheral Interface (SPI)
Serial Communication Interface (SCI)
Local Interconnect Network (LIN)
Inter-Integrated Circuit (I2C)
Controller Area Network (CAN)
Power Management Bus (PMBus)
Fast Serial Interface (FSI)

## Slide 9: SCI Pin Connections
Transmitter-data
buffer register
SCI Device #1
SCIRXD
SCITXD
SCITXD
SCIRXD
SCI Device #2
8
Receiver-data
buffer register
8
Transmitter-data
buffer register
Receiver
shift register
Transmitter
shift register
8
Receiver-data
buffer register
Receiver
shift register
Transmitter
shift register
8
(Full Duplex Shown)
RX FIFO_0
RX FIFO_15
RX FIFO_0
RX FIFO_15
TX FIFO_15
TX FIFO_0
TX FIFO_15
TX FIFO_0

## Slide 10: SCI Data Format
Communications Control Register (SCICCR)
0 = 1 Stop bit
1 = 2 Stop bits
0 = Odd
1 = Even
0 = Disabled
1 = Enabled
0 = Disabled
1 = Enabled
0 = Idle-line mode
1 = Addr-bit mode
# of data bits = (binary + 1)
e.g. 110b gives 7 data bits
Stop
Bits
Even/Odd
Parity
Parity
Enable
Loopback
Enable
Addr/Idle
Mode
SCI
Char2
SCI
Char1
SCI
Char0
7
6
5
4
3
2
1
0
This bit present only in Address-bit mode
NRZ (non-return to zero) format
Start
LSB
2
3
4
5
6
7
MSB
Addr/
Data
Parity
Stop 1
Stop 2

## Slide 11: SCI Data Timing
Start bit valid if 4 consecutive SCICLK periods of zero bits after falling edge
Majority vote taken on 4th, 5th, and 6th SCICLK cycles
Start Bit
LSB of Data
Majority
Vote
Falling Edge Detected
SCIRXD
SCICLK
(Internal)
1 2 3 4 5 6 7 8 1 2 3 4 5 6 7 8 1 2
Note: 8 SCICLK periods per data bit

## Slide 12: Multiprocessor Wake-Up Modes
Allows numerous processors to be hooked up to the bus, but transmission occurs between only two of them
Idle-line or Address-bit modes
Sequence of Operation
  1. Potential receivers set SLEEP = 1, which disables RXINT except when an address frame is received
  2. All transmissions begin with an address frame
  3. Incoming address frame temporarily wakes up all SCIs on bus
  4. CPUs compare incoming SCI address to their SCI address
  5. Process following data frames only if address matches

## Slide 13: Idle-Line Wake-Up Mode
Idle time separates blocks of frames
Receiver wakes up when SCIRXD high for 10 or more bit periods
Two transmit address methods
  Deliberate software delay of 10 or more bits
  Set TXWAKE bit to automatically leave exactly 11 idle bits
Last Data
ST
SP
ST
Data
SCIRXD/
SCITXD
Block of Frames
SP
SP
Last Data
ST
Addr
SP
Idle
Period
10 bits
or greater
Idle
Period
10 bits
or greater
Address frame
follows 10 bit
or greater idle
1st data frame
SP
ST
Addr
Idle periods
of less than
10 bits

## Slide 14: Address-Bit Wake-Up Mode
All frames contain an extra address bit
Receiver wakes up when address bit detected
Automatic setting of Addr/Data bit in frame by setting TXWAKE = 1 prior to writing address to SCITXBUF
Last Data
ST
ST
Data
SCIRXD/
SCITXD
Block of Frames
SP
SP
Last Data
ST
Addr
SP
Idle Period
length of no
significance
First frame within
block is Address.
ADDR/DATA
bit set to 1
1st data frame
0
1
0
0
SP
ST
Addr
1
SP
no additional
idle bits needed
beyond stop bits

## Slide 15: SCI Summary
Asynchronous communications format
65,000+ different programmable baud rates
Two wake-up multiprocessor modes
  Idle-line wake-up & Address-bit wake-up
Programmable data word format
  1 to 8 bit data word length
  1 or 2 stop bits
  even/odd/no parity
Error Detection Flags
  Parity error; Framing error; Overrun error; Break detection
Transmit FIFO and receive FIFO
Individual interrupts for transmit and receive

## Slide 16: Module Objectives
Serial Peripheral Interface (SPI)
Serial Communication Interface (SCI)
Local Interconnect Network (LIN)
Inter-Integrated Circuit (I2C)
Controller Area Network (CAN)
Power Management Bus (PMBus)
Fast Serial Interface (FSI)

## Slide 17: Local Interconnect Network (LIN)
A broadcast serial network
  One master, up to sixteen addressable slaves
  Serial link layer similar to UART (e.g., start, data, stop bits)
  Single wire (plus ground)
  12V bus (originally desiged for automotive apps)
  No bus arbitration or collision detection
    Master initiates all communication
    A single slave responds
  Configurable Baud Rate up to 20 Kbits/s
C2000 LIN module
  Compliant with the LIN spec 2.1
  Can be used as an SCI (UART), if desired

## Slide 18: LIN Module Block Diagram
SCIRXSHF
TD7
TD6
TD5
TD4
TD3
TD2
TD1
TD0
SCITXSHF
Mask
Filter
Synchronizer
LINRX
LINTX
Checksum
Calculator
Parity
Calculator
Bit
Monitor
RD0
RD1
RD2
RD4
RD5
RD6
RD7
RD3
8

## Slide 19: LIN Message Frame
Sync Break – beginning of a message
Sync Field – bit rate synchronizing occurs
ID Field
  Identifier: 6-bit ID, 2-bit parity
  Message (optional): 2, 4, or 8 bytes
Data Field – 1-bit start, 8-bit data, 1-bit stop bit
Checksum Field – 1-bit start, 8-bit checksum, 1-bit stop
In-Frame & Inter-byte Spaces – can be 0
Sync
Break
Sync
Field
ID
Field
Data
Field
Check
Sum
Field
Data
Field
Data
Field
Data
Field
Data
Field
Interbyte Spaces
In-Frame Space
1 to 8 Data Fields
Master Sends
Slave Responds
Message Frame

## Slide 20: LIN Data Timing
To make a determination of the bit value, 16 samples of each bit are taken with majority vote on samples 8, 9, and 10
Majority
Vote
LINRX
LM_CLK
(Internal)
Majority
Vote
Majority
Vote

## Slide 21: LIN Bus Connections
RX
TX
LIN Controller
(F28004x)
LIN bus
1 KW
(master node only)
LIN Transceiver
12 V
12 V
~5 KW
Vdd (e.g., 3.3 V)
Vdd
Notes: TI transceiver: SN75LBC031
- interfaces the single ended CAN controller with the differential CAN bus.
- transmission rate up to 1Mbit/s
2 states on the bus:
recessive: CAN_H = CAN_L = 2.5V
dominant: CAN_H = 3.5V and CAN_L = 1.5V

## Slide 22: LIN Summary
Functionally compatible with standalone SCI of C28x devices
Identification masks for filtering
Automatic master header generation
231 programmable transmission rates with 7 fractional bits
Automatic wakeup support
Error detection (bit, bus, no response, checksum, synchronization, parity)
Multi-buffered receive/transmit units

## Slide 23: Module Objectives
Serial Peripheral Interface (SPI)
Serial Communication Interface (SCI)
Local Interconnect Network (LIN)
Inter-Integrated Circuit (I2C)
Controller Area Network (CAN)
Power Management Bus (PMBus)
Fast Serial Interface (FSI)

## Slide 24: Inter-Integrated Circuit (I2C)
NXP Semiconductors I2C-bus specification compliant, version 2.1
Data transfer rate from 10 kbps up to 400 kbps
Each device can be considered as a Master or Slave
Master initiates data transfer and generates clock signal
Device addressed by Master is considered a Slave
Multi-Master mode supported
Standard Mode – send exactly n data values (specified in register)
Repeat Mode – keep sending data values (use software to initiate a stop or new start condition)
28x
I2C
I2C
Controller
I2C
EPROM
28x
I2C
.
.
.
.
.
.
.
.
.
.
.
.
Pull-up
Resistors
VDD
Serial Data (SDA)
Serial Clock (SCL)

## Slide 25: I2C Block Diagram
TX FIFO
RX FIFO
I2CDXR
I2CDRR
I2CXSR
I2CRSR
Clock
Circuits
SDA
SCL

## Slide 26: I2C Operating Modes
Operating Mode Description
Slave-receiver mode Module is a slave and receives data from a master
(all slaves begin in this mode)
Slave-transmitter mode Module is a slave and transmits data to a master
(can only be entered from slave-receiver mode)
Master-receiver mode Module is a master and receives data from a slave
(can only be entered from master-transmit mode)
Master-transmitter mode Module is a master and transmits to a slave
(all masters begin in this mode)

## Slide 27
I2C Serial Data Formats
S
Slave Address
R/W
ACK
Data
Data
ACK
ACK
P
1
7
1
1
n
1
n
1
1
7-Bit Addressing Format
S
11110AA
R/W
ACK
AAAAAAAA
Data
ACK
ACK
P
1
7
1
1
8
1
n
1
1
10-Bit Addressing Format
S
Data
ACK
Data
Data
ACK
ACK
P
1
n
1
n
1
n
1
1
Free Data Format
R/W = 0 – master writes data to addressed slave
R/W = 1 – master reads data from the slave
n = 1 to 8 bits
S = Start (high-to-low transition on SDA while SCL is high)
P = Stop (low-to-high transition on SDA while SCL is high)

## Slide 28: I2C Arbitration
Arbitration procedure invoked if two or more master-transmitters simultaneously start transmission
  Procedure uses data presented on serial data bus (SDA) by competing transmitters
  First master-transmitter which drives SDA high is overruled by another master-transmitter that drives SDA low
  Procedure gives priority to the data stream with the lowest binary value
1
0
1
0
0
1
0
1
1
0
0
1
0
1
SCL
SDA
Data from device #1
Data from device #2
Device #1 lost arbitration and switches to slave-receiver mode
Device #2 drives SDA

## Slide 29: I2C Summary
Compliance with Philips I2C-bus specification (version 2.1)
7-bit and 10-bit addressing modes
Configurable 1 to 8 bit data words
Data transfer rate from 10 kbps up to 400 kbps
Transmit FIFO and receive FIFO

## Slide 30: I2C Interrupt/polling Flags

## Slide 31: I2C Additional Modes

## Slide 32: Module Objectives
Serial Peripheral Interface (SPI)
Serial Communication Interface (SCI)
Local Interconnect Network (LIN)
Inter-Integrated Circuit (I2C)
Controller Area Network (CAN)
Power Management Bus (PMBus)
Fast Serial Interface (FSI)

## Slide 33: Controller Area Network (CAN) A Multi-Master Serial Bus System
CAN 2.0B Standard
High speed (up to 1 Mbps)
Add a node without disturbing the bus (number of nodes not limited by protocol)
Less wires (lower cost, less maintenance, and more reliable)
Redundant error checking (high reliability)
No node addressing (message identifiers)
Broadcast based signaling
C
E
D
A
B

## Slide 34: CAN Bus
Two wire differential bus (usually twisted pair)
Max. bus length depend on transmission rate
  40 meters @ 1 Mbps
CAN
NODE B
CAN
NODE A
CAN
NODE C
CAN_H
CAN_L
120W
120W

## Slide 35: CAN Node Wired-AND Bus Connection
RX
TX
CAN Controller
(TMS320F28004x)
CAN_L
CAN_H
120W
120W
CAN Transceiver
(e.g. TI SN65HVD23x)

## Slide 36: Principles of Operation
Data messages transmitted are identifier based, not address based
Content of message is labeled by an identifier that is unique throughout the network
  (e.g. rpm, temperature, position, pressure, etc.)
All nodes on network receive the message and each performs an acceptance test on the identifier
If message is relevant, it is processed (received); otherwise it is ignored
Unique identifier also determines the priority of the message
  (lower the numerical value of the identifier, the higher the priority)
When two or more nodes attempt to transmit at the same time, a non-destructive arbitration technique guarantees messages are sent in order of priority and no messages are lost

## Slide 37: Non-Destructive Bitwise Arbitration
Bus arbitration resolved via arbitration with wired-AND bus connections
  Dominate state (logic 0, bus is high)
  Recessive state (logic 1, bus is low)
Node A wins arbitration
CAN Bus
Node A
Node B
Node C
Start
Bit
Node B loses arbitration
Node C loses arbitration

## Slide 38: CAN Message Format
Data is transmitted and received using Message Frames
8 byte data payload per message
Standard and Extended identifier formats
Standard Frame: 11-bit Identifier (CAN v2.0A)
11-bit
Identifier
R
T
R
S
O
F
I
D
E
r0
DLC
0…8 Bytes Data
CRC
ACK
E
O
F
Arbitration
Field
Control
Field
Data Field
Extended Frame: 29-bit Identifier (CAN v2.0B)
Control
Field
11-bit
Identifier
R
T
R
S
O
F
I
D
E
r0
DLC
0…8 Bytes Data
CRC
ACK
r1
18-bit
Identifier
S
R
R
E
O
F
Arbitration Field
Data Field

## Slide 39: CAN Block Diagram
SN65HVD23x
3.3 V CAN Transceiver
CAN Bus
Message
RAM
32
Message
Objects
(mailboxes)
CAN Core
Message
RAM
Interface
Message Handler
Register and Message
Object Access (IFx)
Module Interface
CAN_RX
CAN_TX
Test Modes Only
CAN
CPU Bus
(8, 16 or 32-bit)
To ePIE
DMA

## Slide 40: CAN Summary
Fully compliant with CAN standard v2.0B
Supports data rates up to 1 Mbps
Thirty-two message objects
  Configurable as receive or transmit
  Configurable with standard or extended identifier
  Programmable receive mask
  Uses 32-bit time stamp on messages
  Programmable interrupt scheme (two levels)
  Programmable alarm time-out
Programmable wake-up on bus activity
Two interrupt lines
Self-test mode

## Slide 41: MCAN
F28003x has one CAN (DCAN) and one MCAN, but they are not compatible.
MCAN supports both classic CAN and CAN FD protocols.
In CAN FD, the frame/message ID uses the 29-bits format used in the Extended ID version of classic CAN (Standard ID is 11 bits long).
The message payload size has been increased up to 64 bytes of data in each CAN-frame / message, compared to only 8-bytes in the classic CAN frame.
CAN FD (5 Mbps) is ~5x times faster than classic CAN (1 Mbps)
CAN FD can handle CAN frames/messages with 11-bit ID as well.

## Slide 42: Module Objectives
Serial Peripheral Interface (SPI)
Serial Communication Interface (SCI)
Local Interconnect Network (LIN)
Inter-Integrated Circuit (I2C)
Controller Area Network (CAN)
Power Management Bus (PMBus)
Fast Serial Interface (FSI)

## Slide 43: Power Management Bus (PMBus)
Provides an interface between the MCU and devices compliant with the SMI Forum PMBus Specification:
  Part I version 1.0 and Part II version 1.1
  Enables a standard 2-wire communications protocol between power supply components
Based on SMBus and supports I2C mode
  uses a similar physical layer to I2C
Support for master and slave modes
Support for three speeds:
  Standard Mode: Up to 100 kHz
  Fast Mode: 400 kHz
  Fast Mode+: 1000 kHz
    Applicable to module operating in I2C mode with input clock at 20 MHz
Four-byte transmit and receive buffers
Packet error checking (PEC)

## Slide 44: Conceptual Block Diagram
SCL is the bus clock
  Normally controlled by the master; can be held low by a slave to delay a transaction (to allow more time for processing)
SDA is the bidirectional data line
CONTROL is a slave input that can trigger an interrupt
  Can be used to tell a slave device to shut down
ALERT is a slave output/master input
  Allows a slave to request attention from the master
GPIO
MUX
DMA
Shift Register
DIV
Bit Clock
PMBCTRL
PMBTXBUF
PMBRXBUF
PMBus Module
Registers
SYSCLK
CPU
PIE
PMBUSA_INT
ALERT
CTL
SCL
SDA

## Slide 45: PMBus Connections
F28004x
PMBus
Module
Alert
Control
Data
Clock
DEVICE
#1
Physical
Address
Write
Protect
Alert
Control
Data
Clock
DEVICE
#2
Physical
Address
Write
Protect
Alert
Control
Data
Clock
DEVICE
#N
Physical
Address
Write
Protect

## Slide 46: PMBus Summary
Provides a standard and flexible means for digital power management
SDA and SCL timings derived from SYSCLK
  To comply with the PMBus timing specifications the bit clock must be set to 10 MHz or less
Four-byte Transmit Data Buffer
Four-byte Receive Data Buffer
Clock high and low time-outs
CONTROL and ALERT signals

## Slide 47: Module Objectives
Serial Peripheral Interface (SPI)
Serial Communication Interface (SCI)
Local Interconnect Network (LIN)
Inter-Integrated Circuit (I2C)
Controller Area Network (CAN)
Power Management Bus (PMBus)
Fast Serial Interface (FSI)

## Slide 48: Fast Serial Interface (FSI)
Ensure reliable high-speed serial communication across an isolation barrier
  Provides galvanic isolation where different circuits do not have common power and ground connections
Consists of independent transmitter (FSITX) and receiver (FSIRX) cores
  Each cores is configured and operated independently
Point-to-point (single master/single slave)
Fast transfer: 50 MHz
Dual data rate (100 Mbps @ 50 MHz clock)
Single or dual data lines
Programmable data length
Hardware- or software-calculated CRC
Frame error detection
Two interrupts per FSI core

## Slide 49: Transmitter / Receiver CPU Interface
FSI Transmitter
FSI Receiver
Core Signals
Core Signals

## Slide 50: Transmitter / Receiver Core Signals
TXCLK – Transmit clock
TXD0 – Primary data output line for transmission
  For multi-lane transmission:
    Contains all the even numbered bits of the data and CRC bytes
    Other frame fields will be transmitted in full
TXD1 – Additional data output line for transmission
  Configured for multi-lane transmission:
    Contain all the odd numbered bits of the data and CRC bytes
    Applies only to the data words and the CRC bytes
RXCLK – Receive clock
  Connected to the TXCLK of the transmitting FSI module
RXD0 – Primary data input line for reception
  Connected to the TXD0 of the transmitting FSI module
RXD1 – Additional data input line for reception
  Connected to the TXD1 of the transmitting FSI module if multi-lane transmission is used
Transmitter Core Signal
Receiver Core Signal

## Slide 51: Point to Point Connection
Note: while there is no true concept of a master or a slave node in the FSI protocol, this example uses this nomenclature as a simple way to describe the data flow

## Slide 52: FSI Summary
Highly reliable high-speed serial peripheral for communicating over an isolation barrier
High-speed data rate and low channel count
  Increases the amount of information transmitted and reduce the costs
Separate transmit and receive modules
Point-to-point communication protocol
  FSI transmitter core communicates directly to a single FSI receiver core
Skew compensation for signal delay due to isolation
Line break detection

## Slide 53: Lab 11: SCI Echoback Example
Download and install C2000Ware
Import and run a project from C2000Ware
  Driverlib SCI echoback example
    Each character received by the SCI port is sent back to the host
Use CCS terminal feature to view the data
  Terminal settings
    Choose terminal: Serial Terminal
    Serial Port: (from COM port number X)
    Baud rate: 9600
    Data size: 8
    Parity: None
    Stop bits: 1
    Encoding: Default (ISO-8859-1)

## Slide 54
C2000 Technical Training
www.ti.com/c2000