## Slide 1
Lite-On Singapore (LOS)
11KW OBC Microprocessor Partitioning
02/02/2023

## Slide 2
11KW OBC - MCU Architecture
TI
TMS320F28379S
Additional Analog Sensing
VBIAS – 1 Ch
NTC Thermistor – 1 Ch
(3 ADC temp sense Channels are connected through an Analog Mux).
AC INLET
EMI
RELAY
Relay
Drive
Input Voltage, Current Sensing
NPC
Rectifier
PWM Driver
PWM
Outputs
Analog IN
Analog IN
PWM Outputs
Analog IN
DO
CAN
DO
DI
Phase A, B, C
Mux Sel. 1-3
Relay PWM
PWM
VPFC_OUT
DI
Zero Crossing Detector Digital Input - 3
ZCD A, B, C
Auxiliary Supply –(to Pri. Drive Circuits)
Control PWM (Open Loop)
Secondary Auxiliary
Supply (Open Loop)
PFC_OUT
PFC
NEG
BS_PWM
PFC_EN
PFC_OK , AC_OK
800V DC Output
CAN H/L
(ECAP)
PFC Output Voltage Sensing
ISO7241CDW
PWM Output
TZ Input
Analog Input
Digital Input
Digital Output
COM (I2C/UART/SPI/CAN)
Isolator
TZ
HW OCP
ORPS PWM
HW OVP
TZ
DC Link
Bulk Cap
TI
TMS320F28379S
PWM
Driver
Isolator
CLLLC DC-DC Converter
PWM Driver
Output Voltage
Current Sensing
HV DC TERMINAL
VPFC
V_OUT
I_OUT
SIGNAL CONNECTOR
NXP
FS32K144
CAN
transceiver
18V_P
3.3V _P
AUX
Power
CAN H/ L
18V_P
…
BATTERY
I_CLLLC
PWM
Outputs
Analog IN
Analog IN
PWM
Outputs
DI
Output Voltage
Sensing
APM
Primary
Isolator
APM
Secondary
PFC_OK , AC_OK
PSFB Controller
ISO7241CDW
SBC
CAN
CLLLC PWM
SR PWM
CAN
CAN
SPI
SPI

## Slide 3
11KW OBC - CAN Communication
CLLLC_OK
Primary DSP / TI
CAN ECU
Secondary DSP / TI
CAN Stack
CAN Stack
OBC
For OBC Control and Data
APM / NXP
CAN Stack
CAN Stack
CAN Transceiver
CAN Transceiver
UARTStack
UARTStack
Reserved for Future
UARTStack
UARTStack
Reserved for Future
CAN Transceiver
CAN Transceiver
OBC_OK
CP_READY
GUI/ECU
PFC EN
PFC_OK
AC_OK
DSP_OK

## Slide 4
TI TMS320F28379S
TMS320F28379 32-bit CPU
  200MHz
  512KB flash
  132KB local RAM
  IEEE 754 single-precision floating-point instructions
Programmable Control Law Accelerator (CLA)
  200MHz
  IEEE 754 single-precision floating-point instructions
  Executes code independently of main CPU
On-chip memory
  512KB of flash (ECC-protected) across two independent banks
  132KB of RAM (ECC-protected or parity-protected)
  Dual-zone security supporting third-party development
  Unique Identification (UID) number
ADC
  Three 3.5-MSPS, 12-bit Analog-to-Digital Converters (ADCs)
  Up to 24 external channels

## Slide 5
NXP FS32K144
Arm™ Cortex-M4F/M0+ core, 32-bit CPU
  Supports up to 112 MHz frequency (HSRUN mode) with 1.25 Dhrystone MIPS per MHz
  Arm Core based on the Armv7 Architecture and Thumb®-2 ISA
  Integrated Digital Signal Processor (DSP)
  Single Precision Floating Point Unit (FPU)
Memory and memory interfaces
  Up to 2 MB program flash memory with ECC
  Up to 256 KB SRAM with ECC
Communications interfaces
  Up to three FlexCAN modules (with optional CAN-FD support)
Safety and Security
  128-bit Unique Identification (ID) number
  Error-Correcting Code (ECC) on flash and SRAM memories

## Slide 6
Manual code
MATLAB code
Manual code

## Slide 7: THANK YOU
Empowering A Green Future