## Slide 1: TMS320F28004x Microcontroller Workshop
Texas Instruments
C2000 Technical Training
Copyright © 2019 Texas Instruments. All rights reserved.
C2000 is a trademark of Texas Instruments.

## Slide 2: Workshop Outline
1. Architecture Overview
2. Programming Development Environment
Lab: Linker command file
3. Peripheral Register Programming
4. Reset and Interrupts
5. System Initialization
Lab: Watchdog and interrupts
6. Analog Subsystem
Lab: Build a data acquisition system
7. Control Peripherals
Lab: Generate and graph a PWM waveform
8. Direct Memory Access (DMA)
Lab: Use DMA to buffer ADC results
9. Control Law Accelerator (CLA)
Lab: Use CLA to filter PWM waveform
10. System Design
Lab: Run the code from flash memory
11. Communications (SCI echoback from C2000Ware)
12. Support Resources

## Slide 3: Required Workshop Materials
http://training.ti.com/c2000-f28004x-microcontroller-workshop
F280049C LaunchPad (LAUNCHXL-F280049C)
Install Code Composer Studio v9.0.1
Run the workshop installer
  F28004x Microcontroller Workshop-1.0-Setup.exe
    Lab Files / Solution Files
    Workshop Manual

## Slide 4: F280049C LaunchPad
XDS110 emulation circuitry
USB101: USB Interface
XDS110 External Debug Port
XDS110 Debug Probe
JP1-3: USB Power Isolation
J101: JTAG/UART Isolation
LED5: GPIO34 (green)
LED4: GPIO23 (red)
S1: Reset
J2/J4 *
* = BoosterPack plug-in module connector
J1/J3 *
J5/J7 *
J6/J8 *
F280049
S2: Boot Modes
J11: FSI
J15: VREFHI
J14: CAN
J12/13: Encoder
JP8
(connects
3.3V/5V
to J5/J7)
LED0: Power (USB)
LED1: Power (device)

## Slide 5: F280049C controlCARD
XDS100v2 emulation and isolation circuitry
J1:A - USB emulation/ UART
S1:A - isolated emulation and UART communication enable switch
S1: Boot Modes
LED D2: GPIO31 (red)
LED D3: GPIO34 (red)
LED D1: Power (green)
S7: PGA Filter
S8: ADC VREFHI
S4: JTAG / cJTAG
S2: GPIO10 / GPIO35
S3: GPIO08 / GPIO37
S6: GPIO26 / GPIO27
S5: GPIO24 / GPIO25
J1: FSI

## Slide 6: controlCARD Docking Station
5 V Power Connector
Power Switch (External / USB)
JTAG
Connector
USB Connector
LED D1:
Power (green)
180-pin HSEC8 Edge Card Interface
Analog
Signals
GPIO
Signals
Analog
Signals
GPIO
Signals

## Slide 7
C2000 Technical Training
www.ti.com/c2000