## Slide 1: 11kW OBC CLLLC CC Forward
Lim Shu Fan
9.5.2022

## Slide 2
Getting the plant transfer function (Ts to Io for CC in Forward mode)
Input perturbation – switching period
Output signal– Output current

## Slide 3
Steps to get Bode plots in MATLAB
Go to Apps -> linearization manager -> select the switching period as input perturbation and output current as output signal
Go to Apps -> Model linearizer -> estimation tab
In Estimation tab -> Model initial conditions -> take simulation snapshot -> put in simulation steady state time at 0.012s
In Estimation tab -> input signal -> select fixed sample time sinestream
  Sample time -> 1e-7 (if 50e-6, can only measure frequency range up to 10kHz)
  Frequency unit -> Hz
  Add new frequencies to the signals -> 10Hz to 100kHz, number of frequencies 30
  Select all the frequencies and change amplitude to 25/50 (because +/-5kHz around 83kHz/48kHz)
Select Bode and simulation will start

## Slide 4
The plant transfer function (open loop sweep) 250V output 9.25kW
GDC=-8.89277dB, KDC=10^(GDC/20), fz1= 20kHz, fp1=2.2kHz, fp2=7kHz
Operating point
Vin = 800V
Vout = 250V
Iout = 37A
Fsw = 83kHz

## Slide 5
The plant transfer function (open loop sweep) 470V output 11kW
GDC=-17.0763dB, KDC=10^(GDC/20), Q0=0.63, f0=1.8kHz, fz1= 14kHz
Operating point
Vin = 800V
Vout = 470V
Iout = 23.4A
Fsw = 48kHz

## Slide 6
The uncompensated open loop gain at 470V and 250V respectively
Uncompensated loop gain 470V 11kW
Uncompensated loop gain 250V 9.25kW

## Slide 7
2P2Z compensator design (50us)
Compensated loop gain 470V 11kW
Compensated loop gain 250V 9.25kW
Design parameters
Fz0 =2.2kHz
Qc =0.63
Fp= 15kHz
Gfc=-60dB
Kc=1/(10^(Gfc/20))
Tustin
Design Output
Fc =156Hz
PM =86deg
GM=-35dB
Design Output
Fc =398Hz
PM =87deg
GM=-22dB

## Slide 8
At 800V input, 250V output and 9.25kW,

## Slide 9
At 800V input, 350V output and 11kW,

## Slide 10
At 800V input, 400V output and 11kW,

## Slide 11
At 800V input, 470V output and 11kW,

## Slide 12
PI compensator design (50us)
Compensated loop gain 470V 11kW
Compensated loop gain 250V 9.25kW
Design parameters
FzL =820Hz
Gfc=12dB
KL=1/(10^(Gfc/20))
Tustin
Design Output
Fc =207Hz
PM =91deg
GM=-23dB
Design Output
Fc =635.6Hz
PM =100deg
GM=-17dB

## Slide 13
At 800V input, 250V output and 9.25kW,

## Slide 14
At 800V input with 30Vpp ripples at 120Hz, 250V output and 9.25kW,
Output ripple specs is +/-2% of output voltage.
At 250V, output ripple should be < +/-5V.
Output ripple specs is +/-5% of output current.
At 37A, output ripple should be < +/-1.85A.

## Slide 15
At 800V input, 350V output and 11kW,

## Slide 16
At 800V input, 400V output and 11kW,

## Slide 17
At 800V input, 470V output and 11kW,

## Slide 18
At 800V input with 30Vpp ripples at 120Hz, 470V output and 11kW,
Output ripple specs is +/-2% of output voltage.
At 470V, output ripple should be < +/-9.4V.
Output ripple specs is +/-5% of output current.
At 23.4A, output ripple should be < +/-1.17A.
Marginally passing at high limit.

## Slide 19
Control design using PID tuner – Settings for simulation run at 470V 11kW

## Slide 20
Control design using PID tuner – Plant identification

## Slide 21
Control design using PID tuner – PID tuning

## Slide 22
Bode plot of plant and Open loop bode plot

## Slide 23
At 800V input, 250V output and 9.25kW,

## Slide 24
At 800V input, 350V output and 11kW,

## Slide 25
At 800V input, 400V output and 11kW,

## Slide 26
At 800V input, 470V output and 11kW,