## Slide 1: 11kW OBC CLLLC CV Reverse
Lim Shu Fan
13.5.2022

## Slide 2
Getting the plant transfer function (Ts to Vpri for CV in reverse mode)
Input perturbation – switching period
Output signal– Primary side voltage

## Slide 3
Steps to get Bode plots in MATLAB
Go to Apps -> linearization manager -> select the switching period as input perturbation and output current as output signal
Go to Apps -> Model linearizer -> estimation tab
In Estimation tab -> Model initial conditions -> take simulation snapshot -> put in simulation steady state time at 0.012s
In Estimation tab -> input signal -> select fixed sample time sinestream
  Sample time -> 1e-7 (if 50e-6, can only measure frequency range up to 10kHz)
  Frequency unit -> Hz
  Add new frequencies to the signals -> 10Hz to 100kHz, number of frequencies 30
  Select all the frequencies and change amplitude to 20/10 (because +/-2kHz around 58kHz/82kHz)
Select Bode and simulation will start

## Slide 4
The plant transfer function (open loop sweep) 250V output 8.35kW
GDC=11.6841, KDC=10^(GDC/20), fz1= 12kHz, fp1=35Hz, fp2=2.4kHz
Operating point
Vin = 250V
Vout = 800V
Iout = 10.31A
Fsw = 58kHz
NOTE: Simulation cannot run at 250V 9.25kW!

## Slide 5
The plant transfer function (open loop sweep) 470V output 11kW
Operating point
Vin = 470V
Vout = 800V
Iout = 13.75A
Fsw = 82kHz
GDC=12.7054, KDC=10^(GDC/20), fz1= 15kHz, fp1=200Hz, fp2=4kHz

## Slide 6
The uncompensated open loop gain at 470V and 250V respectively
Uncompensated loop gain 470V 11kW
Uncompensated loop gain 250V 8.35kW

## Slide 7
PI compensator design (50us)
Compensated loop gain 470V 11kW
Compensated loop gain 250V 8.35kW
Design parameters
FzL =20Hz
Gfc=15.38dB
KL=1/(10^(Gfc/20))
Tustin
Design Output
Fc =255Hz
PM =56deg
GM=-19dB
Design Output
Fc =81Hz
PM =64deg
GM=-25dB

## Slide 8
At 250V input, 800V output and 8.35kW,
Init value of controller is 513
Output ripple specs is +/-2% of output voltage.
At 800V, output ripple should be < +/-16V.

## Slide 9
At 250V input, 800V output and 8.9kW,
Init value of controller is 531
NOTE: Simulation cannot run at 250V >9kW!

## Slide 10
At 350V input, 800V output and 11kW,
Init value of controller is 437

## Slide 11
At 400V input, 800V output and 11kW,
Init value of controller is 399

## Slide 12
At 470V input, 800V output and 11kW,
Init value of controller is 363

## Slide 13
Control design using PID tuner – Settings for simulation run at 250V 8.35kW

## Slide 14
Control design using PID tuner – Plant identification

## Slide 15
Control design using PID tuner – PID tuning

## Slide 16
Bode plot of plant and Open loop bode plot

## Slide 17
At 250V input, 800V output and 8.35kW,
Init value of controller is 511

## Slide 18
At 350V input, 800V output and 11kW,
Init value of controller is 436

## Slide 19
At 400V input, 800V output and 11kW,
Init value of controller is 397

## Slide 20
At 800V input, 470V output and 11kW,
Init value of controller is 361