## Slide 1
Snaku
2022/07/27
APM Software Architecture of OBC_6K6_2in1 project

## Slide 2
SW Block Diagram of APM
Architecture and Interface
Development Tools
Operation Mode of APM
Bootloader Introduction
Agenda

## Slide 3
SW Block Diagram of APM (1/2)
MCU Driver layer
PC
UDS Library TP Library
Bootloader [60%]
CAN Comm. [50%]
Diagnostic
stack
Flash Driver [100%]
Erase/Program
SPI Comm. [100%]
SBC Initial
Verify
Application Firmware [80%]
CAN Comm. [100%]
Interaction message
Network Mgmt.
Output V/I setting [100%]
PWM duty update
Signal Measurement
[100%]
ADC
GPIO
CAP
APM State Machine [100%]
ON / OFF
Sleep
Soft Start
Fault
APM Power Derating [100%]
current limit for thermal / voltage
Timer Scheduler [100%]
Timer counting
Timer trigger
SPI Communication [60%]
SBC Initial
Petting watchdog
Cali. & Conf. Data [100%]
Load
Verify
Read
CLI tool [70%]
Diagnostic service [60%]
PCAN driver
File I/O [100%]
YMAL / S19 / BIN
reflash appl.
access cali. data
access conf. data
assign AES Key
CAN msg. forwarding
J1772 Handling [60%]
OBC State Machine [100%]
CP/PP
S2
Fault Memory Mgmt. [70%]
ON / OFF
UART comm. [100%]
DSP BootROM
Diagnostic
Stack [50%]
ISO-TP
routine
security
DTC
DID
session
MCU Safety Mechanism [10%]
core
other
SBC Safety
Security [90%]
Key Mgmt.
SHE API
UART comm. [0%]
DSP BootROM
reflash DSP
Data Interface [100%]
Get
Set
EEPROM, snapshot.
In progress
Not develop yet

## Slide 4
SW Block Diagram of APM (2/2)
MCU Driver Config and Generate by NXP’s ProcessorExpert
PC
UDS/TP Library
Bootloader
CAN Comm.
.\source\stack
uds_app.c
uds_app_cfg.c can_tp.c
Flash Driver
flash_api.bin
SPI Comm.
sbc.c
sSBCInitial( )
Application Firmware repo: \\FLS106\evps_rd\Repo_hg\OBC6K6_LV_APPL_v2
CAN Comm.
networkManagement.c
sNmTask( )
can.c
sCan0Task( )
sCan2Task( )
Output V/I setting
pwm.c
sPwmLvdcVoltUpdate()
sPwmLvdcCurrUpdate()
Signal Measurement
adc.c
sAdcTask( )
gpio.c
sGpioTask( )
APM State Machine
housekeep.c
sStateMachine( )
APM Power Derating housekeep.c
sPowerDeratingSet( )
Timer Scheduler
timer.c
pTimers[ ]
sTimerRun( )
SPI Communication
sbc.c
sSBCInitial( )
safetyMeasure.c
FS45_WD_Refresh( )
Cali. & Conf. Data [100%]
nvm.c
sNvmXxxxDataRead( )
sNvmXxxxDataWrite( )
CLI tool
Diagnostic service
cli.py
readCalibrationData()
readConfigurationData()
clearCalibrationData()
download(cali_bin_file)
download(conf_bin_file)
PCAN driver
File I/O
ObcCali.yaml
ObcConf.yaml
J1772 Handling
evse.c
sEvseTask( )
OBC State Machine
obc.c
sObcTask( )
Fault Memory Mgmt. dtcmgr.c, DTC_Handle( )
eeprom.c, sEEP_Task( )
UART comm.
obc.c
sObcBootromXfer( )
Diagnostic
Stack
.\source\uds_stack
uds_app.c
UDS_MainFun( )
uds_app_cfg.c gs_astUDSService[]
can_tp.c
CANTP_MainFun( )
MCU Safety Mechanism safetyMeasure.c
sTestTask( )
Security
she.c
sbSheBootModeSet( )
sbSheMemoryUpdate()
UART comm.
none
Data Interface if.c
sbIfSet( )
sbIfGet( )
Driver
repo: \\FLS106\evps_rd\Repo_hg\OBC6K6_LV_BOOT_v2
repo: \\FLS106\evps_rd\Repo_hg\OBC6K6_CLI_v2

## Slide 5
SW Architecture -- APM Control part

## Slide 6
SW Architecture -- External CAN Communication part

## Slide 7
SW Architecture -- Internal CAN Communication part

## Slide 8
SW Development tools
S32K44 Firmware
CLI tool
repo: \\FLS106\evps_rd\Repo_hg\OBC6K6_LV_BOOT_v2
repo: \\FLS106\evps_rd\Repo_hg\OBC6K6_CLI_v2
repo: \\FLS106\evps_rd\Repo_hg\OBC6K6_LV_APPL_v2
Python 3.7.4
Package Version
--------------- -----------
bincopy 16.9.1
bitstruct 8.10.0
can-isotp 1.5
canmatrix 0.9.1
cantools 35.1.0
crccheck 0.6
cryptography 3.4.7
PyInstaller 3.6
python-can 3.3.2
pywin32-ctypes 0.2.0
PyYAML 5.3.1
udsoncan 1.10
…

## Slide 10
OBC 6.6KW Bootloader Introduction (1/4)
OBC 6.6KW S32K144 bootloader is modify from NXP Unified Bootloader V1.0 (2020.Q1)
      UDS (ISO14229), TP (ISO1765-2/CAN, ISO17987-2/LIN)
      Flash driver download from host (i.e., flash_api.bin )
      App validity check in bootloader
      APP and bootloader control signal reside in RAM
      Using reset (watchdog) switch to APP or bootloader
      CRC, software AES
  NXP has released V2.0 Unified Bootloader (2022.Q1) it supports S32K3, S32K1, and S12Z I don’t merge the code change of V2 to our code base

## Slide 11
OBC 6.6KW Bootloader Introduction (2/4)
I add CSEc module,
for AES computation,
KEY access, random
number generation

## Slide 12
Unified bootloader reset/power on process
      The following checks are performed by bootloader during the power on/reset. 1. Check update APP flag [ in SRAM ] 2. Check APP validity [ flags in flash ]
OBC 6.6KW Bootloader Introduction (3/4)
IsRequestEnterBootloader():
SRAM[ 0x2006FF1 ] == 0x5A ?
Boot_IsAPPValid():
IsFlashProgramSuccessful() and
IsFlashEraseSuccessful() and
IsFlashStructValid()

## Slide 13
OBC 6.6KW Bootloader Introduction (4/4)
flash_api.bin, which is
download via CAN before start erase routine
application code will update this information when it get request to download request

## Slide 14
SW Block ID for Bootloader
Application
(374KB)
0x0000 0000
0x0002 0000
0x0007 E000
appl info.
0x0002 0200
Int. vector
0x0002 0600
appl Ver.
0x0002 0700
Bootloader
(128KB)
Conf. data 4KB
Cali. data 4KB
0x0008 0000
0x0007 F000
boot Ver.
0x0001 FE00
Secure Boot
check area
Software Blocks
can be updated
by bootloader
SW Block ID for update:
ID 0 : flash driver (in SRAM) ID 1 : application ID 2 : configuration ID 3 : calibration
S32K144 P-Flash sector size : 4KB
1
2
3

## Slide 15
Erase Routine
add an option as Block ID in Routine Control request
ID 0 : flash driver ID 1 : application ID 2 : configuration ID 3 : calibration
= 0x41
= { 0 | 1 | 2 | 3 }

## Slide 16
Download calibration data by CLI tool: ‘obc.exe write cali’
S19 to BIN
YAML to S19
enter prog. session
to start bootloader
download flash driver i.e., flash_api.bin
to SRAM
download cali. data i.e., ObcCali.bin
to P_Flash

## Slide 17
CAN log (1/3)
;-------------------------------------------------------------------------------
; Message Time Type ID Rx/Tx
; Number Offset | [hex] | Data Length
; | [ms] | | | | Data [hex] ...
; | | | | | | |
;---+-- ------+------ +- --+----- +- +- +- +- -- -- -- -- -- -- --
1 6253.431 DT 07E0 Rx 8 02 10 03 AA AA AA AA AA // ext. session
2 6255.064 DT 07E8 Rx 8 02 50 03 00 00 00 00 00
3 6355.184 DT 07E0 Rx 8 03 28 03 03 AA AA AA AA // comm. control
4 6356.724 DT 07E8 Rx 8 02 68 03 00 00 00 00 00
5 6456.985 DT 07E0 Rx 8 02 10 02 AA AA AA AA AA // prog. session
6 6458.695 DT 07E8 Rx 8 03 7F 10 78 00 00 00 00
7 6478.368 DT 07E8 Rx 8 02 50 02 00 00 00 00 00
8 6558.508 DT 07E0 Rx 8 02 27 01 AA AA AA AA AA // req. seed
9 6564.766 DT 07E8 Rx 8 10 12 67 01 31 F4 38 75
10 6609.382 DT 07E0 Rx 8 30 00 00 AA AA AA AA AA
11 6610.160 DT 07E8 Rx 8 21 32 6D 64 D2 00 00 00
12 6610.580 DT 07E8 Rx 8 22 00 00 00 00 00 00 00
13 6664.138 DT 07E0 Rx 8 10 12 27 02 6B 77 CC AB // reply key, key = AES128_Ectrypt(seed)
14 6664.921 DT 07E8 Rx 8 30 00 01 00 00 00 00 00
15 6677.021 DT 07E0 Rx 8 21 78 32 F3 00 A5 19 73
16 6679.091 DT 07E0 Rx 8 22 B0 10 12 9F 13 AA AA
17 6681.731 DT 07E8 Rx 8 02 67 02 00 00 00 00 00
18 6780.899 DT 07E0 Rx 8 05 2E F1 5A 55 55 AA AA // clear sw fp.
19 6781.819 DT 07E8 Rx 8 03 6E F1 5A 00 00 00 00
20 6882.550 DT 07E0 Rx 8 10 08 34 00 41 00 00 00 // req. download
21 6883.359 DT 07E8 Rx 8 30 00 01 00 00 00 00 00 // addr = 0,
22 6895.533 DT 07E0 Rx 8 21 05 C4 AA AA AA AA AA // size = 1476
23 6900.473 DT 07E8 Rx 8 04 74 20 00 80 00 00 00 // max block = 128
24 6997.273 DT 07E0 Rx 8 10 82 36 01 79 04 00 00 // tx data, seq=1
...

## Slide 18
CAN log (2/3)
;-------------------------------------------------------------------------------
; Message Time Type ID Rx/Tx
; Number Offset | [hex] | Data Length
; | [ms] | | | | Data [hex] ...
; | | | | | | |
;---+-- ------+------ +- --+----- +- +- +- +- -- -- -- -- -- -- --
...
266 8663.245 DT 07E0 Rx 8 2A 40 AA AA AA AA AA AA
267 8666.177 DT 07E8 Rx 8 04 76 0C 07 44 00 00 00
268 8765.083 DT 07E0 Rx 8 01 37 AA AA AA AA AA AA // transfer exit
269 8766.149 DT 07E8 Rx 8 01 77 00 00 00 00 00 00
270 8866.807 DT 07E0 Rx 8 10 08 31 01 02 02 00 00 // checksum routine
271 8867.743 DT 07E8 Rx 8 30 00 01 00 00 00 00 00
272 8879.690 DT 07E0 Rx 8 21 07 11 AA AA AA AA AA
273 8880.713 DT 07E8 Rx 8 03 7F 31 78 00 00 00 00
274 8882.933 DT 07E8 Rx 8 05 71 01 02 02 00 00 00
275 8981.499 DT 07E0 Rx 8 06 31 01 FF 00 41 03 AA // erase routine
276 8985.294 DT 07E8 Rx 8 03 7F 31 78 00 00 00 00 // block ID = 3
277 9000.172 DT 07E8 Rx 8 05 71 01 FF 00 00 00 00
278 9083.232 DT 07E0 Rx 8 10 08 34 00 41 03 00 00 // req. download
279 9084.196 DT 07E8 Rx 8 30 00 01 00 00 00 00 00 // addr(block) = 3
280 9096.117 DT 07E0 Rx 8 21 01 A8 AA AA AA AA AA // size = 424
281 9100.850 DT 07E8 Rx 8 04 74 20 00 80 00 00 00 // reply max size = 128
282 9197.913 DT 07E0 Rx 8 10 82 36 01 55 AA 30 00 // tx data, seq=1
283 9198.861 DT 07E8 Rx 8 30 00 01 00 00 00 00 00
284 9210.786 DT 07E0 Rx 8 21 01 E6 07 03 0F 0D 07
...

## Slide 19
CAN log (3/3)
;-------------------------------------------------------------------------------
; Message Time Type ID Rx/Tx
; Number Offset | [hex] | Data Length
; | [ms] | | | | Data [hex] ...
; | | | | | | |
;---+-- ------+------ +- --+----- +- +- +- +- -- -- -- -- -- -- --
...
343 9541.910 DT 07E0 Rx 8 22 00 00 00 00 00 AA AA
344 9550.072 DT 07E8 Rx 8 04 76 03 00 00 00 00 00
345 9643.776 DT 07E0 Rx 8 10 2A 36 04 00 00 00 00 // tx data, final
346 9644.745 DT 07E8 Rx 8 30 00 01 00 00 00 00 00
347 9656.575 DT 07E0 Rx 8 21 00 00 00 00 00 00 80
348 9658.586 DT 07E0 Rx 8 22 3F 00 00 00 00 00 00
349 9660.595 DT 07E0 Rx 8 23 00 00 00 00 00 00 00
350 9662.714 DT 07E0 Rx 8 24 00 00 00 00 00 00 00
351 9664.526 DT 07E0 Rx 8 25 00 00 80 3F 00 00 00
352 9666.580 DT 07E0 Rx 8 26 00 AA AA AA AA AA AA
353 9674.005 DT 07E8 Rx 8 04 76 04 00 00 00 00 00
354 9768.375 DT 07E0 Rx 8 01 37 AA AA AA AA AA AA // transfer exit
355 9769.408 DT 07E8 Rx 8 01 77 00 00 00 00 00 00
356 9870.160 DT 07E0 Rx 8 10 08 31 01 02 02 00 00 // checksum routine
357 9871.131 DT 07E8 Rx 8 30 00 01 00 00 00 00 00
358 9882.967 DT 07E0 Rx 8 21 3E 7A AA AA AA AA AA
359 9883.989 DT 07E8 Rx 8 03 7F 31 78 00 00 00 00
360 9885.971 DT 07E8 Rx 8 05 71 01 02 02 00 00 00
361 9984.798 DT 07E0 Rx 8 02 11 01 AA AA AA AA AA // reset ECU
362 9985.910 DT 07E8 Rx 8 03 7F 11 78 00 00 00 00
363 10005.726 DT 07E8 Rx 8 02 51 01 00 00 00 00 00