## Slide 1: 30KW DC Charger FW Implementation CES SG Understanding & Queries for Clarification/Support 16th Oct 2019

## Slide 2
Understanding on Primary MCU
FW Implementation

## Slide 3
TI
TMS320F28069
Input V & I Analog Sensing
6 Channels
2 Channels Per Phase
VA, IA, VB, IB, VC & IC
Additional Analog Sensing
Total 12 Channels
VBIAS – 1 Ch
NTC Thermistor – 11 Ch
(Out of 11, 3 Channels are connected Directly and 8 Channels are connected through an Analog Mux).
Primary MCU - Control Block Diagram
INLET
EMI
RELAY
Relay
Drive
Input Voltage, Current Sensing
Interleaved Vienna Rectifier
Vienna
Rectifier
Vienna
Rectifier
PWM Driver
PWM Outputs
Analog IN
Analog IN
PWM Outputs
Analog IN
DO
I2C Master
UART
DO
DI
Phase A
Phase B
Phase C
Mux Sel. 1-3
Relay PWM
AH
BH
CH
AL
BL
CL
VPFC_OUT
DI
Zero Crossing Detector Digital Input - 3
ZCD A, B, C
VPFC_MID
VPFC_OUT OVP
VPFC_MID OVP
Auxiliary Supply –(to Pri. Drive Circuits)
Control PWM (Open Loop)
Secondary Auxiliary
Supply (Open Loop)
PFC_OUT
PFC_NEG
BS_PWM
PFC_EN
AC_OFF
PFC_OK
800V DC Output
RX
TX
DATA
CLOCK
I2C EEPROM 24LC04B
ISO7241CDW
(ECAP)
PFC Output Voltage Sensing
ISO7241CDW
To/From Secondary MCU
For Calibration Data
PWM Output
TZ Input
Analog Input
Digital Input
Digital Output
COM (I2C/UART/SPI/CAN)
Isolator
Isolator
TZ
HW OCP
ORPS PWM
HW VBC OVP
TZ

## Slide 4
Primary MCU – Task handler timing plan
ISR
Main() Tasks

## Slide 5
Primary MCU – Peripheral Config. & Logics
Digital Inputs:
  PFC_EN
    Purpose – To Control “Turn ON” and “Turn OFF” of PFC PWM.
    Logic – High -> Enable PFC PWM and enter to SS Loop
    Low -> Disable PFC PWM.
    Delay to Enable /Disable PWM after detection - To be defined
  Zero Crossing Detectors – ZCDA, ZCDB and ZCDC – Not Used Currently (Future backup)
    Purpose – To Detect & generate interrupt during input voltage Zero Crossing.
    To Compute Frequency, Phase Sequence PLL for SVPWM Synchronization
    Logic – Used with Edge Triggered Enhanced Capture Input to trigger interrupt.
Digital Output:
  AC_OFF
    Purpose – To notify secondary MCU on the status of Input. Just to display on GUI.
    Logic – High -> AC I/P is available and within valid range btw all phases
    Low -> AC I/P is OFF or phase Unbalance detected or I/P out of range.
    Delay/Thresholds to detect AC OK/Fail are to be defined.
  PFC OK
    Purpose – To notify secondary MCU on the status of PFC Output to TURN OFF D2D.
    Logic – High -> PFC Output is within valid range.
    Low -> PFC Output is out of range or OVP triggered(*).
    Delay/Thresholds to Detect PFC OK/Fail are to be defined.

## Slide 6
Primary MCU – Peripheral Config. & Logics
Analog Inputs:

## Slide 7
Primary MCU – Peripheral Config. & Logics
Analog Inputs:
  Analog Inputs – For Control Loop
  VCSA, VCSB, VCSC – 2.44V @ 442Vpk Input V with zero Cross @ 1.65V
  - With Max Sensing @ 1035Vpk @ 3.3V
  ICSA, ICSB, ICSC – 2.692V @ 72.5Apk Input I with zero Cross @ 1.65V
  - With Max Sensing @ 100Apk @ 3.087V
  PFC_VOUT – 2.889V @ 800V, 3.070V @ 850V
  PFC_VMID – 2.573V @ 400V, 2.894V @ 450V
  Analog Inputs – For V,I RMS Calculation
  Same signals (as in control Loop) are used for VI calculation also.
  Analog Input – VBIAS
  Purpose – Detection of Voltage source for SB1 (for ref Calibration / Tuning of ADC)
  Analog Input – 11 NTC Thermistor – Temperature sensing
  Thermistor used – TSM2A103F34D1RZ , B25/85 Beta Value - 3435
  3 Channels are connected directly to MCU
  and 8 Channels are connected through 8 by 1 Analog Mux.
  Analog Input – For Output OVP Protection - SW
  PFC_OVP, PFC_MID_OVP – 10-20mS to Shutdown. Recovery response to be defined.

## Slide 8
Primary MCU – Peripheral Config. & Logics
Communications:
  UART:
  Baud rate – 115200 bps
  Data’s to Share to Secondary MCU :
  Phase Voltages – VA, VB, VC
  Phase Current – IA, IB, IC
  Real Phase Power – PA, PB, PC
  Bulk Voltage – VPFC, VMID
  Line Frequency – ?
  Debug Data’s – to be defined
  Data’s to Receive:
  Calibration Data’s
  Commands for Configuration/Setup.
  Debug Commands
  Either data packets can be auto transmitted periodically or Transmitted based on the request from secondary/host.
  I2C Master: (For Calibration Data Read/Write Access to I2C EEPROM
  Clock Frequency – 100 khz
  I2C Slave Address – 0xA0 (1st 256x8bit), 0xA2 (2nd 256x8bit),
  Data’s to Save to EEPROM:
  Input Voltage, Current & Power Calibration Data’s (TBD).

## Slide 9
Primary MCU – Peripheral Config. & Logics
PWM Trip Zone(TZ) Inputs – For Protection:
  PFC_TZ
  HW OCP @ 160Apk I/P Current. – Cycle by Cycle Current limit (Trip PWM)
  VBC_OVP
  HW OVP for Bulk @ 890V PFC_OUT – Shutdown PFC. and recovery to be defined.
PWM Outputs:
  Relay PWM: (H)
  Config – Independent PWM Mode
  Frequency – 30KHz
  ON/OFF Logic – Turn ON/OFF input threshold/delays to be defined.
  BS_PWM (Open Loop): (H & L)
  Config – Complementary PWM Mode
  Frequency – 100KHz
  Duty % - 50% Duty
  ON/OFF Logic – ON after MCU startup (with some delay).
  ORPS_PWM (Open Loop): (H & L)
  Config – Complementary PWM Mode
  Frequency – 100KHz
  Duty % - 50% Duty
  ON/OFF Logic – ON after MCU startup (with some delay).

## Slide 10
Primary MCU – Peripheral Config. & Logics
PWM Outputs:
  DRAH, DRBH, DRCH, DRAL, DRBL, DRCL : (Closed Loop Control)
  Config – 6 Independent PWM Channels from 3 Pairs of PWM
  to Control Interleaved Vienna Rectifier (3 PWM’s for each Vienna rectifier)
  Frequency - 30khz
  Control algorithm - Space Vector PWM (SVPWM)
  **To be defined/studied for understanding and implementation.
  Compensator Type – Normal PI
  Protections (PWM Trip Zone) – I/P Current OCP @ 160Apk (Trip Cycle by Cycle )
  PFC_VOUT OVP @ 890V (Trip and Latch , Recover once recovery threshold reached ??)
Interrupts:
  ADC Interrupt – 30KHz, High Priority, For Main Control Loop
  PWM Trip Zone Interrupt – High Priority.
  ECAP Interrupt – (Reserved) Medium Priority, to detect & Process Voltage Zero Crossing
  UART RX and TX Interrupts – Medium Priority , Minimal execution time.
  Other Timer Interrupt – 100uS (for Main Task Handler), Low Priority
  I2C Master Interrupt – Low priority, called only during startup, Loading EEPROM data and during saving calibration data.

## Slide 11
Understanding on Secondary MCU
FW Implementation

## Slide 12
Secondary MCU - Control Block Diagram
PWM Output
TZ Input
Analog Input
Digital Input
Digital Output
COM (I2C/UART/SPI/CAN)
LLC 1 & LLC 2
LLC1
LLC2
LLC3
LLC4
LLC 3 & LLC 4
Buck 1 & 2
BUCK 1
BUCK 2
BUCK 3
BUCK 4
Buck 3 & 4
IBCK12
HVDC+
HVDC-
BAT+
BAT-
HVDC V & I Sense
EMI & Oring
VBAT Sense
550V
550V
550V
550V
IBCK34
TI
TMS320F28069
Additional Analog Sensing
Total 12 Channels
VAUX – 1 Ch
NTC Thermistor – 11 Ch
(Out of 11, 3 Channels are connected Directly and 8 Channels are connected through an Analog Mux).
LLC & BUCK V & I Sensing
VLLC1 to 4 - 4 Channels
VBUCK1 & 3 - 2 Channels
IBUCK1 & 3 - 2 Channels
V&I HVDC – 2 Channels
VBAT Sense – 1 Channel
PWM DRIVER
LED DRIVER
FAN DRIVER
To/From Primary MCU
I2C Master
DATA
For Calibration/
Config Data
CLOCK
I2C EEPROM M24256-BWDW6TP
UART
RX
TX
CAN Bus Driver
Mux Sel. 1-3
TX
RX
CAN
CAN Addr. Selection
VLLC3
ILLC3
VLLC4
ILLC4
VBUCK1
VBUCK2
VBUCK3
VBUCK4
IBUCK12
IBUCK34
VHVDC
IHVDC
VHVDC
VBAT_SEN
OVP/OCP/ SCP
PFC EN
8A/B
3A/B
2A/B
6A/B
1A/B
7A/B
4A
PWM Outputs
Analog IN
TZ Inputs
DI’s
DI
DO
DI
DO
PWM
Output
DI
DO
DO
AC OK & PFC OK
3 LED
Control Pins
To FAN
To LED’s
3 FAN Speed Inputs
To/From System
Output
Connector
D2D EN
6 Bit Address
From Dip Switch
To VOUT Discharge Control
Discharge EN
LLC OCP
HVDC OCP
BUCK OVP
IHVDC
VBUCK1-4
ILLC1-4
+800V
-800V
VLLC1
ILLC1
VLLC2
ILLC2
3 Ph AC I/P ~323-553Vac

## Slide 13
Secondary MCU – Task handler timing plan
ISR
Main() Tasks

## Slide 14
Secondary MCU – Peripheral Config. & Logics
Digital Inputs:
  D2D_EN
    Purpose – To Control Charging “Enable/Disable” and “Turn ON/OFF” of D2D.
    Logic – Low -> Enable Charger and D2D Conversion
    High-> Disable Charger and D2D Conversion.
    Delay to Enable & Disable Charger, after signal detection - To be defined
  AC_OK and PFC_OK from Primary MCU:
    Purpose – To Notify the secondary MCU on the status of AC Input and PFC Boost Status to Enable/Disable the DC to DC Conversion.
    AC_OK Logic – High -> AC I/P is available and within valid range btw all phases
    Low -> AC I/P is OFF or phase Unbalance detected or I/P out of range.
    PFC_OK Logic – High -> PFC Output is within valid range.
    Low -> PFC Output is out of range or OVP triggered(*).
  CAN Address Selection Inputs:
    Purpose – To Fix the CAN Bus Address during initialization for its communication.
    Address Range – 6 Bits – 64 Address Combination.
    Hex Address Range – 0x01 to 0x04.
    Hex Address 0x00 is for Special Applications.

## Slide 15
Secondary MCU – Peripheral Config. & Logics
Digital Output:
  PFC_EN
    Purpose – To notify Primary MCU to Enable/Disable PFC, based on the Status of the D2D_EN pin.
    Logic – High -> Enable PFC PWM and enter to SS Loop
    Low -> Disable PFC PWM.
    Delay to Enable /Disable PWM after detection - To be defined.
  VOUT_Discharge
    Purpose – To Discharge the O/P Voltage at the terminals as soon as the charger
    shutdown the output (for safety reason).
    Logic – After Output Shutdown Enable(High) this pin for predetermined time to discharge the O/P voltage & disable it afterwards before the next output
    turn ON.
  LED Control

## Slide 16
Secondary MCU – Peripheral Config. & Logics
Analog Inputs:
  Analog Inputs – For Buck Converter Closed Control Loop
  VBuck1 & VBuck3 – 2.53V @ 500V Output
  - VBuck = VBuck_ADV / 0.00506
  IBuck1 & IBuck3 – 3.005V @ 74.8A O/P I
  - IBuck = IBuck_ADV / 0.04018
  VHVDC – 2.505V @ 1000V Output
  - VHVDC = VHVDC_ADV / 0.002505
  IHVDC – 2.1432V @ 80A O/P I
  - IHVDC = IHVDC_ADV / 0.026787
  VBAT_SEN – 2.505V @ 1000V Output
  - VBAT_SEN = VBAT_SEN_ADV / 0.002505
  Analog Inputs – For LLC Open Loop
  VLLC1 to VLLC4 – 2.489V @ 550V Output
  - VLLC = VLLC_ADV / 0.004525
  Analog Input – Vaux
  Purpose – Detection of Voltage source for SB1 (for ref Calibration / Tuning of ADC)
  Analog Input – 11 NTC Thermistor – Temperature sensing
  Thermistor used – TSM2A103F34D1RZ , B25/85 Beta Value - 3435
  3 Channels are connected directly to MCU
  and 8 Channels are connected through 8 by 1 Analog Mux.

## Slide 17
Secondary MCU – Peripheral Config. & Logics
Communications:
  UART:
  Baud rate – 115200 bps
  Data’s to Receive from Primary MCU :
  Phase Voltages – VA, VB, VC
  Phase Current – IA, IB, IC
  Real Phase Power – PA, PB, PC
  Bulk Voltage – VPFC, VMID
  Line Frequency – ?
  Debug Data’s – to be defined
  Data’s to Send:
  Calibration Data’s
  Commands for Configuration/Setup.
  Debug Commands
  Either data packets can be auto transmitted periodically from Primary MCU or Transmitted based on
  the request by secondary/host.
  I2C Master: (For Calibration Data Read/Write Access to I2C EEPROM
  Part No - M24256-BWDW6TP
  Clock Frequency – 100 khz
  I2C Slave Address – 0xA0 (32k * 8Bit),
  Data’s to Save to EEPROM:
  Output Voltage, Current & Power Calibration Data’s (TBD).

## Slide 18
Secondary MCU – Peripheral Config. & Logics
Communications:
  CAN Bus:

## Slide 19
Secondary MCU - Control Block Diagram - New
PWM Output
TZ Input
Analog Input
Digital Input
Digital Output
COM (I2C/UART/SPI/CAN)
LLC 1 & LLC 2
LLC1
LLC2
LLC3
LLC4
LLC 3 & LLC 4
ILLC12
HVDC+
HVDC-
BAT+
BAT-
HVDC V & I Sense
EMI & Oring
VBAT Sense
550V
550V
550V
550V
ILLC34
TI
TMS320F28069
Additional Analog Sensing
Total 12 Channels
VAUX – 1 Ch
NTC Thermistor – 11 Ch
(Out of 11, 3 Channels are connected Directly and 8 Channels are connected through an Analog Mux).
LLC & BUCK V & I Sensing
VLLC1 to 4 - 4 Channels
VBUCK1 & 3 - 2 Channels
IBUCK1 & 3 - 2 Channels
V&I HVDC – 2 Channels
VBAT Sense – 1 Channel
PWM DRIVER
LED DRIVER
FAN DRIVER
To/From Primary MCU
I2C Master
DATA
For Calibration/
Config Data
CLOCK
I2C EEPROM M24256-BWDW6TP
UART
RX
TX
CAN Bus Driver
Mux Sel. 1-3
TX
RX
CAN
CAN Addr. Selection
VLLC3
ILLC3
VLLC4
ILLC4
I2
I34
VHVDC
IHVDC
VHVDC
VBAT_SEN
OVP/OCP/ SCP
PFC EN
8A/B
3A/B
2A/B
6A/B
4A
PWM Outputs
Analog IN
TZ Inputs
DI’s
DI
DO
DI
DO
PWM
Output
DI
DO
DO
AC OK & PFC OK
3 LED
Control Pins
To FAN
To LED’s
3 FAN Speed Inputs
To/From System
Output
Connector
D2D EN
6 Bit Address
From Dip Switch
To VOUT Discharge Control
Discharge EN
LLC OCP
HVDC OCP
BUCK OVP
IHVDC
VBUCK1-4
ILLC1-4
+800V
-800V
VLLC1
ILLC1
VLLC2
ILLC2
3 Ph AC I/P ~323-553Vac

## Slide 20
Secondary MCU – Peripheral Config. & Logics
PWM Trip Zone(TZ) Inputs – For Protection:
  BUCK OVP TZ (Active LOW)
  HW OVP @ 575V on any Buck O/P with Ref set @ 2,911V
  BUCK OCP TZ (Active LOW)
  HW Buck OCP @ 99A on Buck1 or 3 O/P with Ref set @ 1.65V
  LLC OCP TZ (Active LOW)
  HW LLC OCP @ 30APk(60A) on LLC Primary Side @ 1.65V
PWM Outputs:
  FAN PWM: (H) 4A
  Fan Model - V12E12BS1B5
  Config – Independent PWM Mode
  Frequency & Fan Control Algorithm – To Be Defined.
  LLC1 DRA, DRB, DRC & DRD – Open Loop
  Config – Complementary PWM Mode
  Frequency – 100KHz
  Duty % - 50% Duty
  LLC2 DRA, DRB, DRC & DRD – Open Loop
  Config – Complementary PWM Mode
  Frequency Range – 100KHz
  Duty % - 50% Duty

## Slide 21
Secondary MCU – Peripheral Config. & Logics
PWM Outputs:
  Buck1 DRA, DRB & Buck2 DRA, DRB : (Closed Loop)
  Control Algorithm:
Frequency Range – 45KHz
Config – Complementary PWM Mode
Controller Type 2P1Z

## Slide 22
Secondary MCU – Peripheral Config. & Logics
Interrupts:
  ADC Interrupt – 20KHz, High Priority, For Main Buck Control Loop.
  1mS Timer Interrupt – for LLC Open Loop Control.
  PWM Trip Zone Interrupt – High Priority for Protections.
  CAN Bus Interrupt for Rx & Tx - Medium Priority , Minimal execution time.
  UART RX and TX Interrupts – Medium Priority , Minimal execution time.
  Other Timer Interrupt – 100uS (for Main Task Handler), Low Priority
  I2C Master Interrupt – Low priority, called only during startup, Loading EEPROM data and during saving calibration data.

## Slide 23
Clarification required &
Support needed

## Slide 24
Queries for Clarification
Is “Vienna rectifier” uses, Space Vector PWM control (SVPWM) ? Or? Yes SVPWM
Are you using/having any plant model or Model based design files for Vienna rectifier?
Are you using/having any plant model or Model based design files for LLC/Buck Converter?
Is our understanding on Interrupts/peripheral configs for primary MCU are correct?
Control Loop interrupt is triggered by Timer ? Or PWM? Or ADC? ADC
Are we missing any interrupts @ Primary MCU?
What is the compensator type (2p2z, 3p3z) used for ?
    Vienna – Normal PI
    LLC - Open Loop
    Buck - 2P1Z
Is there any document for the FW, to understand the requirements of delays/thresholds for Relay/PFC Turn ON/OFF, CAN bus commands, UART data/commands etc..
Is any specific CAN Bus Specification (Req. commands/data & address to implement) available for this project? if so can share the document.
.

## Slide 25
Support / Document needed from HQ
Is HQ works with Model Based Design (MBD) for control Loop design? With MATLAB/Simulink or PSIM? If so, can share
    Any document on MBD procedure.
    Any training material for MBD? Mainly for control algorithm/Loop Design.
    Any model-based design files used for this project. (for Vienna or LLC).
For our better understanding on the FW implementation, can HQ provide us with the below documents/details of this project?
    Control Algorithm and its implementation details for Vienna Rectifier & LLC/Buck Converter.
    Any document on TI’s “CLA” usage with this project in both primary and secondary MCU’s.
    Access to Project Source code (For Control Loop ISR and Configs) for both Primary & Secondary MCU’s. (Mainly to understand the peripheral Configuration and Control loop, CLA implementation in TI MCU’s).
    Any other document with details on Fault protection trigger and recovery mechanism. (OVP, OCP, OTP, Input Fail etc..)
CAN Bus documents specific to this project/to EV Chargers to understand its requirements.
  Preliminary CAN bus spec. provided

## Slide 26
Thanks CES SG Understanding & Clarifications