## Slide 1: 6.6 KW OBC system state diagram
喚醒來源
初期韌體不允許三個state直接跳轉
必須先回 standby 才能換別的模式
CAN = Charging
Standby
(off)
Charging & DCDC
IDLE
IGN = high or CAN = Standby
IGN = low and
CAN = IDLE
IGN = high and
CAN = DCDC
IGN = low or CAN = Standby
CAN = Charging
IGN = high and CAN = Charging_DCDC
CAN = Standby
or EVSE disconnect
CAN = Charging
IGN = high and
CAN = DCDC
IGN = high and
CAN = Charging_DCDC
IGN = high and ( CAN = DCDC or EVSE disconnect )
IGN = high and CAN = Charging_DCDC
IGN = low or
CAN = Standby
Charging State
DCDC
State
Sleep
IGN = high or CAN signal or
J1772 Pilot
IGN = low
and CAN no signal

## Slide 2: 6.6 KW LV MCU state diagram
Power On
1. AUX_EN = high (on)
2. Delay 0.5 sec
Sleep State
CAN0_STB = high (off)
EEP_WP = low (writable)
Delay 1 sec
AUX_EN = low (off)
send sleep command to SBC
Idle State
DUMMY_EN = high (on)
LVDC_EN = high (off)
HVDC_EN = high (req . off)
EEP_WP = high (read only)
ORING_EN = low (off)
send Cali data to HV & AC MCU
IGN = low and
CAN no signal
Standby State
DUMMY_EN = high (on)
LVDC_EN = high (off)
HVDC_EN = high (req . off)
AUX_EN = high (on)
ORING_EN = low (off)
EV_READY = low
VENT_REQ = low
DC-DC state
AC-DC state
Pilot State = C | D
DUMMY_EN = high (on)
LVDC_EN = high (off)
ORING_EN = low (off)
wait slave MCU state = ACDC
Fault State
DUMMY_EN = high (on)
LVDC_EN = high (off)
HVDC_EN = high (req. off)
AUX_EN = high (on)
ORING_EN = low (off)
Write Fault Code to EEPROM
send Cali data if not finish
fault
clear
OBC-DC state
Pilot State = C | D
DUMMY_EN = high (on)
LVDC_EN = low (on)
ORING_EN = high (on)
Delay 0.5s
wait slave MCU state = OBCDC
check LV_UVP
IGN = high and CAN = DCDC
CAN = ACDC
IGN = high and CAN = OBCDC
Any fault
detected
IGN = low or CAN = IDLE | Standby or OtherSideOff
EVSE disconnect
or CAN = IDLE | Standby
or OtherSideOff
( CAN = Standby | ACDC | DCDC | OBCDC
or IGN = high )
and Calibration Data Ready
IGN = low
and CAN = IDLE
IGN = low or CAN = IDLE | Standby or OtherSideOff
IGN = high and CAN = OBCDC
IGN = high and (CAN = DCDC or EVSE disconnect )
CAN = ACDC
IGN = high and
CAN = DCDC
CAN = ACDC
IGN = high and CAN = OBCDC
Pilot State = B
DUMMY_EN = low (off)
HVDC_EN = high (off)
LVDC_EN = low (on)
ORING_EN = high (on)
Delay 0.5s
wait slave MCU state = DCDC
check LV_UVP
Charger Coupler Task
1. Monitor Polit and Proximity signals
2. If EVSE Coupler depressed
or Pilot state != (C or D)
or ACDC fault 
HVDC_EN = high (off)
Else HVDC_EN = low (on)
CAN = Standby | ACDC | DCDC | OBCDC
or IGN = high
Start

## Slide 3: 6.6 KW HV MCU state diagram
Start
Power On
Delay 0.5 sec
Idle State
HVDC_PWM_EN = high (off)
BYPASS_ON = low (off)
HVCB_ON = low (off)
Standby State
HVDC_PWM_EN = high (off)
BYPASS_ON = low (off)
HVCB_ON = low (off)
UART != IDLE
Fault State
HVDC_PWM_EN = high (off)
BYPASS_ON = low (off)
HVCB_ON = low (off)
fault
clear
UART = IDLE
DC-DC state
AC-DC state
OBC-DC state
wait PFC_OK == high (on)
delay 0.01s
HVDC_PWM_EN = low (on)
delay 0.5s
HvUvpCheck = true
IGN = high and UART = DCDC
IGN = high and UART = OBCDC
and HVDC_EN# = low
UART= IDLE | Standby or OtherSideOff or PFC_OK = low
or HVDC_EN# = high or CP_STATE = B
UART = OBCDC
IGN = high and (UART = DCDC or EVSE disconnect )
UART = ACDC
IGN = high and UART = DCDC
UART = ACDC
IGN = high and UART = OBCDC
HvUvpCheck = true
HVDC_PWM_EN = high (off)
wait HV > UV threshold
wait PFC_OK == high (on)
delay 0.01s
HVDC_PWM_EN = low (on)
delay 0.5s
HvUvpCheck = true
UART = ACDC
and HVDC_EN# = low
UART = IDLE | Standby or EVSE disconnect
or OtherSideOff
or PFC_OK = low
or HVDC_EN# = high
or CP_STATE = B
UART = IDLE | Standby or OtherSideOff
Any fault
detected

## Slide 4: 6.6 KW AC MCU state diagram
Start
Power On
Delay 0.01 sec
Idle State
PFC_EN = high (off)
RLY_DRV = low (off)
PFC_OK = low (off)
EN_L & EN_N = high (on)
VBULK_380V_EN = high (off)
Standby State
EN_L & EN_N = high (on)
PFC_EN = high (off)
PFC_OK = low (off)
RLY_DRV = low (off)
VBULK_380V_EN = high (off)
UART != IDLE
Fault State
fault
clear
UART = IDLE
PFC_EN = high (off)
RLY_DRV = low (off)
PFC_OK = low (off)
EN_L & EN_N = high (on)
VBULK_380V_EN = high (off)
Timer
Event (10KHz)
ADC ISR
Sample ADC half channels …
暫時取消 Zero Crossing Ctrl EN_N = high
EN_L = high
Any fault
detected
DC-DC state
AC-DC state
OBC-DC state
InrushSwitchCtrl()
wait RLY_DRV = high (on)
delay 0.02s
PFC_EN = low (on)
wait PFC_OK_P = high (on)
delay 0.7s
GridCheck = true
BusUvpCheck = true
UART = DCDC and IGN = high
UART = OBCDC and IGN = high
UART= IDLE or OtherSideOff or CP_STATE = B
UART = OBCDC
IGN = high and (UART = DCDC or EVSE disconnect )
UART = ACDC
UART = DCDC and IGN = high
UART = ACDC
UART = OBCDC
UART = ACDC
UART = IDLE | Standby or EVSE disconnect
or OtherSideOff
or CP_STATE = B
UART = IDLE | Standby or OtherSideOff
PFC_EN = high (off)
PFC_OK_P = low (off)
RLY_DRV = low (off)
InrushSwitchCtrl()
wait RLY_DRV = high (on) 
delay 0.02s
PFC_EN = low (on)
wait PFC_OK = high (on)
delay 0.7s
GridCheck = true
BusUvpCheck = true
InrushSwitchCtrl()
If RLY_DRV = low (off) if Vbulk > Vac_rms * 1.414 * BulkThreshold
RLY_DRV = high (on) Else:
RLY_DRV = low (off)
Port Check Task
1. If VBus < 350v & AC/OBC-DC state 
PFC_OK = low (off)
Else
If 395 < Vbus < 405 
PFC_OK = high (on)
2. AC_Level_Select( )
AC_Level_Select( )
If Vac_rms < 160v: AC_LINE_select = high (110v)
PKLMT_select = high (110v)
BulkThreshold = 0.8
If Vac_rms > 165v:
AC_LINE_select = low (220v)
PKLMT_select = low (220v)
BulkThreshold = 0.9

## Slide 5: 6.6KW off timing
Idle state
Standby state
Fault state
Sleep state
190A
300V
24A
190A
300V
24A
190A
300V
24A
190A
300V
24A

## Slide 6: 6.6KW DC-DC state timing
Standby state
DC-DC state
190A
300V
24A
CAN Voltage command, soft-start, 0.1V/ms
300V
24A
Current limit

## Slide 7: 6.6KW AC-DC state timing
Standby state
AC-DC state
190A
300V
24A
190A
CAN command
Current limit
3s
Max
20ms
500ms
10ms
10ms

## Slide 8: 6.6KW OBC-DC state timing
Standby state
OBC-DC state
190A
300V
24A
CAN command
Current limit
CAN command with soft-start
Current limit
3s
Max
20ms
500ms
10ms
10ms

## Slide 9: 6.6KW Power on  Standby

## Slide 10: 6.6KW Standby DC-DC
Soft-Start
190A
CAN Command with Soft-Start
CAN command
↗ Duty : 0.1V / ms ↗

## Slide 11: 6.6KW DC-DC  Standby
190A
CAN Command
CAN command
先 disable 才改變 duty

## Slide 12: 6.6KW StandbyAC-DC
CAN Command
CAN command
0. 53s
190A

## Slide 13: 6.6KW AC-DCStandby
CAN Command
CAN command
先關 HV 才關 PFC

## Slide 14: 6.6KW StandbyOBC-DC
CAN Command
CAN command
190A
Soft-Start
CAN command

## Slide 15: 6.6KW OBC-DC Standby
CAN Command
CAN command
190A
CAN Command
CAN command
先 disable 才改變 duty

## Slide 16: 6.6KW HV OVP when OBC-DC after fix LV MCU re-start issue
300V
24A
CAN Command
CAN command
13.5V
190A
CAN Command
CAN command

## Slide 17: 6.6KW HV OCP(HW) when OBC-DC

## Slide 18: 6.6KW HV OVP(HW) when OBC-DC

## Slide 19: 6.6KW HV OCP when OBC-DC

## Slide 20: 6.6KW HV OTP when OBC-DC

## Slide 21: 6.6KW LV OVP when OBC-DC
300V
24A
CAN Command
CAN command
13.5V
190A
CAN Command
CAN command

## Slide 22: 6.6KW LV OV(HW) when OBC-DC
300V
24A
CAN Command
CAN command
13.5V
190A
CAN Command
CAN command

## Slide 23: 6.6KW LV OC(HW) when OBC-DC
300V
24A
CAN Command
CAN command
13.5V
190A
CAN Command
CAN command

## Slide 24: 6.6KW LV OTP when OBC-DC
300V
24A
CAN Command
CAN command
13.5V
190A
CAN Command
CAN command

## Slide 25: 6.6KW Vbat OV when OBC-DC

## Slide 26: 6.6KW Vbat UV when OBC-DC
LV MCU CAN BUS Off

## Slide 27: 6.6KW Pilot over frequency when AC-DC

## Slide 28: 6.6KW Pilot under frequency when AC-DC

## Slide 29: 6.6KW Pilot error (-12V) when AC-DC

## Slide 30: 6.6KW Bulk OV(HW) when OBC-DC

## Slide 31: 6.6KW Bulk OV when OBC-DC

## Slide 32: 6.6KW Bulk UV when OBC-DC

## Slide 33: 6.6KW PFC OTP1 when OBC-DC

## Slide 34: 6.6KW PFC OTP2 when OBC-DC

## Slide 35: 6.6KW Grid OV when AC-DC

## Slide 36: 6.6KW Grid UV when AC-DC

## Slide 37: 6.6KW Grid over frequency when AC-DC

## Slide 38: 6.6KW Grid under frequency when AC-DC